## Slide 1
3GPP TSG RAN Meeting #101 RP-231800
Bangalore, India, September 11 - 15, 2023
Source: vivo
Document for: Discussion & Decision
Agenda Item: 8A.2.12.2
Rel-19 Multi-carrier Enhancements (RAN1-led)

## Slide 2
Rel-18 Multi-carrier enhancements
  Objective: Reduce PDCCH overhead and improve throughput for NR CA
    Support multi-cell PUSCH/PDSCH scheduling (one PDSCH/PUSCH per cell) with a single DCI
  Objective: To achieve higher UL capacity for UE with up to 2Tx chains
    Support UL Tx switching for 3 or 4 configured bands with up to 2 Tx
Restrictions in Rel-18 multi-cell PUSCH/PDSCH scheduling with a single DCI due to limited TU
  Same SCS between co-scheduled cells
  Same carrier type between co-scheduled cells
  Single scheduling cell for co-scheduled cells
Background and Motivation
Motivation for Rel-19 enhancements
  Rel-18 multi-cell PUSCH/PDSCH scheduling with a single DCI is not applicable in some cases due to the restrictions, thus may not meet the demand of operator in real deployment
    CA with mixed SCSs and mixed carrier types(e.g., FDD+TDD) is typical deployment in NR
    UE supporting multiple carriers or bands with different SCS/carrier types is typical
  PDCCH overhead issue is not fully addressed
    PDCCH blocking issue on the scheduling cell may remain as both mc-DCI and sc-DCI should be located on the same scheduling cell in Rel-18 MCE
Support different carrier types/SCSs among co-scheduled cells
Support separate scheduling cells for mc-DCI and sc-DCI

## Slide 3
Proposal for Rel-19 MCE WI
  Objective of Rel-19 MCE work item:
    Enhancement for multi-cell scheduling via single DCI [RAN1]
      Support different carrier types/SCSs among a cell combination scheduled via single DCI.
      Support up to two scheduling cells for mc-DCI and sc-DCI for a non-reference cell/P(S)cell.
  TU
    The target scope size for Rel-19 MCE: RAN1 0.5 TU