## Slide 1
3GPP TSG RAN Meeting #101 RP-231803
Bangalore, India, September 11-15, 2023
Rel-19 Sidelink Evolution
Source: vivo
Document for: Discussion
Agenda Item: 8A.2.12.5

## Slide 2
  Background and motivations
    Topic 1: SL underlay
    Topic 2: SL RedCap
    Topic 3: SL FR2
  Rel-19 work planning
Agenda

## Slide 3
Operator
Low spectrum efficiency
Consumer
Bad user experience (XP)
requiring dedicated spectrum for sidelink operation
High Opex/Capex when complicated scheduler is employed
poor network availability, low throughout, and high latency
Not optimized for personal device
difficult of dynamic sharing between Uu and SL resources
difficult of device/network installation, administration and maintenance
high power consumption
due to limited FR1 spectrum and congested unlicensed band
high device cost, limited device space/size, etc.
Background
General motivations for sidelink evolution in Rel-19
Key aspects to deploy commercial D2D services

## Slide 4
Solutions:
SL underlay
  Dynamically sharing the Uu spectrum resources for SL transmissions
  Interference cancellation
    SLUL suppression (e.g., SL PSD limitation)
    ULSL cancellation
Motivation:
Enabling SL business on existing licensed spectrums
Enabling better involvement of operators
Motivation:
Enabling low-cost and Energy-efficient commercial personal IoT device
Motivation:
Enabling high-capacity commercial usage
Enabling new SL operating spectrums
Solutions:
SL RedCap
  Further power saving enh.
    SL WUS/GTS, etc.
  Very Low Power (VLP) UE
    For both licensed and unlicensed spectrums
  PA-less devices
Solutions:
SL on FR2
  Beam management
  Resource allocation enh.
  Operating on both FR2-1 and FR2-2
  For all the cast types
Further sidelink evolutions
Ignition of commercial SL business
Power and cost
Spectrum and User XP
Throughput

## Slide 5
SL underlay
Further sidelink evaluations

## Slide 6
Motivations
Sidelink Underlay
In addition to traditional Uu communication, there is increasing demand for short range device to device (D2D) communication (e.g. P1-G1) due to XR services
NR sidelink technologies are designed for D2D but
  Sidelink over dedicated ITS spectrum: Only available for V2X use cases.
  Sidelink over licensed spectrum (Uu): The current design (and RAN4 spec) assumes that sidelink (if deployed) uses orthogonal resource than Uu, leading to capacity degradation to Uu and/or complicated NW scheduler.
  Sidelink over unlicensed spectrum: Not reliable and need to employ complex channel access mechanism, with little/limited involvement of operators.
Candidate Uu
resource
Sidelink resource pool
Observation: It is desirable to enable operators to deploy high quality commercial D2D business on existing licensed spectrum without degradation to existing Uu cellular service.

## Slide 7
Key idea for potential enhancement
Sidelink Underlay
Sidelink Underlay Transmission over licensed spectrum uses wide bandwidth and a stringent PSD restriction, to exploit higher spatial multiplexing gain from existing cellular spectrum.
  Power domain: Sidelink underlay transmission follows a UWB-like PSD restriction (e.g. <-40dBm/MHz)
  Frequency domain: Sidelink underlay transmission spans a wideband (e.g. 100MHz) that is fully shared with cellular transmission (Uu)
  Time domain: Sidelink underlay transmission is limited to in certain slots (e.g. UL slots)
frequency
Uu
Uu
SL
SL
frequency
Uu
Uu
SL
Typical Sidelink
Sidelink Underlay
Tx Power
Tx Power
Uu
Proposal: Study the feasibility and benefit, and specify necessary specification changes to support Sidelink underlay transmission over licensed spectrum
Licensed carrier (e.g. 100MHz)

## Slide 8
Benefits
Sidelink Underlay
Sidelink underlay transmission over licensed spectrum can have the following benefits
  Benefit 1: Satisfy the increasing demand of commercial D2D communication by exploiting the existing spectrum
    Relevance: No need to reserve dedicated orthogonal spectrum/resource(s) for sidelink services
  Benefit 2: Provide better QoS (high robustness, low latency) than unlicensed spectrum
    Relevance: No need to perform channel access due to competing spectrum with other systems
  Benefit 3: Increase the spectrum efficiency (more spatial reuse of the spectrum) by serving D2D communication with no impact to cellular communications
    Relevance: No reduction of Uu capacity due to very low power sidelink underlay transmission while additional D2D capacity is introduced
  Benefit 4: Enable better involvement of operators into the commercial D2D business
    Relevance: Operators can step into the business by providing higher quality/less interfering spectrum (than unlicensed band), as well as radio link/network management/administration.

## Slide 9
Feasibility study (sidelink->cellular interference)
Sidelink Underlay
Interference from sidelink D2D to cellular Uu
  Baseline: Dense Urban with cellular Uu users only (10 Uu UEs/cell, 100MHz carrier)
  Sidelink Underlay: Dense Urban with both cellular Uu users and sidelink D2D pairs (10 Uu UEs/cell, 5 D2D pairs/cell with full buffer traffic, 100MHz carrier)
  System level evaluation (assumption in Appendix) is performed to compare UPT performance of the above two scenarios
Observation: When UL resource is used for SL underlay transmission, the impact to Uu UL from sidelink D2D can be ignored (UPT loss <=0.5%) if sidelink transmission PSD<=-40dBm/MHz
Chart: Uplink UPT loss in Dense Urban Scenario
| Baseline | PSD=-20 | PSD=-40 | PSD=-60
Mean UPT | 419.951 | 400.3977 | 417.846 | 419.2269
UPT loss | 0.046559 | 0.0050101 | 0.0017219
Curve for PSD=-40/-60 dBm/MHz almost coincides with baseline

## Slide 10
Feasibility study (cellular->sidelink interference)
Sidelink Underlay
Interference from cellular Uu to sidelink D2D
  Figure a: Interference CDF to SL in dense urban from Uu interface
  Figure b: SL Link level performance with interference according to Fig. (a) with different traffic load (RU)
  Table c: Equivalent sidelink (communication range 5m) SNR is ~8.5dB when PSD is -40dBm/MHz
Observation: Sidelink underlay transmission with PSD=-40dBm/MHz can work (low MCS) even when the Uu UL traffic load is high, and higher MCS (e.g. 16QAM) can be possible when the Uu UL traffic load is low.
(b)
(a)
Frequency (GHz) | 4
SCS (KHz) | 30
PRB number | 273
Bandwidth (MHz) | 98.28
PSD (dBm/MHz) | -40
Total Tx Power (dBm) | -20.07534852
Tx power Per PRB (dBm) | -44.43697499
Noise power Per PRB (dBm) | -109.437
Range (m) | 5
Channel model | InH - Office LOS
Pathloss | 56.5333809
Rx power Per PRB | -100.9703559
Equivalent SNR | 8.466644106
(c)

## Slide 11
SL RedCap
Further sidelink evaluations

## Slide 12
Personal local IoT Networks
SL RedCap
Home automation
Wearable devices
Great demand in the industry on the non-cellular wireless commercial IoT use cases
  Including such as the personal IoT device (earbuds, sensor, etc.), wireless docking, wireless streaming, etc.
Personal local IoT networks
  Becoming complex network topology while self organizing/management/maintenance is desirable
    Typically installed/maintained by a consumer, not a telecom or wireless specialist/professional
  Demanding high traffic volume, e.g., Hi-Res Audio/Music, Wireless Display, gaming, etc.
  While devices are severely sensitive to the weight and size of the devices, and most highly battery constrained.
    Usually constrained by the physical dimension limitations, such as sensor, earbuds, etc.
Observation: NR sidelink has very high potentials to enable 3GPP system in this market, E.g., highly controllable and manageable with operators involved.

## Slide 13
NR sidelink has very high potentials to enable 3GPP system in the personal IoT market
  E.g., highly controllable/manageable with operators involved
However, the power consumption and device complexity level are not good enough for many commercial personal devices (HMD, watch, earbud, etc.).
Motivation
SL RedCap
Proposal: Supporting SL RedCap in Rel-19
  Enabling PA-less sidelink device
  Enabling very low power (VLP) operations (such as SL underlay, VLP channel access, etc.)
  Introducing SL WUS signal and operations

## Slide 14
UE power class
  Power class 3 (23dBm), Power class 2(26dBm) supported for general use cases of Uu (as well as for sidelink)
  LTE eMTC and NB-IOT supports power class 5 (20dBm) and power class 6 (14dBm) (Not supported for sidelink)
PA-less sidelink devices
SL RedCap
GaAs based external PA is required to support 23dBm
  The PAE (PA efficiency) is very low (less than 5%) at low power level, e.g. 0~10dBm
    Typically for personal IoT or XR/gaming where the traffic is predominately within the localized area
  GaAs based PA also increases the device cost
    10-12% overall relative cost saving
  Consuming internal device space
    Especially for some personal IoT device such as glasses frames, earbuds, blood pressure monitor, etc
Figure 1. Power efficiency (marked red when less than 5%), N78 and N41
Two PA implementation choices: 1) Constant 4.2V P_DC; 2) APT (adaptive power tracking)

## Slide 15
Preliminary evaluation results of SL VLP
SL RedCap
Parameter | value
Deployment | Indoor 120 * 80
Carrier Frequency | 6GHz
Communication type | unicast
Bandwidth | 20MHz
Subcarrier spacing | 15KHz
Channel model | P2P link defined in TR 37.885
Channel Access | LBT type1 with CAPC P=2
Resource allocation scheme | R16 resource allocation mode 2 for single-slot based transmission
ED threshold | -70dBm
Traffic model | Normal UE: FTP 3 as in TR 38.889 λ= 0.05,packet size: 0.5M VLP UE: The packet size of VLP UE is half of normal UE Wi-Fi: same with normal UE
UE dropping model | 6 SL-U pairs and 4 STAs per AP per 20 MHz Only one VLP UE exists per UE pair
Observation: SL VLP UE can maintain good UPT performance with lower power consumption and device complexity compared to normal UE.

## Slide 16
Preliminary evaluation results of SL WUS
SL RedCap
Observation: SL WUS can achieves significant power saving gain without notable PRR performance impact to both VUE and PUE.
Parameter | value
Deployment | Urban scenario
Link type | V2V, V2P, P2V
UE type | VUE : PUE = 2:1 (300:150)
Communication type | unicast
Bandwidth | 40MHz
Subcarrier spacing | 30KHz
DRX duration | 250ms
Traffic parameter for Periodic VUE | Packet arrival interval of periodic traffic: 500ms Packet latency requirement of periodic traffic: 500ms Packet size of periodic traffic: 800 or 1200byte
Traffic parameter for Aperiodic VUE | Packet arrival interval of aperiodic traffic: 250ms + an exponential random variable with the mean of 250 ms Packet latency requirement of aperiodic traffic: 250ms Packet size of aperiodic traffic: 200 ~ 2000byte
Traffic parameter for PUE | Traffic type: Periodic traffic Packet arrival interval of periodic traffic: 1000ms Packet latency requirement of periodic traffic: 100ms Packet size of periodic traffic: 800 or 1200byte

## Slide 17
SL FR2
Further sidelink evaluations

## Slide 18
Motivation
SL FR2
Proposal: Specify SL FR2 in Rel-19, including at least
  Beam management, including (initial) beam training, maintenance, measurement/reporting, recovery, etc.
  Resource allocation enhancement
  Operating on both FR2-1 and FR2-2
  Supporting unified framework for all the cast types
PQI Value | Resource Type | Default Priority Level | Packet Delay Budget | Packet Error Rate | Default Maximum Data Burst Volume | Default Averaging Window | Example Services
New value#1 | Delay Critical GBR | 5 | 5ms | 10-4 | 20000 bytes | 2000 ms | Interactive service - consume VR content with high compression rate via tethered VR headset
New value#2 |  | 6 | 10ms | 10-4 | 20000 bytes | 2000 ms | interactive service - consume VR content with low compression rate via tethered VR headset; Gaming or Interactive Data Exchanging;
XR and gaming are the acknowledged killer applications for XR glasses, Head Mounted Displays (HMDs), etc.
  SA2 has defined the corresponding PQI for such kinds of requirements.
  RAN1 has evaluated and concluded that current NR SL cannot support the required data rate.
The NR SL over FR2 (licensed/unlicensed) band is attractive because of the potentially higher performance and reliability, and better device integration level, than the other competitive technologies (e.g., 802.11ad/aj/ay, etc.).

## Slide 19
Rel-19 work planning
Work scope and TUs

## Slide 20
Candidate objectives
  Study and specify mechanism to support sidelink underlay transmission over licensed spectrum [RAN1, RAN2, RAN4]
    Dynamically resource sharing between Uu and SL transmissions
    Interference mitigation and cancellation
    Power control enhancement
  Study and specify mechanism to support sidelink RedCap devices over licensed and unlicensed spectrum [RAN1, RAN2, RAN4]
    Further power saving enhancements
    Very low power operation
    PA less device
  Specify enhanced sidelink operation on FR2-1 and FR2-2 [RAN1, RAN2, RAN4]
    Beam management, including (initial) beam training, maintenance, measurement/reporting, recovery, etc.
    Resource allocation enhancement
Rel-19 work planning
Work scope
Proposal: Sidelink evolution is introduced as a Rel-19 RAN1-lead work item with study phase (SI+WI).
  RAN1 (Leading WG): 1 TU, RAN2: 1 TU, RAN4: 1 TU

## Slide 22
Appendix
SLS evaluation assumption for sidelink underlay
Parameters | Value
Scenario | Dense Urban single layer
Layout | hexagonal grid, 7 macro sites, 3 sectors per site with wrap around
Inter-BS distance | 200m
Minimum BS-UE (2D) distance | 35m
Minimum UE-UE (2D) distance | 2m
Carrier frequency | 4GHz
Simulation bandwidth | 100MHz (273RB for 30kHz SCS)
Subcarrier spacing | 30kHz
TDD | All UL slot
BS Tx power | 49dBm
UE Tx power | 23dBm, P0 = -80, Alpha = 0.8
UE distribution | 80% indoor 3km/h and 20% outdoor 30km/h
BS receiver noise figure | 5dB
UE receiver noise figure | 9dB
UE number | 10 uu users/cell, 5 D2D pairs/cell
BS antenna height | 25m
UE antenna height | hUT = 3(nf1-1) +1.5, nf1 for outdoor UEs: 1, nf1 for indoor UEs: nf1~uniform (1, Nf1) where Nf1 = 1
BS antenna configurations | (M,N,P,Mg,Ng;Mp,Np)= (8,8,2,1,1;2,8), (dH, dV) =(0.5, 0.8)λ
Uu UE antenna configurations | (M,N,P,Mg,Ng;Mp,Np)= (1,2,2,1,1; 1,2)
SL UE antenna configurations | (M,N,P,Mg,Ng;Mp,Np)= (1,1,1,1,1; 1,1)
receiver | MMSE-IRC as the baseline receiver
Traffic model for Uu UL | 0.5Mbytes/packet, 18 packet/s
Traffic model for sidelink | Full buffer