## Slide 1
3GPP TSG RAN #101 RP-231805
Bangalore, India, September 11-15, 2023
Agenda Item: 8A.2.13.4
Source: vivo, NTT DOCOMO, INC., China telecom, China Unicom, TCL
Title: Rel-19 MUSIM enhancements (RAN2-led)
Document for: Discussion

## Slide 2
MUSIM-Gap enhancements
Motivation: For the periodic/short time activities in NW B, a finer granularity MUSIM gap in NW A is more suitable:
R17 per UE MUSIM gap causes data interruption in NW A
R18 MUSIM capability switching causes the related resources release with data throughput loss in NW A
Potential objectives:
  Specify the request/configuration of a finer granularity MUSIM gap (e.g. per CG, per FR, per CC) [RAN2]
Specify new RRM requirement for the finer granularity MUSIM gap [RAN4]
R19: A finer granularity MUSIM Gap

## Slide 3
MUSIM-Optimization for same operator and RAN sharing
Motivation:
Based on vivo statistics in China, 34% of dual USIM phones have the USIMs from the same operator. And in case of RAN sharing, the USIMs in the same device from the different operators may be served by the same RAN.
The performance of both network and UE can be improved if the network knows multiple USIMs are in the same device.
PO alignment in both RRC_IDLE/INACTIVE:
UE power saving gain: 35%
Dynamic capability sharing in both RRC_CONN: Avoid throughput loss
RRC_CONN+RRC_IDLE: Paging proxy
Avoid unnecessary data interruption in one NW
  Potential objectives: The UE reports the association information of multiple USIMs to the network, e.g., to CN or RAN. The coordination of RRC configuration and scheduling between USIMs can be based on the association information. [RAN2/SA2/CT1]

## Slide 4
MUSIM
WID (0.5~1TU for RAN2, 0.5TU for RAN4)
Objectives: To specify MUSIM enhancements in Rel-19:
    Enhancements of finer granularity (e.g. per CG, per FR, per CC) MUSIM gap:
      Specify the request/configuration of a finer granularity MUSIM gap [RAN2]
    Specify new RRM requirement for the finer granularity MUSIM gap [RAN4]
  The optimization for same operator and RAN sharing:
    Specify UE indicating the association information of multiple USIMs to the network, e.g., to CN or RAN. The coordination of RRC configuration and scheduling between USIMs can be based on the association information. [RAN2/SA2/CT1]
  Left over from R18 Capability switching, e.g., More information reporting for MUSIM band conflicting. [RAN2]