## Slide 1
3GPP TSG RAN # 101 RP-231808
Bangalore, India, September 11-15, 2023
Agenda Item: 8A.2.15
Source: vivo
Title: Rel-19 L2 UP Protocol enhancements (RAN2-led)
Document for: Discussion

## Slide 2
  L2 UP protocol enhancements
Simplify the UE process (e.g. security operation) due to high data rate in NR
  Motivation: Full data rate UPIP is mandatory in R16, high data process requirement for UEs
  For the same total bits, with the less number of PDU, Both integrity and encrypt Process time will be reduced due to PDCP Concatenation. (higher PDCP concatenation, less process time)
Both integrity and encrypt Process time are reduced with PDCP Concatenation.

## Slide 3
  L2 UP protocol enhancements
  PDCP SDUs concatenation or Partial PDU security
PDCP SDUs concatenation
Partial PDU Security need to be confirmed by SA3.
  Objective：Study the L2 UP protocol enhancement for PDCP concatenation.[RAN2]

## Slide 4
  L2 UP protocol enhancements
  Initial
  T-reordering expires
The unnecessary RLC SDU retransmission should be avoided.
Reduce the unnecessary RLC SDU retransmission
    RLC AM receiving window driven by its lower edge, i.e. RX_Next
      The PDU at lower edge will be retransmitted untill successful reception or reaching the Maximum retx number, i.e. RLF and re-estab.
    PDCP performs Re-ordering operation
      When t-reordering timer expires, receiving window is updated. Even if retx in RLC is successful, packet is discarded, which waste radio resources
  Objective： Study to avoid the unnecessary RLC SDU retransmission.[RAN2]

## Slide 5
L2 UP protocol enhancements
  SID(1TU for RAN2)
Objectives:
    Study the L2 UP protocol enhancement for PDCP concatenation.[RAN2]
    Study to avoid the unnecessary RLC SDU retransmission.[RAN2]