## Slide 1
3GPP TSG RAN #101 RP-231815
Bangalore, India, Sep 11-15, 2023
Source: vivo, CMCC, CATT, China Telecom, China Unicom, Nordic Semiconductor ASA,…
Document for: Discussion and Decision
Agenda Item: 9.2.6
Recommendation for LP-WUS waveform

## Slide 2
Outlines
Background
Comparison on potential LP-WUS waveforms
Motivation for unified LP-WUS signal design
Necessity on LP-SS for envelop detection based LP-WUR
Recommendation for LP-WUS waveform

## Slide 3
Background
RAN1 part of LP-WUS/WUR study completed in RAN1#114
Potential recommendation of LP-WUS waveform was discussed, the following possible agreement received majority support but objected by two companies.
Possible Agreement
Add the following recommendation to the conclusion section:
From RAN1 point of view, among the waveforms evaluated, OFDMA waveform and OOK waveform (with or without OFDMA sequences) with OOK1/4 scheme are recommended for possible down-selection.

## Slide 4
Comparison on potential LP-WUS waveforms (TR 38.869 )
 | OOK (OOK-1/4) | FSK (FSK-2) | OFDM
Receiver power consumption | Lowest power consumption LP-WUR ‘On’ power <=4units, and <=1 unit is reported by majority | Similar or slightly higher than OOK | Highest power consumption LP-WUR ‘On’ power <= 30 units, and >=10 units reported by majority
Timing error tolerance | Moderate robustness <=5us for OOK-1@30kHz <=3 us for OOK-4 M=2, <=1us for OOK-4 M=4. | Moderate robustness <=2us for FSK-2 M=1, <=2/3 us for FSK-2 M=2. | Tolerance to timing error varies with sliding window size, e.g., up to 4us but requires sliding window at receiver -> increased power consumption
Frequency error tolerance | The most robust 800kHz for OOK-4 M=4 | Good robustness 200kHz for M=2 | Less robustness 26kHz
Coverage note 1 | Feasible to reach MSG3 coverage via: 0.9~17.28note2 MHz*Symbol/bit (urban) 0.18~8.64 MHz*Symbol/bit (rural) | Feasible to reach MSG3 coverage via : 4.32~25.92note2 MHz*Symbol/bit (urban) 4.32MHz*Symbol/bit (rural) | Feasible to reach MSG3 coverage via: 0.31~4.32 MHz*Symbol/bit (urban) 1.8~3.6 MHz*Symbol/bit (rural)
Network overhead (SYS-BW 20MHz / 100MHz) | LP-WUS carrying up to 24bits, 5MHz <=1.98%, targeting MSG3 coverage LP-SS, 5MHz <=0.4% (320ms LP-SS periodicity and 1 slot (30kHz) duration) | LP-WUS carrying up to 24bits, 5MHz <=1.98%, targeting MSG3 coverage LP-SS not reported by companies | LP-WUS carrying up to 24bits, 5MHz <=0.16%, targeting MSG3 coverage LP-SS not needed
Network power consumption | LP-SS (1slot duration, MSG3 coverage) Power consumption increase caused by LP-SS is up to 3.9%/2.7%/1.1% for zero/low/medium loads. LP-WUS not reported | Not reported by companies | LP-WUS not reported by companies; LP-SS not needed
note 2: reported by one company (3dB additional antenna loss for WUR compared with MR)
note 1: RedCap and non-RedCap UE cases are not further distinguished

## Slide 5
Comparison on potential LP-WUS waveforms
Summary
Power consumption : OOK FSK < OFDM, there is no guarantee that OFDM receiver can be implemented with sufficient low power consumption, i.e. 10 units.
Time/frequency error tolerance:
  OOK is most tolerant to frequency error
  Similar time error tolerance for OOK, FSK. OFDM requires receiver sliding window for similar time error tolerance with the cost of higher receiver power consumption.
Coverage: To reach MSG 3 coverage, the required resource per bit: OFDM<OOK<FSK
The network overhead: To reach MSG 3 coverage, the system overhead of all LP-WUS waveforms are marginal (<=1.98%)
The network consumption: To reach MSG 3 coverage, the additional increased network power consumption rate is marginal (up to 3.9%/2.7%/1.1% for zero/low/medium loads)
Selection between OOK and FSK
OOK (OOK-1/OOK-4) is recommended, due to the following:
  OOK receiver has the lowest power consumption
  OOK provides better or similar performance than FSK in terms of time/frequency error tolerance.
  OOK requires less resources than FSK to achieve the MSG-3 coverage target.
  Much more inputs to RAN1 study for OOK than that of FSK
≈

## Slide 6
An Unified LP-WUS design (hybrid OOK/OFDM)
Waveform generation (TR 38.869 conclusion)
OOK can be generated by modulating sub-carriers of CP-OFDM and by existing gNB transmitter.
Knowledge of sequence(s) used in LP-WUS waveform generation may improve performance for a receiver with I/Q branches, i.e. OFDM-based receiver
An unified LP-WUS design: OFDM sequence(s) modulated on top of OOK
An common unified LP-WUS transmitted from the gNB that can be detected by UEs with two possible LP-WUR architectures
  OOK based LP-WUR (envelop detector ) for lowest power consumption
  OFDM based LP-WUR for better performance (coverage, inter-cell interference) by detecting the known OFDM sequence(s) that may be used by gNB Tx to generate OOK “ON” duration
Reduce overhead: No separate LP-WUS transmissions for two LP-WUR architectures
Simplify the UE grouping/sub-grouping management for gNB
Potential payload size of LP-WUS
LP-WUS shall be able to carry at least 8bits (excluding CRC, if any)
  For IDLE/INACTIVE mode, to provide at least similar subgrouping indication as in R17 PEI
  For CONNECTED mode, to provide command for UE PDCCH monitoring

## Slide 7
Necessity of LP-SS for envelop detection based LP-WUR
Necessity on LP-SS for RRM measurement and synchronization in IDLE/INACTIVE
RAN1 concluded the following:
At least for LP-WUR that cannot receive existing PSS/SSS (i.e envelop detector based LP-WUR), periodic LP-SS signal is beneficial for the following functionalities:
(a) RRM measurements by LP-WUR, if supported
(b) At least coarse time synchronization of LP-WUR.
(c) At least coarse frequency synchronization of LP-WUR.
For LP-WUR that can receive existing PSS/SSS potentially assisted by PBCH DMRS/TRS for synchronization (i.e. OFDM based LP-WUR)
existing PSS/SSS potentially assisted by PBCH DMRS/TRS may be used for above functionality.
RAN1 Study Conclusion
RAN1 concluded the following are beneficial for LP-WUS operation in IDLE/INACTIVE
MR serving and neighbor cell measurement with further time domain relaxation than Rel-18
At least serving cell RRM offloading from MR to LP-WUR

## Slide 8
Recommendation for LP-WUS waveform and LP-SS
LP-WUS
  Recommend to specify an unified LP-WUS design that is applicable for both envelop detection based LP-WUR and OFDM based LP-WUR, and for both IDLE/INACTIVE and CONNECTED mode usage.
    OOK (OOK-1 and/or OOK-4) based LP-WUS is supported for envelop detection based LP-WUR
      OFDM sequence(s) can be additionally modulated on top of OOK for OFDM based LP-WUR for better detection performance
    Information payload carried by LP-WUS can be [1~X] bits (excluding CRC, if any), with X>=8, upper limit to be decided in WI phase
    LP-WUS shall be able to reach at least the coverage of existing Msg3 PUSCH of single transmission.
    It shall be possible to generate the unified LP-WUS with existing hardware from gNB transmitter perspective
LP-SS
  Recommend to specify an OOK (OOK-1 and/or OOK-4) based periodic LP-SS for envelop detection based LP-WUR for synchronization and serving cell measurement purpose, with its coverage performance no worse than LP-WUS and periodicity no less than [320ms]
    It shall be possible to generate the OOK based LP-SS with existing hardware from gNB transmitter perspective
    For OFDM based LP-WUR, existing NR signal, e.g., SSS can be used for synchronization and measurements, instead of LP-SS.

## Slide 10
Description on OOK-1/OOK-4 /FSK-2 Waveforms
OOK-1: Single-bit in 1 OFDM symbol, SCs of LP-WUS
Single-bit in 1 OFDM symbol, SCs of LP-WUS are
  OOK=1 means all SCs are modulated
  OOK=0 means all SCs are zero power (from base-band point of view)
OOK-4: Transform M-bit OOK in time domain
  N SCs of OOK-1 are generated by a transformation (DFT/Least square)
    N’ samples are generated from M-bits
    signal modification may or may NOT be used
    truncation or other additional modification may
    or may NOT be used, if not used, N is the same as N’
  N’ can be the same as K
FSK-2: N SCs of LP-WUS are separated to 2^M segments with potential guard-bands in-between and around.
  segment comprises one sub-carrier or multiple contiguous SCs
  one segment from 2^M segments is modulated, other segments of SCs are zero power (from base-band point of view)
TR 38.869 section 7.2.1.1

## Slide 11
Power consumption for potential LP-WUS waveforms reception
Receiver architectures for OOK: power consumption and noise figure
  Relative power consumption and noise figure for OOK-1/2/4 with heterodyne architecture with IF envelope detection
  Relative power consumption and noise figure for OOK-1/2/4 with homodyne/zero-IF architecture with baseband envelope detection
  Relative power consumption and noise figure for FSK with parallel heterodyne architecture
  Relative power consumption and noise figure for FSK with parallel homodyne architecture
Source reference | [7A-1] | [7A-2] | [7A-3] | [7A-4] | [7A-5] | [7A-6]
Power consumption (ON state) | 0.1 for single-branch, 0.01 for each additional branch | 0.5 | 0.1~1 | 0.1 | 0.1~1 | 1~4
Noise figure (dB) | 15 | 10~15 | [9-15] | 15 | 12 | 12~15
Source reference | [7A-1] | [7A-2] | [7A-3] | [7A-4] | [7A-5] | [7A-6] | [7A-7] | [7A-8] | [7A-9] | [7A-10]
Power consumption (ON state) | 0.09 for single-branch, 0.01 or 0.02 for each additional branch | 0.5 | 0.1~1 | 0.1 | 0.05~ 0.5 | 0.5~1 | 0.1~0.5 | 4 | ~1 | 0.1~0.5
Noise figure (dB) | 15 | 10~15 | [10-16] | 15 | 12 | 15 | 12~15 | 15 | ~15 | 12
Source reference | [7A-1] | [7A-2] | [7A-3] | [7A-4]
Power consumption (ON state) | 0.1 for single-branch, 0.01 for each additional branch | 0.5 | 0.1~1 | 0.1
Noise figure (dB) | 15 | 10~15 | [9~15] | 15
Source reference | [7A-1] | [7A-2] | [7A-3] | [7A-4]
Power consumption (ON state) | 0.09 for single-branch, 0.01 or 0.02 for each additional branch | 0.5 | 0.1~1 | 0.1
Noise figure (dB) | 15 | 10~15 | [10~16] | 15
TR 38.869 section 7.1.1a.1, 7.1.1a.2

## Slide 12
Power consumption for potential LP-WUS waveforms reception
Receiver architectures for OFDM: power consumption and noise figure
  Relative power consumption and noise figure for OFDM-based signal with time-domain correlation
  Frequency-domain correlation (with FFT)
Source reference | [7A-1] | [7A-3] | [7A-5] | [7A-6] | [7A-7] | [7A-8] | [7A-9]
Power consumption (ON state) | 0.15~0.2 | 10 | 10~20 | 10~30 | 1~5 | 10~20 | ~5
Noise figure (dB) | 15 | 9.5 | 9.5 or 12 | 9 | 7~10 | 9 | 15~25
Source reference | [7A-2] | [7A-3] | [7A-5] | [7A-7] | [7A-10] | [7A-10]
Power consumption (ON state) | 10 | 30 | 20~30 | 1~5 | 10 | 4
Noise figure (dB) | 7~12 | 7 | 9.5 or 12 | 7~10 | 9 | 12
TR 38.869 section 7.1.1a.3

## Slide 13
Coverage evaluation for potential LP-WUS waveforms
OOK, Urban, Normal UE
For Normal UE in Urban, [8A-2], [8A-3], [8A-5], [8A-6], [8A-7], [8A-8], [8A-11], [8A-13] and [8A-14], show OOK based LP-WUS is feasible to achieve comparable MIL (i.e.MIL margin Y>=-1dB) than PUSCH for Msg.3
[8A-2], [8A-5], [8A-6], [8A-8], [8A-11] and [8A-13] show that, with LP-WUS resource X = 1.8~8.64 MHz*Symbol/bit, MIL margin Y = -0.93~11.97dB, assuming no power boosting for LP-WUS;
[8A-7] show that, with LP-WUS resource X=17.28 MHz*Symbol/bit, MIL margin Y=0.06dB, assuming antenna element gain of LP-WUR is 3dB worse than MR.
[8A-3] show that, with LP-WUS resource X=241.92 MHz*Symbol/bit, MIL margin Y=-0.96dB, assuming 4dB HARQ gain from 2 retransmissions for Msg3 PUSCH and no power boost for LP-WUS
[8A-2], [8A-11] and [8A-14], show that, with LP-WUS resource X=0.9~4.32 MHz*Symbol/bit, MIL margin Y=-0.61dB~1.24dB, assuming 3dB power boosting for LP-WUS
FSK, Urban, Normal and Redcap UE
TR 38.869 section 8.2
For normal UE and Urban scenario, comparing MIL of FSK based LP-WUS to legacy PUSCH for Msg.3,
[8A-2], [8A-5] and [8A-7] show it is feasible to achieve comparable MIL (i.e.MIL margin Y>=-1dB)
  [8A-2] with LP-WUS resource X=4.32 MHz*Symbol/bit, MIL margin Y=-0.31dB
  [8A-5] with LP-WUS resource X=4.32 MHz*Symbol/bit, MIL margin Y=-0.43dB
  [8A-7] with LP-WUS resource X=25.92 MHz*Symbol/bit, MIL margin Y=-0.34dB, assuming antenna element gain of LP-WUR is 3dB worse than MR.
[8A-3] show that with the LP-WUS resource of X=9.72 MHz*Symbol/bit , the MIL margin Y is -13.06 dB.
OFDM, Urban, Normal UE
For Normal UE and Urban scenario, [8A-3], [8A-5], [8A-7], [8A-8], [8A-11] and [8A-13], show OFDM based LP-WUS is feasible to achieve comparable MIL (i.e. MIL margin >=-1dB) than PUSCH for Msg.3
[8A-5], [8A-8], [8A-11] and [8A-13] show that with LP-WUS resource X= 0.31~4.32 MHz*Symbol/bit, MIL margin Y=0.06dB~18.03dB
[8A-7] shows X= 1.08 MHz*Symbol/bit, MIL margin Y=-0.24dB, assuming antenna element gain of LP-WUR is 3dB worse than MR.
[8A-3] shows that with LP-WUS resource X= 2.16 MHz*Symbol/bit, MIL margin Y=2.82dB, assuming 4dB HARQ gain from 2 retransmissions for Msg3 PUSCH