## Slide 1
3GPP TSG RAN #101 RP-231816
Bangalore, Sep 11-15, 2023
Source: vivo, CATT, China Telecom, Nordic Semiconductor ASA, Spreadtrum Communications
Document for: Discussion and Decision
Agenda Item: 9.2.6
Handling of RRM Studies for LP-WUS/WUR SI

## Slide 2
Outlines
Motivation
RRM Measurement Aspects Studied by RAN 1
Proposed RAN 4 Study Scope and TU Request

## Slide 3
Motivation
Necessity on RRM relaxation of MR and RRM offloading to LP-WUR
MR RRM relaxation/ offloading to LP-WUR | Mean power saving gain range** | Mean power saving gain average** | # of input sources
No MR RRM relaxation and offloading to LP-WUR | -211% | -624%~-5% | 5
MR RRM relaxation < 8 times | 4% | -18%~50% | 6
8 times <= MR RRM relaxation < =16 times | 40% | -18%~60% | 9
MR RRM relaxation >16 times | 60% | 22%~90% | 9
No RRM relaxation, fully offloading to LP-WUR | 83% | 76%~94% | 10
* TR 38.869
** Power saving gain obtained when compared
to i-DRX with or without PEI
Table Power saving gain via duty-cycled LP-WUS monitoring**
Chart: 
| No MR RRM relaxed | MR relaxed < 8 times | 8times ≤ MR relaxed ≤ 16times | MR relaxed > 16 times | MR offload RRM to LR
min: power saving gain | -6.24 | -0.18 | -0.18 | 0.22 | 0.76
mean: power saving gain | -2.11 | 0.04 | 0.4 | 0.6 | 0.83
max: power saving gain | -0.05 | 0.5 | 0.6 | 0.9 | 0.94
RAN 1 Study Conclusion*
RAN1 studied the LP-WUS /LP-WUR operation in IDLE /INACTIVE and concluded the following
UE power saving gain cannot be observed if the existing Rel-18 MR RRM measurement periodicity for serving and neighbor cells are applied and UE MR enters in ultra-deep sleep during LP LP-WUS monitoring

## Slide 4
RRM Measurement Aspects Studied by RAN 1
RRM measurement signal for LP-WUR
RAN1 concluded the following:
At least for LP-WUR that cannot receive existing PSS/SSS (i.e envelop detector based LP-WUR), periodic LP-SS signal is beneficial for the following functionalities:
(a) RRM measurements by LP-WUR, if supported
(b) At least coarse time synchronization of LP-WUR.
(c) At least coarse frequency synchronization of LP-WUR.
For LP-WUR that can receive existing PSS/SSS potentially assisted by PBCH DMRS/TRS for synchronization (i.e. OFDM based LP-WUR)
existing PSS/SSS potentially assisted by PBCH DMRS/TRS may be used for above functionality.
RAN1 Study Conclusion
RAN1 concluded the following are beneficial for LP-WUS operation in IDLE/INACTIVE
MR serving and neighbor cell measurement with further time domain relaxation than Rel-18
At least serving cell RRM offloading from MR to LR

## Slide 5
RRM Measurement Aspects Studied by RAN 1
LP-WUR RRM Measurement Metric: RSRP and RSRQ
RSRP and RSRQ measurement accuracy based on LP-SS (based on OOK, for envelop detector based LP-WUR)
SNR target X= {-3, -6, -9, -11} dB: under TDL-C channel, depending on 90% accuracy of 3 or 5 dB, (1 -70) symbols spreading over 1-5 periods is required for measurement
SNR target X= {-9, -11} dB: under AWGN channel, depending on 90% accuracy of 3 or 5 dB, (1 -20) symbols spreading over 1-3 periods is required for measurement
SNR target X is seen by LP-WUR, corresponding SNR observed by MR and LR is different due to NF difference between them
RSRP measurement accuracy based on SSS (for OFDM based LP-WUR)
SNR target X= [-3, -6] dB: under AWGN channel, depending on 90% accuracy of 3dB, 1 OFDMA symbol in 1 period is required
  Observation:
  RAN1 has complete the study and justified a set of enhancements for RRM measurements which are beneficial for LP-WUS/WUR operation in IDLE/INACTIVE states. However, RAN4 was not involved in the study due to no RAN4 RRM TU allocated to the SI.

## Slide 6
Proposed RAN4 study scope and TU request
Proposal 1: RAN4 to review the outcome of RAN1 studies on RRM aspects for LP-WUS/WUR for feasibility verification.
  RRM measurement offloading to LP-WUR, including
    Consider different LP-WUR architectures:
      LP-SS based RRM measurement for envelop detection based LP-WUR
      SSS based RRM measurement for OFDM based LP-WUR
    For each of above, to review:
      LP-WUR RRM metrics, e.g. LP-RSRP/LP-RSRQ;
      SNR target X for LP-WUR RRM measurement considering the practical noise figure of LP-WUR
      Measurement accuracy target Y for LP-WUR RRM considering the practical noise figure of LP-WUR
  Proposal 2: Additional TU requested for RAN4 RRM
 | 4Q'2023 | 
 | 9-Oct | 13-Nov
Low power WUS (RAN4) RF | 0.25 | 0.25
Low power WUS (RAN4) RRM | 0.25 | 0.25

## Slide 8
RRM Metrics: TR.38.869
For at least RRM serving cell measurement performed by LP-WUR based on reference signal(s), RAN1 identified at least the following metrics for further study and evaluation (including feasibility, complexity, power consumption, etc)
LP-RSSI or Energy detection: linear average of total received power over a RSSI resource.
    FFS RSSI resource.
LP-RSRP: linear average of received power of resource of reference signal(s) or signal(s) parts.
    FFS resource of reference signal(s) or signal(s) parts
LP-SINR = LP-RSRP/(power of interference and noise)
    FFS how to define “power of interference and noise”
LP-RSRQ= [N x] LP-RSRP/LP-RSSI, where N is the factor of resource size difference for evaluation LP-RSRP and LP-RSSI.
Accounting AGC accuracy, ADC of at least 4 bits is required.
Note: Reference signal for performing measurements can be e.g. SSB (PSS/SSS/PBCH DMRS), LP-WUS-waveform sequence, LP-SS
Note: The definition of metrics could be further refined based on future study