## Slide 1
3GPP TSG RAN Meeting #101 RP-231852
Bangalore, India, September 11-15, 2023
Agenda Item: | 8A.2.2
Source: | Spreadtrum Communications
Title: | Views on Rel-19 MIMO enhancement
Document for: | Discussion and decision
WWW.UNISOC.COM

## Slide 2: R19 MIMO
Motivation on enhancements for mTRP
  For S-DCI based NCJT and CJT, ideal backhaul is always assumed.
  In Rel-18 MIMO, CSI enhancement for CJT has been specified with the following assumptions.
    Targeting FR1
    Up to 4 TRPs
    Assuming ideal backhaul and synchronization
    The same number of antenna ports across TRPs
  In Rel-19, some of the above assumptions can be relaxed to support more realistic assumptions and more divergent deployments.
Multi-TRP transmission

## Slide 3: R19 MIMO
Multi-TRP with different antenna port layouts across TRPs
RS
RS
Report
UE assisted antenna calibration across TRPs
  Study, and if justified, specify CSI enhancement to support different antenna port layouts across TRPs
    Rel-18 Type-II codebook refinement for CJT and its associated CSI reporting
  Potential enhancements for mTRP
  Study, and if justified, specify UE assisted antenna calibration across TRPs for non-ideal synchronization
    UE reporting of inter-TRP synchronization error measured via legacy DL reference signal

## Slide 4: R19 MIMO
  Motivation on UL enhancement
  UL performance is getting more important to better support CPE/FWA/vehicle/industrial devices
  In Rel-18 MIMO, several UL related enhancements have been discussed, such as simultaneous multi-panel UL transmission and 8 Tx UL operation.
  Frequency-selective precoding is one of the potential enhancements to further improve UL performance.
Frequency selective precoding
Potential UL enhancements
  Study, and if justified, specify frequency-selective precoding
CIR

## Slide 5: R19 MIMO
  Motivation on latency reduction for beam management
  Overhead and latency of beam measurement/reporting procedure will become a critical issue when the number of beams is large or the UE moves with high speed.
  Latency reduction of beam measurement and reporting was discussed in Rel-17, but no progress was achieved due to low priority.
  UE initiated beam management can be considered as a candidate solution to reduce latency.
UE initiated beam management
  Potential enhancements for beam management
  Study, and if justified, specify UE initiated beam management

## Slide 6: R19 MIMO
  Summary of potential MIMO enhancements in R19
  Study, and if justified, specify UE assisted antenna calibration across TRPs for non-ideal synchronization
    UE reporting of inter-TRP synchronization error measured via legacy DL reference signal
  Study, and if justified, specify CSI enhancement to support different antenna port layouts across TRPs
    Rel-18 Type-II codebook refinement for CJT and its associated CSI reporting
  Study, and if justified, specify frequency-selective precoding
  Study, and if justified, specify UE initiated beam management

## Slide 7
Thanks