## Slide 1
MIMO Evolution in Rel-19
Bangalore, India, September, 11th – 15th, 2023
Agenda item: 8A.2.2
Source: Nokia, Nokia Shanghai Bell
RP-231890 3GPP RAN#101

## Slide 2
Overview
Motivations and key proposals for MIMO evolution work Rel-19​
MIMO technologies are at the heart of many NR operations, in particular regarding beam management
3GPP has enhanced MIMO over the last few releases, including a renewal and extension of the beam management framework to address new scenarios, including multiple TRPs and joint transmission
It is important to ensure the renewed framework is complete, so that it is a solid baseline for any future enhancements
At the same time, the overall scope of MIMO work in Rel-19 needs to be constrained, and any new areas to be considered based on clear market needs
In Rel-19 the key areas for MIMO enhancements are:
  Beam management: UE assisted operation, dynamic TCI state updates
  Extend number of CSI-RS ports for Type-I/II CB to 64 (and potentially 128)
  Multi-TRP enhancements: simultaneous UL transmissions (Rel-18 leftover)
  CSI enhancements for joint transmission (type II CSI)
  Enhancements for SRS-based CSI-acquisition

## Slide 3
Beam management / Multi-Beam operation
UE-centric operation
UE initiated/assisted Beam Management ​(BM)
  Thus, UE could be enabled to trigger the beam reporting/change that can reduce latency and overhead (reduced need for periodic reporting)
    Faster than periodic L1-RSRP reporting
    Assume legacy CSI reporting as baseline
  Furthermore, gNB could allow some flexibility in the beam pair link selection by allowing UE to select among a given set​
  Reduces overhead and latency compared to existing procedures, which is particularly relevant in highly dynamic channels, such as in FR2
Dynamic TCI state update for periodic CSI-RS​
  Periodic CSI-RS is the main time and frequency tracking source signal of the NR system​
  In addition, typically, periodic CSI-RSs are used for BM measurements and CSI acquisition​
  However, only RRC-based beam switching is currently allowed​, which is therefore relatively slow
  System operation would be enhanced significantly if more dynamic beam switching is supported for periodic CSI-RS, e.g., MAC based

## Slide 4
Extending number of CSI-RS ports for CSI Acquisition
There is widespread deployment of Massive MIMO with 64TRX arrays in the upper FR1 bands (3.5GHz, etc.).
  CSI acquisition with Type I and Type II CSI is currently limited to 32 ports.
  Leveraging SRS for CSI acquisition in TDD can provide high mean UE SE, but the edge rates can be unacceptably low with large ISDs due to limited UL TX power and path-loss challenges.
  Leveraging precoded CSI-RS with CRI/PMI can provide acceptable edge rates with larger ISDs, while penalizing mean UE SE compared to that when leveraging SRS.
Initial performance assessment of a 64-port Type I extension: (SLS at 3.5GHz UMa-500m with full buffer traffic)
  Compared to CRI/PMI feedback: a 64-port Type I extension can provide higher (>20%) mean UE SE with similar rates at cell edge
  Compared to SRS-based CSI acquisition: a 64-port Type I extension can provide significantly higher edge rates (>100%) but with only a small (<10%) decrease in mean UE SE.
Propose to support extending the CSI acquisition to 64 ports, and possibly to 128 ports as well
  Prioritize support for 64 ports with arrays having 8-columns (4,8,2) and 16-columns (2,16,2).

## Slide 5
Enhanced multi-TRP operation
Simultaneous UL transmissions of PUCCH and PUSCH – Rel-18 leftover
Simultaneous UL transmissions from multiple panels (STxMP) of PUCCH and PUSCH
  The scope of the Rel-18 simultaneous UL transmissions objective for multi-TRP was restricted to simultaneous transmission of two PUCCHs or two PUSCHs, meaning that simultaneous UL transmissions of PUCCH and PUSCH is not possible.
  Avoiding overlap between PUSCH and PUCCH may not be feasible in practice, especially under Multi-DCI mode.
  Therefore, to unleash full potential of the simultaneous UL transmissions feature, simultaneous transmissions of PUCCH and PUSCH can be adopted/enabled in Rel-19.
  Example of STxMP of PUCCH and PUSCH:
PUSCH
Time
Frequency
PUCCH
TRP-1
TRP-2

## Slide 6
CSI acquisition framework
Extension of Type II CSI
Extend Type II CSI to support Rank 8:
Motivation: improve CJT performance with low-to-moderate traffic levels where the higher rank per UE can significantly improve performance.
Rel-18 extends Type II CSI to support CJT with up to rank 4 per UE
In Rel-19 extend Type II for CJT to support up to rank 8 per UE for 8RX UEs, e.g. supporting up to rank 4 on each panel  increase spatial multiplexing capabilities for CJT

## Slide 7
Latency and overhead reduction for SRS-based CSI-acquisition
Gap-less SRS switching
Typically, it would be beneficial to use 1T8R antenna switching configuration to increase DL throughput
  See Figure, which does not take into account latency and overhead increase
However, due to use of guard periods with antenna switching, the UL SRS resource overhead and latency may increase drastically (e.g. 1T4R  3 guard periods required or 1T8R 7 guard periods required), thus compromising the potential gains
To reduce latency and overhead related to antenna switching, new antenna switching configurations could be specified (e.g. 1T8R for 4/8TX UEs) with reduced amount of guard periods or even without any guard periods
This should be feasible for UEs capable of transmitting and receiving simultaneously with, e.g. 4/8TX and 4/8RX
Benefits of such an approach include:
Reduced number of scheduling restrictions and interruptions per UE​
Higher UL SRS resource utilization​
Improved SRS-based CSI acquisition latency and reduced overhead while maintaining higher quality SRS-based CSI acquisition

## Slide 8
Summary
Beam Management / Multi Beam Operation:
Dynamic TCI state updates for periodic CSI-RS: MAC-CE rather than RRC-configured TRS and CSI-RS: better for dynamic channels
UE initiated/assisted Beam Management
Improving latency and streamlining the beam management framework
CSI Acquisition Framework
Extend CSI acquisition to 64 (128?) ports
FR1: Study extending Type II CSI to up to Rank 8 operation
Improving SRS-based CSI-acquisition latency & quality
Reference Signals
SRS: Gap-less operation for antenna-switched UEs.
Improving system performance in FR1 and FR2
Improving latency and flexibility for UL transmissions for M-TRP
Multi-TRP enhancements:
Simultaneous UL transmissions of PUCCH and PUSCH