## Slide 1
3GPP TSG RAN Meeting #101 RP-231910
Bangalore, India, September 11-15, 2023
Agenda Item: | 8A.2.11
Source: | Spreadtrum Communications
Title: | Channel modeling for ISAC in Rel-19
Document for: | Discussion and decision
WWW.UNISOC.COM

## Slide 2: Background
Index | Use Case | Index | Use Case
1 | Intruder detection in smart home | 17 | Health monitoring at home
2 | Pedestrian/animal intrusion detection on a highway | 18 | Service continuity of unobtrusive health monitoring
3 | Rainfall monitoring | 19 | Sensor Groups
4 | Transparent Sensing Use Case | 20 | Sensing for Parking Space Determination
5 | Sensing for flooding in smart cities | 21 | Seamless XR streaming
6 | Intruder detection in surroundings of smart home | 22 | UAVs/vehicles/pedestrians detection near Smart Grid equipment
7 | Sensing for railway intrusion detection | 23 | AMR collision avoidance in smart factories
8 | Sensing Assisted Automotive Maneuvering and Navigation | 24 | Roaming for sensing service of sports monitoring
9 | AGV detection and tracking in factories | 25 | Immersive experience based on sensing
10 | UAV flight trajectory tracing | 26 | Accurate sensing for automotive maneuvering and navigation service
11 | Sensing at crossroads with/without obstacle | 27 | Public safety search and rescue or apprehend
12 | Network assisted sensing to avoid UAV collision | 28 | Vehicles Sensing for ADAS
13 | Sensing for UAV intrusion detection | 29 | Gesture Recognition for Application Navigation and Immersive Interaction
14 | Sensing for tourist spot traffic management | 30 | Sensing for automotive maneuvering and navigation service when not served by RAN
15 | Contactless sleep monitoring service | 31 | Blind spot detection
16 | Protection of Sensing Information | 32 | Integrated sensing and positioning in factory hall
3GPP SA1 is working on the identification of use cases and KPIs for ISAC
The identified use cases are captured in TR 22.837

## Slide 3: Typical use cases
Typical use cases for further study in RAN1 Rel-19
    UAV: sensing for flight trajectory tracing, collision avoidance, intrusion detection
    Smart traffic: sensing in highway, railway, crossroads, parking space
    Smart home: intruder detection, health monitoring
UAV
Smart home
Smart traffic

## Slide 4: Channel model for sensing
In order to evaluate sensing performance, it is essential to define channel model for sensing.
TR 38.901 has modeled the multipath channel between gNB and UE without the modeling of sensing target(s).
Radar Cross Section (RCS) of the sensing target is an important factor in channel modeling for sensing.
Typical RCS for simple shapes
Example of channel model for sensing

## Slide 5: General objective
Mono-static sensing
Bi-static sensing
Sensing target
Sensing target
Sensing target
Sensing target
Tx
Rx
Tx
Rx
Tx
Rx
Tx
Rx
Sensing target
Tx
Rx
Sensing target
Tx
Rx
General objective
  Study on channel modeling enhancement for sensing based on TR 38.901 [RAN1]
    Large scale fading including RCS of the sensing target
    Small scale fading
      Modeling of sensing path
      Modeling of interference path from the environment
    Study whether/how to ensure spatial consistency
    Strive to define a unified channel model for varies sensing modes

## Slide 6: Appendix
Large scale fading
  Pathloss considering distance from transmitter to sensing target and distance from sensing target to receiver
    Pathloss calculation can be based on TR 38.901
  Radar Cross Section (RCS) of the target is modeled as additional large scale fading parameter
    Randomly generated based on specific distribution, e.g. Uniform distribution, Gaussian distribution,…
Bi-static sensing
Mono-static sensing
RCS
RCS

## Slide 7: Appendix
Small scale fading for single-hop assumption
  Step 1: Generate delay/power/angles of each cluster between transmitter and receiver according to TR 38.901.
    For mono-static sensing: The angles are symmetrical.
  Step 2: Calculate delay/power/angles of sensing cluster between transmitter and sensing target and between sensing target and receiver according to the location of sensing target.
  Step 3: Replace one cluster with the sensing cluster.
  Further steps are according to TR 38.901.
Bi-static sensing
Mono-static sensing

## Slide 8: Appendix
Small scale fading for multi-hop assumption
  Step 1: Generate delay/power/angles of each cluster between transmitter and sensing target according to TR 38.901.
  Step 2: Identify the locations of scatters according to departure angles and delays.
  Step 3: Calculate delay/power/angles of each cluster between sensing target and receiver including clusters that passing through the identified scatters.
    For mono-static sensing: The reflection clusters are the same as the forward clusters.
  Step 4: Perform random coupling of the generated clusters and calculated clusters.
  Further steps are according to TR 38.901.
Bi-static sensing
Mono-static sensing

## Slide 9
Thanks