## Slide 1: Views on scope for NR RAN Topology enhancements in Rel-19
3GPP TSG RAN Meeting #101
Bangalore, India
September 11-15, 2023
Agenda Item: 8A.2.14.1
RP-231973
Qualcomm Incorporated

## Slide 2
The legacy building blocks for 5G RAN topologies should be enhanced to provide a broader range of use cases, such as:
  5G access for UEs onboard aircrafts, cruise ships, helicopters and vehicles in remote areas with limited sky visibility
  Multi-hop/redundant backhauling of mobile relays for public safety and disaster recovery
  Backhauling via NTN, and Xn-/NG-based NTNTN handover for backhaul.
  Support for onboard/on-site MEC, local services, and inter-UE communications.
  No need for roaming or RAN-sharing agreements between onboard/onsite access PLMNs and backhaul PLMN(s)
NR RAN Topology Enhancements: New use cases via WAB & IAB

## Slide 3
UE
Integrated Access and Backhauling (IAB):
  Relay holds DU function (IAB-DU) and UE function (IAB-MT).
  Backhauling via dedicated BAP sublayer on L2.
Wireless Access and Backhauling (WAB):
  Relay holds full gNB function and UE function (WAB-MT).
  Backhauling over PDU session betw. WAB-MT and BH UPF.
WAB vs. IAB
UE’s
NGC
IAB
DU
NR
IAB
node
Access PDU session
WAB
MT
gNB
BH
UPF
UE’s
NGC
BH PDU session
NR
gNB
NR
WAB
node
Access PDU session
IAB
MT
IAB-donor
NG
NG
AMF
UE
Access
Access
BH
IAB
DU
IAB
node
IAB
MT
NR
NR
BH
BH
DN
DN
WAB vs. IAB
  Rel-16/17 IAB supports multi-hop/redundant topologies on BH. Multi-hop WAB has not been defined by 3GPP .
  Rel-18 mobile IAB supports IAB-node mobility with single-hop BH. A mobile gNB (WAB) has not yet been considered by 3GPP.
  IAB supports in-band operation for access and backhaul. An equivalent solution has not yet been considered for WAB by 3GPP.
  IAB supports end-to-end QoS across access and backhaul. An equivalent solution is presently not supported for WAB.
  The WAB node can support local services at the relay via implementation by collocating a UPF with the gNB. This is not possible for IAB since the IAB-node does not support a CU function.
  WAB does not require RAN sharing between access PLMN and BH PLMN. IAB does require such RAN sharing.
  WAB can apply all legacy Uu mobility procedures on the BH. IAB has limitations since it uses a special L2 stack with BAP.
IAB
WAB

## Slide 4: 5G access for UEs in aircrafts, vessels, vehicles in remote areas
  Aspects to be considered for this use case
    Single-hop backhauling is sufficient.
    NTN-based BH with support for Xn- and/or NG-based NTNTN handover.
    Robustness on BH using CHO and/or DC desirable.
    Support for onboard MEC, local services, and direct inter-UE communications.
    Access PLMNs may not have roaming or RAN sharing agreement with BH PLMN
  Best solution candidate: WAB
    Supports MEC/onboard services, legacy NTN mobility procedures on BH, and allows separate PLMNs on access and BH without RAN sharing agreements.
Onboard
Service
Onboard
Service
NTN BH
BH PLMN
UPF
Access PLMN2
NGC
Access PLMN1
NGC
gNB
WAB
MT
UPF
BH gNB
BH PLMN
UPF
Access
PLMN1
NGC
Access
PLMN2
NGC
Onboard
Service
BH PDU session
NTN
BH gNB
NR
NR
Access PDU session
Access PDU session
NR
NR
UE
PLMN1
UE
PLMN 2
DN
DN
DN
gNB/WAB-MT
gNB/WAB-MT
WAB-node

## Slide 5: 5G access for UEs in helicopters (commercial helicopter flights)
  Aspects to be considered for this use case
    Same as for 5G access on aircrafts.
    For backhauling via TN, the onboard MT needs to support UAV functionality since it can “see” many TN gNBs due to high altitude and LOS condition.
    Onboard UEs also have high altitude and LOS condition to TN but they may not support UAV functionality.
  Best solution candidate: WAB
    Full gNB onboard is aware of UAV condition of onboard UE, even if onboard UE does not support UAV functionality.
    Onboard WAB-MT supports UAV functionality to connect to TN.
    WAB-MT can potentially also use NTN for backhauling.
TN BH
BH gNBs on TN
WAB-MT is UAV!
UE
UE
gNB/WAB-MT
gNB
WAB
MT
BH gNB
BH PLMN
UPF
Access
PLMN1
NGC
Access
PLMN2
NGC
BH PDU session
NTN
NR
NR
Access PDU session
Access PDU session
UE
PLMN1
UE
PLMN2
DN
DN
WAB-node

## Slide 6: Multi-hop backhauling for public safety and disaster recovery
  Aspects to be considered to support use case
    gNB deployed in PS/disaster recovery area
    gNB backhauling is supported via NTN and/or TN
    Support for on-site services, MEC and local inter-UE communications.
    gNB coverage can be extended via mesh of moving relay nodes.
  Potential solution: WAB combined with multi-hop IAB
    On-site WAB-node supports NTN backhauling as well as MEC/local services and on-site inter-UE communications.
    WAB-node contains IAB-donor for local coverage extension via multi-hop IAB
IAB
donor
WAB
MT
UPF
BH gNB
BH PLMN
UPF
Access
PLMN
NGC
Onboard
Service
BH PDU session
NTN
NR
Access PDU session
UE
DN
DN
IAB-node
IAB
DU
IAB
MT
NR BH
IAB-node
IAB
DU
IAB
MT
NR BH
NR
WAB-node
Access PDU session
UE

## Slide 7
The new use cases can be addressed using legacy 5G RAN architecture. At this stage, any (major) change to the 5G architecture should be avoided.
RAN3/2 should discuss RAN-related enhancements to support these scenarios. This effort should occur independently from SA2, even if SA2 pursues a parallel effort. Some RAN-related enhancements may have SA2 impact.
A Stage-2 description should be provided to allow operators to understand how these use cases can be supported through implementation. It remains to be discussed if this Stage-2 description is captured by RAN and/or SA2.
Overall assessment of RAN impact to support new use cases

## Slide 8
Since the WAB-MT uses the Uu access link, WAB can use all legacy NTN procedures and NTNTN mobility procedures for backhauling. For the same reason, WAB can leverage intra-TN DC procedures for backhauling.
Mobile multi-hop IAB can leverage Rel-16 IAB, which already support multi-hop redundant BH topologies and topology adaptation for single-donor topologies.
Aspects related to a moving gNB-DU as used by WAB for these new use cases can leverage Rel-18 mobile IAB procedures. This includes PCI collision avoidance and management of TAC broadcast, for instance.
RAN1-related aspects related to in-band operation of access and backhaul can leverage the legacy Rel-16/17 IAB framework.
Co-existence of IAB- and WAB-nodes with same/other operator network nodes can leverage requirements defined by RAN4 for Rel-16 and Rel-18 IAB.
RRM requirements for moving IAB- and WAB-nodes can also leverage requirements defined by RAN4 for Rel-16 and Rel-18 IAB.
Where the new use cases can leverage legacy procedures

## Slide 9
  RAN3 needs to study the impact the moving gNB has on inter-CU neighbor relations. This includes implications on UE mobility, SON/MDT, and other procedures.
  RAN3 needs to study RAN-related aspects in case a UPF is collocated with a moving gNB for the support of MEC, local services, etc.
  RAN3 should discuss support of authorization for backhaul operation of a moving WAB-node.
  RAN3 should discuss how in-band operation of access and BH for WAB can be supported, e.g., by leveraging inter-donor coordination defined for Rel-16/17 IAB.
  RAN3 may discuss potential enhancements to QoS for the WAB-MT’s BH PDU session.
  RAN2 may discuss enhancements to IAB robustness for single-donor deployments in presence of moving IAB-nodes.
  No impact is expected for RAN1 or RAN4.
  All RAN3-related enhancements require coordination with SA2.
Potential enhancements to be considered for new use cases

## Slide 10
Define Enhancements for the support of WAB including (RAN3-led, RAN2):
  Study impact of gNB mobility within a stationary RAN and in proximity to other mobile gNBs:
    Identify the issues of dynamic inter-gNB neighbor relations resulting from gNB mobility, e.g., ANR, inter-gNB HO/DC and SON.
    Identify RAN-related issues when collocating a UPF with the gNB for MEC, local services and/or local inter-UE communications.
    Enhance inter-gNB- and gNB-to-CN signaling to address these issues, as necessary.
  Define the signaling enhancements for the authorization of WAB nodes.
  Define signaling enhancements to extend the IAB resource multiplexing framework to WAB, as necessary.
  Define enhancements to QoS support on WAB backhaul, as necessary.
  Capture WAB solution and enhancement for WAB-node mobility on Stage 2.
Define enhancements for the support of single-donor IAB topology, including (RAN2-led, RAN3):
  Define enhancements to the robustness of multi-hop routing within the IAB topology in presence of local IAB-node mobility, e.g., such as mesh-based routing.
Coordination with other WGs
  While RAN should perform an independent effort on these topics, coordination with SA2 is necessary, especially on aspects related to BH QoS for WAB, for WAB authorization and on the Stage-2 definitions.
Candidate objectives: