## Slide 1: Views on Rel-19 Positioning
Xiaomi
3GPP TSG RAN#101
Bangalore, India, Sep 11 - 15, 2023
Agenda Item: 8A.2.12.4
Source: Xiaomi
Document for: Discussion
RP-232010

## Slide 2: Motivation
Rel-18 positioning WI includes a number of objectives, such as the sidelink positioning, carrier phase positioning, bandwidth aggregation for positioning, redcap positioning, LPHAP and RAT-dependent positioning integrity.
However, Rel-18 Sidelink positioning needs to be further enhanced, since
  It only supports the basic features;
  The Set B requirements of SL positioning/ranging accuracy can’t be satisfied;
  Power consumption reduction was not considered;
  RAN2 may down scope the SL positioning since it might not be completed on time.
Proposal:
  The Sidelink positioning enhancement should be considered in Rel-19.

## Slide 3: SL positioning enhancement
SL positioning/ranging accuracy improvement
  In Rel-18, RAN1 studied use cases and corresponding requirements and defined the Set A and Set B accuracy requirements respectively.
  The Set B requirements can’t be satisfied based on the Rel-18 SL positioning.
  The following enhancements can be considered for accuracy improvement.
    Wider bandwidth, includes unlicensed band and FR2
    Sidelink positioning method enhancement, for example, SL-CPP
  Power consumption reduction
    It is significantly important, especially for the IIoT and commercial use cases
    The following enhancements can be considered for power consumption reduction
    Partial sensing based SL resource selection for scheme 2
    The SL-DRX impact on SL positioning

## Slide 4: SL positioning enhancement
The objectives of Rel-18 sidelink positioning are dropped by RAN2
  Due to TU limitation, RAN2 may drop some objectives of SL positioning, how to reduce the objectives will be discussed at RAN#101 meeting.
  The objectives dropped by RAN2 can be included in Rel-19 positioning and the detailed objectives can be discussed after RAN#101.

## Slide 5: SL Positioning enhancement
Objectives
  SL positioning/ranging accuracy improvement
    SL positioning in unlicensed band
      Consider R18 SL communication design in unlicensed band as the baseline, and the following aspects can be considered for SL PRS transmission in unlicensed band
        The type 1 and type 2 LBT
        Multi-channel access procedure
        CP extension
        UE to UE COT sharing
        Mcst
        More than one starting symbols
        OCB requirements
        PSCCH-PSSCH/SL-PRS mapping
        Resource selection procedure
      The signaling and procedures for SL positioning in unlicensed band

## Slide 6: SL Positioning enhancement
Objectives
  SL positioning/ranging accuracy improvement
    SL positioning in FR2 spectrum
      Support beam management for SL PRS
    CPP for SL positioning
      Taking Carrier Phase Positioning (CPP) in NR positioning as the baseline, the following enhancements are considered:
        Definition of SL PRS carrier phase
        Measurement and report of SL PRS carrier phase
        Integer Ambiguity
        Phase error mitigation

## Slide 7: SL Positioning enhancement
Objectives
  Power consumption reduction for SL positioning
    Introduce partial sensing based SL resource selection for scheme 2
    Consider the SL-DRX impact on SL positioning
      Introduce SL-DRX
      SL-DRX and SL-PRS alignment
  The objectives of Rel-18 SL positioning dropped by RAN2 can be included in Rel-19 positioning
    The detailed objectives can be discussed after RAN#101 meeting.

## Slide 8: Thanks