## Slide 1
Access / Backhaul link
power control in Rel-19 NCR Enhancement
RP-232014
3GPP TSG RAN Meeting #101
Bangalore, 11th - 15th, September, 2023
Source: SK telecom
Agenda item: 8A.2.13.1

## Slide 2
Introduction
Network-controlled repeater (NCR) was proposed in Rel-18 to increase NR coverage.
  NCR is an advanced repeater from RF repeater.
  NCR includes mobile termination (NCR-MT), and gNB controls NCR through NCR-MT.
However, it was decided to exclude power control of NCR in Rel-18.
  Currently, RF repeaters in LTE networks are used by adjusting the output power based on the input signal power. Therefore, power control of NCR is essential for improved repeater performance compared to RF repeater of LTE
  Considering the scenario of deploying and operating multiple NCRs, power control is an essential technique
So, we discuss the power control of NCR to mitigate interference and optimize transmission power in Rel-19 NCR enhancement

## Slide 3
Discussion
Observation 1: Adjusting the power of the RF repeater is essential from the perspective of LTE network operation.
eNB
  RF repeaters adjust output power based on the strength of the received signal.
  This is not an operation controlled by the eNB. (the operation is not defined in the 3GPP specification)
  Power control for repeater is essential for performance optimization, and since gNB can cotrol the NCR, the performance can be improved compared to LTE repeater
To optimize performance, the RF repeater of LTE network is operated to adjust the output power based on the received signal power
RF repeater

## Slide 4
Discussion
Observation 2: To operate multiple NCRs simultaneously, NCR should be optimized through NCR power control
  Through power control signaling, transmission power of NCR's DL access link and UL backhaul link are adjusted.
  Mitigate interference among UEs in adjacent areas by adjusting the transmission power of DL access link.
  Mitigate interference among NCRs and UEs by adjusting the transmission power of UL backhaul link.
  Power control can save the NCR energy consumption by optimizing NCR transmission power based on the received signal power from NCR to gNB
gNB
NCR#1
NCR#2
Power Control
Signaling
Transmit power of NCR (DL Access link / UL backhaul link)
increases or decreases according to
power control command from gNB

## Slide 5
Discussion
Observation 3: Power control considering the channel condition both DL access link and UL backhaul link of NCR is necessary.
gNB
Power Control
Signaling
  Through power control command, transmission power of NCR's DL access link and UL backhaul link are adjusted.
  The level of power amplification required by DL access link and UL backhaul link can be different.
  Power control command that can separately adjust the power of DL access link and UL backhaul link is required.
Power control commands from gNB that increase or decrease transmit power are used separately to DL access link and UL backhaul link, respectively.
UL power adjustment
NCR#1
DL power adjustment

## Slide 6
Discussion
Observation 4: NCR power control can sufficiently improve performance even with low-complexity power control signaling.
gNB
Power Control
Signaling
  Unlike the UE power control process, NCR power control does not need to be very frequent.
  Considering the complexity of gNB operation, NCR's power control request period is set through the control link, and the gNB performs power control signaling only when the request is received. (ex. periodicity is 30min or more than 1 hour)
  For example, control signaling of power control to optimize performance is transmitted by NCR’s periodic request. After transmitting the power control request, if there is no response from the gNB, the NCR maintains the current power level.
Transmission of power control signaling from gNB is triggered by NCR’s periodic request for power control
NCR#1
Power Control
Request

## Slide 7
Conclusion
Based on the previous observations, we strongly suggest as following;
Proposal:
  NCR power control is essential to improve performance compared to RF repeater operation of LTE network.
  Interference mitigation among NCRs and transmission power optimization using power control in Rel-19 NCR enhancement.
  In addition, power control command can separately adjust the power of DL access link and UL backhaul link.
  Considering the complexity and operational efficiency of gNB, we propose power control signaling with a relatively long period unlike UE power control.

## Slide 8
Thank You.