## Slide 1
High-Power UE (HPUE)
for Rel-19 NR NTN
RP-232017
3GPP TSG RAN#101
Bangalore, 11th - 15th, Sep 2023
Source: SK telecom
Agenda item: 8A.3

## Slide 2
Introduction
In Rel-18, antenna gain of handheld UE was changed from 0 dBi to -5.5 dBi by assuming more realistic UE devices.
  Handheld UE with -5.5 dBi antenna gain may experience UL link budget deficiency issue especially for bad weather.
  At least in emergency scenarios, it is needed to consider increasing power of the handheld devices for successful communication with satellites in Rel-19.
  The coexistence analysis with terrestrial network in TR 38.863 considered PC3 (23 dBm) UE device.
  If HPUE is discussed in Rel-19, further coexistence studies should be performed accordingly.
Therefore, discussions on the handheld device power increase and corresponding coexistence studies are necessary in Rel-19.

## Slide 3
Discussion
Observation 1: With modified antenna gain of -5.5 dBi, handheld UE device may suffer from link budget deficiency.
  Link budgets calculated below are under clear sky assumption. If we assume bad weather, this issue could become more severe.
  Increasing PUSCH repetition level to greater than 20 could solve this issue, however this will cause an increase in latency.
Table 1: Link budget calculation with -5.5 dBi antenna gain based on [R1-2205826]

## Slide 4
Discussion
Observation 2: The default power class for handheld UE in Rel-18 NR NTN is Power Class 3, which has a maximum output power of 23 dBm.
Observation 3: For certain NR bands, NR UE devices are permitted to transmit with power levels exceeding +26dBm.
  The NTN system can adopt power classes already defined in the NR core specifications, such as PC1.5 (+29dBm) and PC1 (+31dBm).
Observation 4: In TR 38.863, Power Class 3 UE () is assumed in NTN UL TPC model.
    = ) where is UL transmission BW (MHz) and is the BS noise figure.
    for UL scenario
  Designing a TPC model for NTN HPUE can be discussed to secure UL link budget while preventing harmful interference with the terrestrial network.
NR satellite band | Class 3 (dBm) | Tolerance (dB)
n256 | 23 | 2
n255 | 23 | 2
NR satellite band | Class 3 (dBm) | Tolerance (dB)
n256 | 23 | 
n255 | 23 | 
Table 2: UE Power Class for NR NTN [TR38.101-5]

## Slide 5
Conclusion
Based on the previous observations, we suggest as follows;
Proposal 1: High-power UE should be discussed as a solution for NR NTN coverage enhancement at least in emergency scenarios.
Proposal 2: Further studies on NTN coexistence with terrestrial network are necessary in the presence of HPUE.

## Slide 6
Thank You.