## Slide 1: NTN PUCCH repetition for Msg4 HARQ ACK
Sources: Panasonic
3GPP TSG RAN #101
Sep 11 - 15, 2023
Agenda: 9.3.2.7
TDOC: RP-232020
For: discussion

## Slide 2: Background
For NTN PUCCH repetition for Msg4 HARQ ACK, last RAN plenary endorsed following in RP-231482
  The discussion on the followings is postponed to RAN#101 however without further discussion in RAN1#114
      whether to support repetitions for PUCCH transmission when dedicated PUCCH resource configuration is not provided
      Regarding the PUCCH transmission behavior after the transmission of HARQ ACK of PDSCH with UE contention resolution identity until the decoding of RRC message containing dedicated PUCCH resource configuration, whether to support SIB indication for the choice between "no PUCCH repetition" or "same as the PUCCH transmission of HARQ ACK of PDSCH with UE contention resolution identity"

## Slide 3: Discussion
In spite of WID says to specify PUCCH enhancements for Msg4 HARQ ACK, Msg4 is not used in the specification.
Msg4 can be 1) "PDSCH with UE contention resolution identity" (MAC Msg4) or 2) "PDSCH containing RRC message with dedicated PUCCH resource configuration" (RRC Msg4).
When RRC Msg4 is separately sent later than MAC Msg4, what PUCCH repetition should be applied until the decoding of RRC message containing dedicated PUCCH resource configuration?

## Slide 4: Discussion
As this discussion of contention based random access procedure is used when UE does not have C-RNTI, there is no other PDSCH except RRC Msg4.
As PDCCH scheduling RRC Msg4 is before the decoding of RRC message containing dedicated PUCCH resource configuration, PUCCH containing HARQ-ACK for RRC Msg4 is before to obtaining dedicated PUCCH resource configuration.
After the decoding of the RRC message in RRC Msg4, whether the repetition is applied or not can be controlled by of dedicated PUCCH resource configuration.
Therefore, the discussion is only for PUCCH for RRC Msg4.

## Slide 5: Discussion and Proposal
There is no technical motivation to have SIB indication of RRC Msg4 for the choice between "no PUCCH repetition" or "same as the PUCCH transmission of HARQ ACK of MAC Msg4". It increases SIB overhead. The same as the PUCCH transmission of HARQ ACK of MAC Msg4 is reasonable.
When Msg4 of WID description is interpreted as RRC Msg4, WID is not extended.
Proposal:
  Msg4 of WID description is interpreted as "PDSCH containing RRC message with dedicated PUCCH resource configuration".
  When dedicated PUCCH resource configuration is not available at UE, the repetition of PUCCH transmission is same as the PUCCH transmission of HARQ ACK of PDSCH with UE contention resolution identity.

## Slide 6: Discussion and Proposal
PUCCH common resource is used among 1) non-repetition case of initial access, 2) PUCCH for MAC Msg4, and 3) PUCCH for RRC Msg4.
When PUCCH repetition is used, PUCCH resource usage is increased linearly to the number of PUCCH repetition. PUCCH common resource is not sufficient.
Proposal:
  Common PUCCH repetition resource when dedicated PUCCH resource configuration is not available at UE should be separated from common PUCCH resource for non-repetition.
  This can be handled as essential correction. No RAN decision may be required.