## Slide 1: Views on Rel-19 RAN scope
Source: Panasonic
RP-232042

## Slide 2: Rel-19 timeline and Load Management
One dedicated quarter for maintenance is useful for the timely agreement at the end of release according to the experience of 2023.
Proposal: One dedicated quarter for maintenance should be allocated before or after 18 month.
R18 RAN1
R18 RAN2/3/4
R18 RAN1
Func
. Freeze
R18 RAN2/3/4
Func
. Freeze
First R18
ASN.1
review
R18 RAN1
Maint
R18 RAN2/3/4
Maint
R19 RAN1
Func
. Freeze
R19 Pkg
(RAN4)
2023
Q1
Q2
Q3
Q4
2024
Q1
Q2
Q3
Q4
R19 Pkg
(RAN1/2/3)
R18 ASN.1
Freeze
2025
Q1
Q2
Q3
Q4
R19 RAN2/3/4
R19 RAN1
R19 RAN2/3/4
Func
. Freeze
R19
ASN.1
Freeze

## Slide 3: AI/ML Air Interface
Functionality-based LCM and model-ID-based LCM were discussed.
Functionality-based LCM reuses existing functionalities and relatively more feasible.
  Assistance information handling is to be discussed in coming quarter further.
Model-ID-based LCM has a lot of potential to improve the overall system performance, but it requires more study on the feasibility. Two-sided model would require model-ID-based LCM.
Model deliver/transfer also has a lot of potential to improve the overall system performance, but it requires more study on the feasibility.
Proposal
  One work item for Functionality-based LCM without model delivery/transfer.
    One use case of UE one-side model should be selected e.g. CSI prediction.
  One study item for Model-ID-based LCM with the capability of model delivery/transfer.

## Slide 4: Duplex Evolution
Normative work on SBFD should be supported.
  In addition to semi-static SBFD, dynamic SBFD with time domain information should be supported for the adaptation of the traffic load.

## Slide 5: Ambient IoT
A WG-level study item should be supported.
  Evaluation methodology including traffic models, power models, and device types.
  Waveform for ambient IoT and its coexistence with NR waveform
  Time and frequency domain resource management and multiplexing for different behavior/function.

## Slide 6: Network Energy Saving Enhancements
Cell DRX/DTX is informed from adjustment cells. These cells can be another frequency or neighbor cells
  On demand SSB, CSI-RS and/or SIBs while considering backward compatibility
  Interaction with LTM (L1L2-triggered mobility) enhancement

## Slide 7: Mobility Enhancements
Further enhance mobility management in Rel-19, inter-CU (central unit) LTM.

## Slide 8: NTN Evolution
RAN3 leaded work item on Regenerative satellite including inter-satellite link.
Enhanced usage of circular polarization
  More flexible polarization indication (e.g. per beam, per UE, per layer) for interference mitigation and/or MIMO.

## Slide 9: Low-power Wake-Up Signal (LP-WUS)/Wake-Up Radio (WUR)
Prefer to have work item.
Some more evaluation/discussion is required to determine OFDMA waveform and OOK waveform before the specification.
If LP-WUR that cannot receive existing PSS/SSS, periodic LP-SS signal should be supported.

## Slide 10: Coverage Enhancements
Work item of the limited scope like a few small objectives.
  multiple PRACH transmissions with different beams
  Enable joint channel estimation for multiple TBs scheduled by a single DCI
  DMRS-less PUCCH
  Waveform switching for Msg3

## Slide 11: SL evolution
Work item of the limited scope:
  URLLC/Industrial IoT
  RedCap