## Slide 1: UAV/UAM Enhancement for Rel-19

## Slide 2: Enhancement direction
Type of aerial UEs for Rel-19 enhancements
  Uncrewed Aerial Vehicle (UAV) UEs are baseline, as targeted in Rel-18.
  Advanced Air Mobility (AAM) UEs can be also considered for Rel-19 and beyond.
    AAM includes both intra-urban air mobility (UAM) and inter-urban air mobility.
    Normal passenger UEs can be onboard inside an AAM aerial UE.
      The presence of passenger UEs inside AAM aerial UE imposes more stringent requirements on connectivity robustness and link performance over radio interface, compared to UAM aerial UEs.
    Note: Pilot AAM services are under preparation in Korea.
Proposed enhancement areas and considerations
  Enhanced measurement and mobility for UAV/UAM
  Access restriction and control of mobility/radio resource usage to fulfill No-Transmit-Zone (NTZ) requirements .
  Sidelink related considerations
  General enhancements for AAM UE support
   Detailed scope of each area is discussed in the following slides

## Slide 3: Scope for Mobility and Measurements
Motivation
  In R18, height-dependent RS sets are introduced to cope with vertically changing radio environments in RRC_CONNECTED. The similar should be done for measurements in RRC_IDLE/INACTIVE.
  Suitable or intended mobility candidates can be different for different heights and locations. Mobility candidate down-selection mechanism based on UE height/location is beneficial.
  Frequent mobility events or ping-pong may happen due to highly dynamic channel environments experienced by flying UEs. Suppression of unnecessary mobility needs to be avoided.
  The Rel-18 enhancement of measurement report was intended to reduce too frequent measurement report triggering under a large number of LOS neighbor cells by introducing the number of triggering cells as measurement report triggering condition. The triggering based on the number of triggering cell may however suppress some important reporting about interference status change.
Proposed enhancements
  Measurement enhancement
    Measurement RS selection based on height for RRC_IDLE/INACTIVE
    Enhancement of measurement reporting procedure to enable best trade-off between timely reporting of radio measurements (including interference) and reasonable RRC signaling overhead
  Mobility enhancement
    Mobility candidate down-selection mechanism based on UE height/location
      Conditional mobility for RRC_CONNECTED and cell reselection for RRC_IDLE and RRC_INACTIVE
    Suppression of frequent mobility events or ping-pong in RRC_CONNECTED
      Time-of-stay and/or priority of target/candidate cells can be considered for mobility execution.

## Slide 4: Scope for No-Transmit Zone
Motivation
  CEPT Decision 22(07) requires UAV UEs to fulfill requirements related to NTZ.
  RAN agreed in RP#100 that the NTZ requirements should be addressed, and asked SA2 whether and how to address the requirements. SA2 responded with reply LS in [1] that they have no plan to do work on NTZ in Rel-18.
  But SA2 stressed out that they consider normative work on NTZ in Rel-19 from system perspective. Being inline with SA2 work, RAN WGs need to start work on NTZ.
Potential assumptions for NTZ related work
  NTZ may span a partial area of a cell coverage or a full cell coverage
  NTZ information can be provisioned to RAN and/or UE.
  Note: The assumptions can be clarified and/or updated as SA2 work in Rel-19 are progressed.
Proposed enhancements
  Access barring mechanism to block access UEs in NTZ
  Enhanced control of mobility and/or radio resources to enable UE to avoid service interruption/degradation due to NTZ
    Mobility control (handover/cell reselection) upon entering/leaving NTZ
    Resource control (BWP/SCell/SCG management) upon entering/leaving NTZ
    NTZ related status information exchange/update between UE and RAN
      Both UE sided information (UE to NW) and NW sided information (NW to UE) can be considered.

## Slide 5: Sidelink Aspects
On necessity of enhancements on cyclic shift detection of RS
  Wireless channel for aerial UEs has much higher LOS probability, which results in a longer propagation delay. This can cause a confusion in detecting the cyclic shifts of a reference signal as mentioned by, e.g., [2].
  While this is a valid observation in using sidelink for aerial UEs, the necessity of specification update requires more consideration:
    PSCCH aspects:
      We first note that cyclic shift random selection for PSCCH DM RS is used in LTE sidelink, not in NR sidelink. In NR sidelink, the orthogonal cover code is randomly selected for PSCCH DM RS.
      When the cyclic shift confusion happens in PSCCH, no immediate issue is seen because the cyclic shift information is not further used in the consequent sidelink operations. As far as the RX UEs successfully decode PSCCH and CRC check is passed, there would be no problem in considering the decoded SCI valid.
      Sometimes, PSCCH DM RS with a cyclic shift can collide with another PSCCH DM RS with a different cyclic shift after a long propagation delay, but this is not different from conventional PSCCH DM RS cyclic shift collision which cannot be completely avoided in random selection.
    PSFCH aspects:
      Confusion in detecting the cyclic shift used in PSFCH can cause a serious problem because this means that the PSCCH/PSSCH TX UE can misunderstand the sidelink HARQ feedback and therefore sends unnecessary retransmissions or terminates a HARQ process not successful yet.
      However, the number of cyclic shifts used for PSFCH is already (pre-)configurable per resource pool in Rel-16. Thus, if the aerial UEs operate sidelink in a pool separated from other UEs, the existing parameter can be (pre-)configured based on the channel characteristics. If RAN identifies a need to operate aerial UEs in the same resource pool shared with other UEs, an enhancement needs to be considered in order to separate PSFCH resources for aerial UEs from the existing ones.

## Slide 6: General Enhancement for AAM support
Motivation
  Until Rel-18, UAV UEs are considered as aerial UEs.
  To support AAM aerial UEs,
    Mechanisms to identify AAM UEs are needed.
    RF requirements related to AAM operating frequency bands need to be defined.
    Enhanced UE assistance information should be considered
      E.g. additional information beyond a set of way points based on AIML capabilities, more controlled reporting of flight path information, on-flight requirements
Scope
  Mechanism for identification of AAM UEs
    Subscription based AAM UE identification
    NR support for AAM over Xn
    UE capabilities specific to AAM
  NS values specific to AAM UEs
  Enhanced flight path information reporting
    Additional information to enable proactive mobility and resources planning
      E.g., Predictive QoS requirements, flight path requirement, etc.
    Note: This enhancement can be applicable to UAV UEs as well.

## Slide 7: Summary of Proposals
Proposed Uu enhancements for aerial UEs
  Measurement enhancements
    Measurement RS selection based on height for RRC_IDLE/INACTIVE.
    Enhancement of measurement reporting procedure to enable best trade-off between timely reporting of radio measurements (including interference) and reasonable RRC signaling overhead.
  Mobility enhancements
    Mobility candidate down-selection mechanism based on UE height/location for conditional mobility and cell reselection.
    Suppression of frequent mobility events or ping-pong in RRC_CONNECTED based on e.g., considering time-of-stay and/or priority of target/candidate cells for mobility execution.
  NTZ related enhancements
    Access barring mechanism to block access UEs in NTZ
    Enhanced control of mobility and/or radio resources to enable UE to avoid service interruption/degradation due to NTZ
      Mobility control (handover/cell reselection) upon entering/leaving NTZ
      Resource control (BWP/SCell/SCG management upon entering/leaving NTZ)
      NTZ related status information exchange/update between UEs and RAN (both UE sided information (UE to NW) and NW sided information (NW to UE) can be considered)
For sidelink aspects,
  RAN needs to decide whether it is a valid scenario to operate aerial UEs in the same resource pool shared with other sidelink UEs.
  If this scenario is deemed valid, RAN needs to consider an enhancement to separate PSFCH resources for aerial UEs from the existing ones.

## Slide 8: Reference
[1] RP-231529, “Reply LS to RP-231485 on support of no-transmit zones for UAVs”
[2] RWS-230185, “UAVs,” Qualcomm Incorporated.