## Slide 1: Proposal on Layer 2 Overhead Reduction in Rel-19

## Slide 2: Motivation for Layer 2 header overhead
  L2 header is always attached to each packet.
    2~5 bytes in MAC
    1~5 bytes in RLC
    1~5 bytes in PDCP
  L2 header overhead problem is more severe for small packet transmission, e.g. VoIP over NTN, IIoT application, pose control in XR, etc.
    Supporting VoIP is important but companies identified that current L2 header design is inappropriate to support VoIP, particularly, over NTN.
      20byte of VoIP packet transmission over long propagation RTT with repetition causes unnecessary high header overhead.
    More new applications requiring small packet transmission are considered such as IIoT applications, pose control in XR, etc.
  It is necessary to study L2 header overhead reduction to increase efficiency of resource utilization.

## Slide 3: Proposed work for Layer 2 header overhead
  RLC header overhead reduction
    Data transmission via TM RLC
      In the current specification, TM RLC is used only for special RRC signaling, and RBs using TM RLC do not use PDCP.
      TM RLC attaches no RLC header. Thus, it is obvious that using TM RLC for data transmission is beneficial for header overhead reduction.
      Support of a DRB having TM RLC and PDCP needs to be considered.
  MAC header overhead reduction
    Header-less MAC subPDU transmission based on enhanced scheduling
      LCH and size of each MAC subPDU are determined during UE uplink scheduling in the current specification.
      If LCH and size of each MAC subPDU can be pre-determined or scheduled along with uplink grant, MAC subheader may not be necessary or can be removed.
    Partial subheader MAC subPDU based on LCH restriction
      In NR, due to LCH restriction in MAC, the network is able to restrict use of uplink configured grant to a certain logical channel, where LCID field in the MAC subPDU may not be necessary or can be removed.

## Slide 4: Motivation for Layer 2 processing overhead
  In NR, UPIP (User Plane Integrity Protection) is introduced to enhance security protection of user plane data against increasing potential security attack.
  It is required to support UPIP for full data rate, but the processing burden is too high at high data rate.
    UE needs to perform UPIP for whole data of a packet.
    The processing load increases as UE peak data rate keeps increasing in upcoming release of NR.
  As more applications require higher peak data rate than now, UPIP processing burden problem should be more serious in near future.
    UPIP needs to be applied at high data rate within UE’s processing power.
  It is necessary to study low burden UPIP while not jeopardizing security concerns.

## Slide 5: Proposed work for Layer 2 processing overhead
  Mechanism to perform UPIP within UE’s processing power.
    UPIP should be enhanced to be applied to part of data stream when UE’s processing power is expected to be exceeded.
      Applying UPIP to selective packets
      Applying UPIP to a part of each packet

## Slide 6: Objectives
  Specify mechanisms to reduce L2 header overhead
    Data transmission via TM RLC.
    Header-less/partial subheader MAC subPDU.
  Support partial UPIP
    Applying UPIP to selective packets or a part of each packet.