## Slide 1: Consideration on AI/ML for air interface
CATT
3GPP TSG RAN Meeting #101 RP-232051
Bangalore, India, September 11-15, 2023

## Slide 2: General consideration
Continuous evolution
vs
Standardization need
Normative interest
vs
Manageable workload
Tentative start
vs
Fancy mechanism
Rel-19 is a suitable release to provide specification support to AI/ML in air interface – a WI is desired
Keep seeking promising new use case for future – a parallel SI can be considered
As a brand new feature, AI/ML may face unseen issues during normative phase
Rel-19 scope should be carefully restricted to ensure a reasonable workload
A simpler and practical start in first release is more important than a fancy but uncertain start
Targeting at 6G, those not in Rel-19 WI scope can be further studied. It does not mean a waste of effort

## Slide 3: Rel-18 progress
SI Progress until 2023Q3
  RAN1 achieved ~85% completion in RAN1#114
    Extension on some agendas (e.g. general aspects of framework, CSI feedback enhancement) may be needed in 2023Q4.
  RAN2 study and RAN4 study are on-going
    Recent progress from RAN2 and RAN4 is not quite optimistic. But still possible to wrap up the study by well taking opportunity of the 2 meetings in 2023Q4.
For Rel-18 AI/ML PHY study, main achievements can be summarized as follows
  Achieve common understanding on fundamental concepts like terminology and collaboration levels.
  Build up the general framework on life cycle management (LCM) of AI/ML-based approaches, including both model-ID-based LCM and functionality-based LCM.
  Identify 6 sub use cases in total, and evaluate performance gain and analyze potential specification impact.
  Investigate the interoperability and testability (RAN4).
Proposal 1: Support WI of AI/ML for air interface in Rel-19 RAN.

## Slide 4: Rel-19 WI – sub use case
Outcome of sub use case study
Proposal 2: For sub use cases selection in Rel-19 WI of AI/ML for air interface:
  1st priority: CSI prediction, spatial-domain beam prediction, direct AI/ML positioning, AI/ML assisted positioning.
  2nd priority: Time-domain beam prediction.
  Premature: CSI compression (need further study at least for RAN4).
Use case | Sub use case | LCM procedure complexity/difficulty |  | Performance gain | Spec impact
 |  | Model training | Data collection |  | 
CSI feedback enhancement | CSI compression | High | Low | Low ~ medium | High*
 | CSI prediction | Low | Low | Low ~ medium | Low
Beam management | Spatial-domain beam prediction | Low | Low | Medium ~ high in intermediate KPI Lack of eventual KPI evaluation | Low ~ medium
 | Time-domain beam prediction | Low | Low | Low ~ high in intermediate KPI (divergent) Lack of eventual KPI evaluation | Low ~ Medium
Positioning accuracy enhancement | Direct AI/ML positioning | Low | Low ~ Medium | High in NLOS, low in LOS | Low
 | AI/ML assisted positioning | Low | Low ~ Medium | High in NLOS, low in LOS | Low
*Note: CSI compression additionally brings new challenges to RAN4 due to two-sided mode testing.

## Slide 5: Rel-19 WI – life cycle management
Functionality-based LCM
  Relatively simple - largely follows legacy UE capability/feature framework
  Good balance between complexity and flexibility
    NW controls the LCM in functionality level
    UE controls the LCM of AI/ML model(s) within a functionality transparently
Model-ID-based LCM
  Aggressive change on top of legacy UE capability/feature framework
    E.g. model identification, global model ID, model transfer (z1 ~ z5) …
  Unclear whether it is really better for NW to make LCM decision for UE-sided model rather than UE makes decision
  Non-negligible offline engineering is required, e.g. model identification Type A, model storage, etc.
Proposal 3: For LCM in Rel-19 WI of AI/ML for air interface, at least functionality-based LCM is supported.
  Model-ID-based LCM can be further studied (e.g. model identification, model transfer).

## Slide 6: Rel-19 SI
Rel-18 RAN1/RAN2/RAN4 leftover (if any)
  E.g. CSI compression, Model-ID-based LCM aspects, RAN4 test of two-sided model. Depending on the outcome in 2023Q4.
RAN2 new use case: UE mobility management
Proposal 4: Additionally support SI of AI/ML for air interface in Rel-19 RAN, including :
  Rel-18 RAN1/RAN2/RAN4 leftover, if any.
  RAN2-led new use case: UE mobility management.
    Sub use cases may include: Handover decision optimization, RLF prediction/avoidance, dynamic parameter tuning.
AI/ML based mobility should also be under network control, but UE is allowed to send adjustment suggestions (e.g. obtained from AI/ML) to network
Guidance and principle
Handover decision optimization
  RRM (e.g. RSRP) prediction
  CHO/HO/target cell prediction
  Time prediction (TTT, exact HO time point)
RLF prediction/avoidance
Dynamic parameter tuning
Potential sub use case/directions

## Slide 7: Conclusion
Proposal 1: Support WI of AI/ML for air interface in Rel-19 RAN.
Proposal 2: For sub use cases selection in Rel-19 WI of AI/ML for air interface:
  1st priority: CSI prediction, spatial-domain beam prediction, direct AI/ML positioning, AI/ML assisted positioning.
  2nd priority: Time-domain beam prediction.
  Premature: CSI compression (need further study at least for RAN4).
Proposal 3: For LCM in Rel-19 WI of AI/ML for air interface, at least functionality-based LCM is supported.
  Model-ID-based LCM can be further studied (e.g. model identification, model transfer).
Proposal 4: Additionally support SI of AI/ML for air interface in Rel-19 RAN, including:
  Rel-18 RAN1/RAN2/RAN4 leftover, if any.
  RAN2-led new use case: UE mobility management.
    Sub use cases may include: Handover decision optimization, RLF prediction/avoidance, dynamic parameter tuning.