## Slide 1: Consideration on channel modeling
CATT
3GPP TSG RAN Meeting #101 RP-232052
Bangalore, India, September 11-15, 2023

## Slide 2: ISAC

## Slide 3: Background
ITU formally stated ISAC as one of the six key usage scenarios in 6G
ISAC has been heatedly discussed in Rel-19 RAN WorkShop
  More than 20 contributions discussed on ISAC in Rel-19 RAN WorkShop in Taipei, June, 2023
  Chair’s assessment on channel modelling (RWS-230448):
Channel Modeling (& possibly additional aspects e.g. for ISAC) for further evolution
Strong interest in exploring study in new areas (RAN plenary invovlement?)
  Very strong interest in channel modeling for integrated sensing and communication (ISAC), and also interest in other possible areas (e.g., use cases, scenarios, key performance metrics (KPIs), potential spec impact, etc.)
  Reasonable interest in exploring study in new spectrum, such as 7-24GHz
    Channel modeling study only?
  Reasonable interest in RIS (Reconfigurable Intelligent Surface) related study
    Channel modeling study only?
Very challenging if study is to be carried out for all the above items
  Which one(s) should be the focus? Necessity for future standard evolution?

## Slide 4: General Consideration
General consideration on ISAC
  1st priority
    Use case identification – guidance for ISAC study, e.g. frequency band, KPIs, sensing mode, etc.
    Channel modeling – fundamental work for evaluation, not only for 5G-Advanced but also for 6G
  2nd priority
    Metrics & evaluation methodology
    Evaluations for each identified use case
    Architectures and procedures in RAN1/RAN2
    Architectures and procedures in RAN3
    Feasibility and test requirements in RAN4
Proposal 1: Rel-19 RAN includes ISAC topic. At least include channel modeling for ISAC study.
Nice-to-have in Rel-19
May be studied in Rel-20 or even Rel-20+

## Slide 5: Use case
Interested use cases based on TR 22.837
Proposal 2: For ISAC study, at least include one indoor and one outdoor use case as starting point.
  Use case identification can be done in RAN1, or in RANP if necessary.
 | Intelligent transportation | Smart factory | Public regulation and safety | Smart home
Examples of sensing functionality | Generation of dynamic 3D map, automatic driving, vehicle or pedestrian tracking | AGV (automated guided vehicles) detection and tracking, Autonomous mobile robots (AMR) collision avoidance | UAV intrusion detection, railway intrusion detection | Health care, gesture recognition, intruder detection
Requirement of sensing accuracy | Medium ~ High | High | Low ~ Medium | Low ~ High
Object-oriented or area-oriented | Object-oriented, Area-oriented | Object-oriented, Area-oriented | Object-oriented, Area-oriented | Object-oriented
Indoor or outdoor | Outdoor | Indoor | Outdoor | Indoor
Frequency band | FFS |  |  | 

## Slide 6: Channel modeling
LLS channel modeling enhancement
  Concatenation-based modeling: separately model channel of:
    Parameters of Tx-Target link
    Parameters of Target-Rx link
    Parameters of Tx-Rx link without sensing target
  Non-concatenation-based modeling
    Replace one CDL path/cluster by sensing target path/cluster
    Select part of CDL path/cluster as path/cluster related to sensing target
    Other paths/clusters are considered as interference
  Proposal 3: Study ISAC channel modeling enhancement for both SLS and LLS based on statistic modeling in TR 38.901.
SLS channel modeling enhancement
Step 1: Set environment, network layout, etc.
Step 2: Assign propagation condition LOS/NLOS
Step 3: Calculate pathloss for each sensing link
Step 4: Generate large scale parameters
Step 5: Generate cluster delays
Step 6: Generate cluster powers
Step 7: Generate arrival and departure angles
Step 8: Coupling of rays within a cluster
Step 9: Generate the cross polarization power ratios
Step 10: Draw initial random phases
Step 11: Generate channel coefficients
Step 12: Apply pathloss and shadowing
Need sensing-specific enhancement
Scenario
Large scale related
Small scale related
Co-efficient generation

## Slide 7: Sensing mode
Initial views on sensing mode
Proposal 4: Channel modeling for all sensing modes can be studied.
(a) gNB mono-static
(b) gNB-to-gNB bi-static
(c) gNB-to-UE bi-static
(d) UE-to-gNB bi-static
(e) UE mono-static
(f) UE-to-UE bi-static
Higher priority
Need clarification
Obvious advantages are expected
gNB as transmitter
  Higher transmission power
gNB as receiver
  Higher spatial resolution by massive antenna
  Higher computation power
  Naturally supports inter-node cooperation
UE mono-static:
  Possible for vehicle UE?
UE-to-UE bi-static
  Possible in limited scenarios, e.g. smart home?

## Slide 8: RIS

## Slide 9: Background
Cui T J , Qi M Q , Wan X , et al. Coding metamaterials, digital metamaterials and programmable metamaterials[J]. Light Science & Applications, 2014, 3(10):e218.
Reconfigurable intelligent surface (RIS) has attracted much attention due to its low cost and energy consumption, small volume, light weight, programmability, and ease of deployment
RIS can be deployed as reflective panels to reflect signals
Deployment of RIS can expand the coverage of each cell to avoid frequent cell handovers and overcome shadowing effects
With RIS, expected spatial propagation characteristics can be deliberately constructed, and the degrees of freedom of wireless channels can be effectively improved
RIS relay

## Slide 10: General consideration
Proposal 5: RIS, if studied in Rel-19, can focus on channel modeling as 1st priority.
  2nd priority aspects can be studied in future release, e.g. power consumption modeling.
1st priority aspects for channel modeling
  Scenario models
    Indoor, outdoor, O2I, etc.
    LoS/NLoS
    Far field, near field
  Array models
    Modeling of different RIS structures
    Modeling of radiation patterns
  Considered links
    BS-RIS, RIS-UE, BS-UE
  Methodologies
    Geometry-based stochastic models
    Map-based/ ray-tracing
    Hybrid models
2nd priority aspects in air interface
  Power consumption modeling
  Access/backhaul links
  Synchronization & broadcasting
  Beam management for BS-RIS/RIS-UE/BS-UE links
  CSI enhancement
  Inter-cell interference mitigation
  Coordination transmission/reception based on RIS

## Slide 11: RIS applications – need to be more concentrated
Proposal 6: RIS channel modeling, if studied in Rel-19, should consider how to limit the workload.
  Strive to one most representative RIS element model, e.g. 1-bit passive RIS element.
  Start with a few popular array patterns (array size, element spacing, polarization, etc.).
Localized massive MIMO based on RIS
Distributed massive MIMO based on RIS

## Slide 12: Channel modeling (1/2)
Map-based ray-tracing?
Tx correlation
Rx correlation
Correlation-based?
Geometry-based stochastic?

## Slide 13: Channel modeling (2/2)
  Stage 1：Without element-level modeling of RIS
  Modeling of the composited channel with RIS
  Typical deployment scenarios
    RIS deployed close to BS (e.g. Tx array)
    RIS deployed close to UE (e.g. Rx array)
    RIS deployed in the middle of BS-UE link (e.g. relay)
  Stage 2: With element-level modeling of RIS
  Radiation pattern of RIS element is modeled
  Only stationary far field modeling is considered
  Stage 3: Complete modeling of RIS
  Radiation pattern of RIS element is modeled
  Stationary/non-stationary far/near field modeling
Geometry-based stochastic modeling
Proposal 7: RIS channel modeling, if studied in Rel-19, should start with geometry-based stochastic modeling as in TR 38.901.

## Slide 14: Conclusion - ISAC
Proposal 1: Rel-19 RAN includes ISAC topic. At least include channel modeling for ISAC study.
Proposal 2: For ISAC study, at least include one indoor and one outdoor use case as starting point.
  Use case identification can be done in RAN1, or in RANP if necessary.
  Proposal 3: Study ISAC channel modeling enhancement for both SLS and LLS based on statistic modeling in TR 38.901.
  Proposal 4: Channel modeling for all sensing modes can be studied.

## Slide 15: Conclusion - RIS
Proposal 5: RIS, if studied in Rel-19, can focus on channel modeling as 1st priority.
  2nd priority aspects can be studied in future release, e.g. power consumption modeling.
Proposal 6: RIS channel modeling, if studied in Rel-19, should consider how to limit the workload.
  Strive to one most representative RIS element model, e.g. 1-bit passive RIS element.
  Start with a few popular array patterns (array size, element spacing, polarization, etc.).
Proposal 7: RIS channel modeling, if studied in Rel-19, should start with geometry-based stochastic modeling as in TR 38.901.