## Slide 1: On the scope of R19 mobility enhancements
CATT
3GPP TSG RAN Meeting #101 RP-232053
Bangalore, India, September 11-15, 2023

## Slide 2: Outline
Inter-CU LTM
  RAN2 related enhancements
  RAN3 related enhancements
Conditional LTM
  RAN2 related enhancements
PHY related enhancements for LTM

## Slide 3: Inter-CU LTM – RAN2 impact
Motivations:
  Enable LTM for inter-CU handover case to achieve lower latency of cell switch and beam switch
Observations for RAN2:
  Observation 1: Reusing intra-CU LTM mechanism for inter-CU case (e.g., early TA/RACH-less, Cell switch command MAC CE for simultaneous cell switch and beam switch) is with minor RAN2 spec impact.
  Observation 2: The RAN2 workload depends on whether to support dynamic switch among multiple candidate cells without RRC reconfiguration for inter-CU LTM.
    Key issue is how to handle security key synchronization between network and UE for subsequent cell switch without RRC reconfiguration.
    It might be horizontal key derivation or vertical key derivation, and KAMF may also be changed with the value of keySetChangeIndicator field set to true.
    The inter-CU LTM case may need to be further divided into inter-CU-CP LTM and inter-CU-UP LTM.
Proposals:
  Proposal 1: Inter-CU LTM is supported in R19. [RAN2, RAN3]
  Proposal 2: Further discuss whether to support dynamic switch among multiple candidate cells for inter-CU LTM.

## Slide 4: Inter-CU LTM – RAN3 impact
Observations for RAN3:
  Observation 3: XnAP enhancements are necessary to support inter-CU LTM.
  Observation 4: Inter-CU LTM procedure with NG interface interaction is with larger latency.
Proposals:
  Proposal 3: XnAP enhancements for Inter-CU LTM are supported in R19. [RAN3]
Procedure | Handling in Legacy L3 HO | Handling in Intra-CU LTM | RAN3 enhancements for Inter-CU/inter-gNB LTM
HO preparation | Candidate cell preparation | Maintenance for multiple intra-CU candidate cells | Support LTM candidate cell configuration procedure in Xn interface, L3 HO preparation procedure may be reused for pre-configuration
HO execution | RACH based | Early TA/RACH-less | RACH resource transfer (from candidate DU to source DU) in Xn interface TA value maintenance and update mechanism Multiple TA values maintenance for subsequent LTM
HO Decision | HO request procedure triggered by CU | Cell switch notification (s-DU -> T-DU) | Source node informs target node via Xn interface
HO Notification | CU is aware via RRC message | Access success from T-DU to CU | Access success information transfer via Xn interface.

## Slide 5: Conditional LTM
Motivations:
  Improved robustness, i.e., cell switch command MAC CE may be missed by UE.
  Less L1 measurement reporting, i.e., for candidate cells.
Issues to address:
  How to acquire early TA?
    If TA is calculated by network, TA has to be indicated to UE before cell switch. So RAR based solutions are needed, which might be more complicated than R18 approach (without RAR).
    Whether TA can be calculated by UE itself and what the solutions look like may not be resolved in R18 mobility enhancements WI.
  How to inform target of the access when RACH-less is applied?
    In case of dynamic UL-Grant, if we follow R18 design, i.e., “the source DU informs the target DU about the selected beam”, UE has to report selected beam to source DU first.
    In case of configured Grant, more resources have to be wasted as target DU has to allocate them much earlier.
  Execution condition to trigger conditional LTM?
    Whether new filtering mechanism for measurement results in MAC layer is needed?
Proposals:
  Proposal 4: conditional LTM is supported in R19. [RAN2]

## Slide 6: PHY related enhancements for LTM
Motivations:
  Further PHY measurement enhancements for LTM as performance optimization are needed.
Potential PHY measurement enhancements include:
  CSI-RS for inter-cell measurement and corresponding L1 measurement report
    Possible gain: enabling narrow beams and appropriate MCS for data communication ASAP
  Dynamic update L1 measurements of candidate cell/beam, or a subset of candidate cells for L1 measurements
    Possible gain: To support subsequent cell switch scenario and saving UE energy consumption
  Measurement filtering operation, e.g. in time domain or spatial domain
    Possible gain: to mitigate ping-pong issue
Proposals:
  Proposal 5: Further PHY measurement enhancements for LTM are supported in R19 [RAN1], e.g.,
    CSI-RS for inter-cell measurement and corresponding L1 measurement report
    Dynamic update of L1 measurements of candidate cells, or a subset of candidate cells for L1 measurements
    Measurement filtering operation, e.g. in time domain or spatial domain

## Slide 7: Summary
Proposals:
  Proposal 1: Inter-CU LTM is supported in R19. [RAN2, RAN3]
  Proposal 2: Further discuss whether to support dynamic switch among multiple candidate cells for inter-CU LTM.
  Proposal 3: XnAP enhancements for Inter-CU LTM are supported in R19. [RAN3]
  Proposal 4: conditional LTM is supported in R19. [RAN2]
  Proposal 5: Further PHY measurement enhancements for LTM are supported in R19 [RAN1], e.g.,
    CSI-RS for inter-cell measurement and corresponding L1 measurement report
    Dynamic update of L1 measurements of candidate cells, or a subset of candidate cells for L1 measurements
    Measurement filtering operation, e.g. in time domain or spatial domain