## Slide 1: Consideration on NTN evolution
CATT
3GPP TSG RAN Meeting #101 RP-232055
Bangalore, India, September 11-15, 2023

## Slide 2: Outline
  NR NTN
  Support of Regenerative Payload
  Support of MBS
  DL Coverage Enhancement
  Support of High TX power UE
  Support of bandwidth lower than 5MHz for FR1
  NTN Positioning
IoT NTN
  Support of 5GC Connection
  Support of Regenerative Payload
  Support of Store & Forward (S&F)

## Slide 3: NR NTN Evolution
Support of Regenerative Payload [RAN3, RAN2]
  Motivation: Regenerative Payload could make radio resource handling and coordination between gNBs more efficiently (e.g. via the ISL), and it could make the deployment more flexible.
  Assumptions:
    Both GSO and NGSO are supported.
    With/without ISL are considered. ISL could be treated as a transport link and no specification work is expected.
    UPF on board could be supported without any extra RAN impact.
  Proposal:
    Support Regenerative payload, full gNB on satellite should be focused on, other architecture options, e.g. gNB-DU on board, IAB like options should be down-prioritized.
    Specify the support of gNB on board in TS 38.300 and define if needed, some enhancements related to NG protocol to address feeder link switch over issue.
  Full gNB on satellite, with ISL

## Slide 4: NR NTN Evolution Cont.
Support of MBS [RAN2, RAN3]
  Motivation: Support of Broadcasting services (e.g. public safety services, multimedia services) in NTN could win greater commercial success. Which makes full use of the characteristics of satellite coverage, and make better use of the satellite resources.
  Proposal: Support both broadcast and Multi-cast in NR NTN.
Identify and specify the potential enhancements on MBS service area management.
  Potential mismatch between the MBS service area and the NTN radio cell coverage should be clarified, e.g. whether the MBS service area could be smaller than a NTN radio cell.
Identify and specify MBS specific UP enhancement with adaptation to “gNB-UE” RTT (e.g. L2 timer enhancements with RTT handling).
Identify and specify MBS specific CP procedure enhancements in NTN (e.g. mobility enhancements, service continuity w.r.t. satellite motion).
  Support MBS over NTN

## Slide 5: NR NTN Evolution Cont.
DL Coverage Enhancement [RAN1, RAN2]
  Motivation: Total TX power is limited within one satellite, so it will restrict the number of active beams and TX power of single beam. Finally it will impact the DL SINR and beam coverage. Hence, improving DL coverage is very necessary and should take into account active beam number, SINR range and power efficiency of control beam. Currently the SSB index in FR1 and SSB transmission period have restricted real deployment of satellite network.
  Proposal:
    Evaluate required SINR target under realistic active beams and total TX power limitation in SI phase.
      Target is to guarantee similar detection performance for all physical channels.
    Extend transmitting period of SSB and system information to reduce power consumption.
    Extend SSB index to improve DL coverage of single physical beam for FR1.
Total spot beam zones within one satellite | Physical beam number in active state | Configured SSB index of each beam | Coverage ratio
1024 | 8 | 64 | 512/1024=50% ( to be in R19)
1024 | 8 | 8 | 64/1024=6.25% (R17 supported)

## Slide 6: NR NTN Evolution Cont.
Support of Higher TX power UE [RAN4]
  Motivation: Satellite access has limited link budget, which is more challenging for mobile phone. Increasing the TX power is one direct and efficient way to improve UL performance. Relevant studies had been discussed in RAN4.
  Proposal: Support higher TX power UE in NR NTN.
    Support +26dBm for FR1 NTN UE
    Support more than +26dBm for non smart phone UE.
Support of bandwidth lower than 5MHz for FR1 [RAN4]
  Motivation: The spectrum resource to be used for NTN is limited in the FR1 bands, and the support of bandwidth lower than 5MHz could make NTN deployment more flexible.
  Proposal: Specify support for UE channel bandwidth less than 5 MHz for NR NTN FR1 bands.
    Output of Rel-18 WID “NR support for dedicated spectrum less than 5 MHz for FR1” could be taken as baseline.
    Identify and specify the RF requirements on supporting of the bandwidth less than 5MHz.

## Slide 7: NR NTN Evolution Cont.
  NTN Positioning [RAN1, RAN2, RAN3]
  Motivation: In Rel-17 and Rel-18, NR NTN operation is relied on the GNSS capability of the UE. In SA1 Rel-19 study item “Study on satellite access – Phase 3”, some use cases related to positioning are raised, refer to TR 22.865. Just like the terrestrial network, it’s really important to make NR NTN system work independently without strong dependency on the other system, e.g. GNSS. And it’s the added value to provide positioning services to UE in the NR NTN system.
  Proposal: Support non-GNSS operation and NTN positioning.
    Study and specify the solutions to allow the access for the non-GNSS capable UEs.
    Study 3GPP positioning methods for UEs using only satellite access, irrespective of the GNSS capability.
      The Rel-18 positioning method(s) for UE location verification could be taken as baseline.
      Multi-satellites in view could be considered, for better accuracy and shorter latency.
  Example of NTN positioning with multi-satellites in view

## Slide 8: IoT NTN Evolution
Support of 5GC Connection [RAN3, RAN2]
  Motivation：There is already 5GC connection for terrestrial NB-IoT/eMTC is already supported in Rel-16. Enable 5GC connection for IoT NTN make the deployment more flexible, e.g. not necessary to deploy the EPC, 5GC could be used instead, with that the same 5GC could be used for IoT NTN, TN, NR NTN.
  Proposal: Support 5GC connection for IoT NTN.
    the 5GC connection for terrestrial NB-IoT/eMTC in Rel-16 could be taken as the BL, if any gap should be further confirmed and specified.
Support of Regenerative Payload and S&F [RAN2, RAN3, SA2?]
  Motivation: As mentioned before, support of Regenerative Payload has some benefits on resource handling and flexible deployment. On top of Regenerative payload architecture, S&F operation allows for delay-tolerant, non-real-time IoT NTN services to be offered in areas, where the UE could be served by the satellites without available feeder link connection, i.e. satellite could not connect to NTN-GW in the remote areas (e.g.mid-sea).
  Proposal: Support Regenerative Payload and S&F for IoT NTN.
    Specify the support of eNB/ng-eNB on board in TS 36.300 and define if needed, some enhancements related to S1 protocol to address feeder link switch over issue.
    Study and identify feasibility and potential impacts to support S&F in RAN (e.g. CP procedure enhancements, some QoS requirement).
S&F operation