## Slide 1: Consideration on R19 MBS enhancements
CATT, CBN, China Telecom
3GPP TSG RAN Meeting #101 RP-232056
Bangalore, India, September 11-15, 2023

## Slide 2: Support ECP in MBS
  R17 MBS, which is based on network-implemented small-scale SFN transmission, cannot meet the following requirements of MBS services:
    TV/Video services requires high spectral efficiency.
    Public safety service requires high reliability in receiving signals at the cell edge.
    The deployment of the low-frequency band (600MHz) in NR requires a larger station distance
Specify the support of extended CP for SCS 15Khz/30kHz [RAN1, RAN2]
Specify the ECP/NCP Switching [RAN1, RAN2]
Motivation
Objective
Proposal 1: ‘Support ECP in MBS’ is included as one objective in the Rel-19 NR MBS WI.

## Slide 3: Multicast enhancement in RAN sharing scenario
CN(PLMN 1)
CN(PLMN 2)
Application Server
Multicast service 1
RAN
Multicast service 1
TMGI 1
TMGI 2
UE in PLMN 2
UE in PLMN 1
UE in PLMN 1
UE in PLMN 1
UE in PLMN 2
UE in PLMN 2
PTM
  Efficiency improvement for multicast in RAN sharing scenario. The similar enhancement is already supported in Rel-18 for broadcast, and there is similar motivation to enhance for multicast.
Specify enhancements to improve the resource efficiency for multicast reception in RAN sharing scenarios[RAN3]
Motivation
Objective
3
Proposal 2: ‘Multicast enhancement in RAN sharing scenario’ is included as one objective in the Rel-19 NR MBS WI.

## Slide 4: MBS enhancements in CA and/or DC scenario
  Higher data rate requirement e.g., for gaming, video in car, and live broadcasting in stadium, etc.
Specify enhancement for multicast reception on multiple CCs in CA scenario [RAN2, RAN1]
Specify enhancement for multicast reception on SN in DC scenario [RAN3]
Motivation
Objective
Proposal 3: ‘MBS enhancements in CA and/or DC scenario’ is included as one objective in the Rel-19 NR MBS WI.

## Slide 5: R17/R18 leftovers
  In R18, Redcap CFR was introduced but limitation exists to use same resources for all types of UEs. It is not resource efficient for MBS services targeted for normal UEs and redcap UEs
  In R17 MBS, legacy power saving mechanism(e.g., PEI,WUS/DCP) is not applicable to MBS, which results in unnecessary power consumption for MBS UEs.
Specify enhancement for using same PDSCH resource for a MBS service targeted for all types of UEs if redcap CFR is configured [RAN1, RAN2]
Study and if necessary, specify power saving enhancements(e.g., extend the legacy power saving mechanisms to MBS)[RAN1, RAN2]
Motivation
Objective
Proposal 4: Consider to address the R17/R18 leftovers(e.g. enhancement for redcap CFR, power saving enhancement for MBS) in the Rel-19 NR MBS WI.

## Slide 6: Summary of the potential work scope of R19 MBS
As a summary, our proposals are in the following
Proposal 1: ‘Support ECP in MBS’ is included as one objective in the Rel-19 NR MBS WI.
Proposal 2: ‘Multicast enhancement in RAN sharing scenario’ is included as one objective in the Rel-19 NR MBS WI.
Proposal 3: ‘MBS enhancements in CA and/or DC scenario’ is included as one objective in the Rel-19 NR MBS WI.
Proposal 4: Consider to address the R17/R18 leftovers(e.g. enhancement for redcap CFR, power saving enhancement for MBS) in the Rel-19 NR MBS WI.