## Slide 1: Consideration on SON/MDT Enhancements
CATT
3GPP TSG RAN Meeting #101 RP-232058
Bangalore, India, September 11-15, 2023

## Slide 2: Outline
  MRO for Mobility enhancement
  SON/MDT enhancements for new NR use cases
  MBS
  SL Relay
  NTN
  Others if supported by majority
  （Use cases should be limited to avoid overload in Rel-19）

## Slide 3: MRO for Mobility enhancement
  Motivation
  L1L2 Triggered Mobility
    New cell switch mechanism
    Too late / too early LTM, LTM to wrong cell for successful / failed LTM
    Ping-pong issue due to fast L1 change
  NR-DC with selective activation cell of groups
    Ping-pong issue due to unsuitable execution condition configuration
  CHO including target MCG and candidate SCGs for CPC CPA
    HO with SN change was deprioritized in R18 and can be restarted in R19
  Objective
  L1L2 Triggered Mobility [RAN3, RAN2]
    RLF / SCG failure report enhancements for failed LTM
    SHR/SPR enhancements for successful LTM
    Whether ping-pong HO issue needs to be handled
  NR-DC with selective activation cell of groups [RAN3, RAN2]
    Whether ping-pong HO issue needs to be handled
  CHO including target MCG and candidate SCGs for CPC CPA[RAN3, RAN2]
    RLF report enhancements for failed CHO+candidate SCG execution
    SHR enhancements for successful CHO+candidate SCG execution

## Slide 4: SON/MDT enhancements for MBS
  Motivation
  MDT
    Legacy L2 measurements for DL data in NW side
    R17/R18 introduce MBS Broadcast/multicast in IDLE/INACTIVE
    To enable the statistical analysis of L2 measurements related to MBS services
  MRO
    MBS capable UE takes high frequency priority if certain conditions are met if UE is receiving or interested to MBS
    Result in potential HOF/RLF issues that cannot be solved by MRO
    Needs to be distinguished from normal case
  Objective
  MDT for MBS broadcast/multicast service(s) [RAN2]
    L2 measurement in IDLE/INACTIVE states
      By UE report
      At least M5/M7
  MRO for MBS service(s) [RAN3, RAN2]
    RLF/HOF report for failure caused by MBS service continuity

## Slide 5: SON/MDT enhancements for SL Relay
  Motivation
  Comprehensive analysis of the applicability of SON/MDT enhancement cases to sidelink connection
    Information reporting from remote UE
    Information transmission between networks
    Parameter optimization for related nodes
  Relay UE on-demand requests SI on behalf of remote UE
    Remote UE sends request SIB to relay on PC5-RRC messages
    Only real request by relay UE should be recorded by relay UE
  Network configures relay thresholds criteria
    To improve the network configured relay threshold values
  Objective
  SONMDT enhancements for SL relay/remote UE [RAN3, RAN2]
    MRO (RLF/HOF) for sidelink remote UE
    RA report for real on-demand SI requirement
    Optimization of the relay threshold(s) setting

## Slide 6: SON enhancements for NTN
  Motivation
  Additional trigger conditions of CHO, e.g. timer based trigger, location based trigger are introduced for NTN
  Objective
  SON enhancements for NTN [RAN3, RAN2]
    NTN-NTN/NTN-TN mobility
      NTN specific (e.g. timing and distance-based CHO) MRO
      NTN specific (e.g. timing and distance-based CHO) SHR
    NTN specific RACH report

## Slide 7: Summary
Proposal1: Support of MRO for mobility enhancement
Proposal2: More use cases are to be considered
    MRO and MDT enhancement for Broadcast/Multicast service
    SON/MDT enhancement for Sidelink Relay
    SON enhancements for NTN
    Others, e.g. NES, IAB, XR, …
    Note use cases should be limited to avoid overload in Rel-19