## Slide 1: Consideration on AI for NG-RAN
CATT
3GPP TSG RAN Meeting #101 RP-232059
Bangalore, India, September 11–15, 2023

## Slide 2: Overview
CN-RAN collaboration
AI inference in gNB-DU
New use cases
  QoE
  Slicing
Model delivery between network entities
Rel-18 leftover

## Slide 3: CN-RAN Collaboration
Motivation
  Access to different type of data
Assumption and background
  No mandatory impact on NWDAF
  Utilising the existing output from NWDAF:
    UE-associated statistics
    UE-associated predictions
Objective
  Enhancement on NGAP (and other interfaces if needed) to support collaboration between CN and RAN
Example of CN-RAN collaboration
  Core Network’s knowledge:
    After visiting Cell #0 and Cell #1 sequentially: UE “A” will probably visit Cell #2 or Cell #4; UE “B” will probably visit Cell #2 or Cell #3.
  RAN’s knowledge:
    If one UE goes westwards across the central crossing, it will probably visit Cell#3 or Cell #4.
  Collaboration [to be supported]:
    UE “A” goes westwards across the central crossing. Thus it will probably visit Cell #4.

## Slide 4: AI inference in gNB-DU
Motivation
  gNB-DUs usually has better access to dynamic data e.g. utilisation of radio resource,layer-1 measurement and per-RB UE traffic data rate
  gNB-DUs has better access to lower-layer adaption e.g. adaption of carrier bandwidth and activate/deactivate Scells
Assumption and background
  Align with existing method introduced in Rel-18 NG-RAN AI WI as possible
Objective
  Delivering prediction from gNB-DUs to gNB-CUs
  Delivering ground truth toward gNB-DUs
  More information toward gNB-DUs if identified:
    Inputs unavailable at gNB-Dus
    UE performance feedback

## Slide 5: New Use Cases
Slicing:
Motivation
  Optimise per slicing level resource partition
Objective
  Delivering per slice load prediction over interfaces(cell level)
  Transfer per slice traffic prediction during HO procedure(UE level)
QoE:
Motivation
  Optimise UE’s (RV)QoE
Assumption and background
  Follow existing RVQoE metrics:
    Initial Playout Delay
    Buffer Level
  Align with the mechanism introduced for the mobility use case introduced in Rel-18
Objective
  Delivering RVQoE predictions over interfaces
  RVQoE ground truth feedback
  Collaboration with CN for longer-term input if needed

## Slide 6: Model delivery&Rel-18 leftover
Model delivery
  Scenarios
    Model sharing between CN and RAN
    Model sharing between NG-RAN nodes e.g. Modal for energy cost prediction
    Model provision from gNB-CU to gNB-DU
  Assumption
    Follow NWDAF’s approach
  Objective
    Signalling design to support model delivery between network entities.
Rel-18 leftover
  NG-based mobility optimization
  MR-DC scenario
  others

## Slide 7: Summary
Proposal 1： Support of CN-RAN collaboration on data collection and data prediction
Proposal 2: Support AI inference in gNB-DU with AI training in either gNB-CU or gNB-DU
Proposal 3: More use cases are to be considered e.g. QoE and Slicing
Proposal 4: Enable model transferring between network entities.
Proposal 5: Further discussion on Rel-18 leftovers e.g. MR-DC