## Slide 1: Views on Low-Power wakeup receiver AI: 8A2.12.1
CATT
3GPP TSG RAN Meeting #101 RP-232065
Bangalore, India, September 11-15, 2023

## Slide 2: Study of LP-WUR/WUS
Study of low-power wakeup receiver (LP-WUR) and wakeup signals (LP-WUS) has been completed with results and observations captured in TR38.869
  Evaluation methodologies
    LP-WUR power model
    MR ultra-deep sleep power model
  Evaluation results
    UE power saving
    User perceived throughput (UPT)/Latency
    Coverage
    Network Overhead
    Network Energy consumption
Study of low-power wakeup receiver architectures
  RF envelop detector
  Heterodyne architecture with IF envelope detection
  Homodyne/zero-IF architecture with baseband envelope detection
  OFDM receiver
L1 signal/channel design for LP-WUR
  OOK, FSK, and OFDM waveform
  Synchronization signals and mechanisms for LP-WUR
  LP-WUS design and related procedures
  UE behavior in monitoring LP-WUS
  RRM measurements

## Slide 3: Observations from LP-WUR Evaluations
UE Power saving
  RRC_IDLE/Inactive UEs
    UE power saving gain up to more than 90% compared to the baseline I-DRX operation by using LP-WUS/WUR to trigger UE MR paging monitoring
    Paging latency reduction and moderate UE power saving gain compared with eDRX
  RRC_CONNECTED UEs
    UE power saving gain up to more than 10% for XR
    UE power saving gain more than 60% and UPT improvement more than 10% using LP-WUS for DRX adaptation for FTP and IM traffic
    UE power saving gain more than 40% and similar UPT performance for always-ON PDCCH monitoring
Coverage - LP-WUS can achieve comparable MIL performance with that of NR PUSCH MSG3
Overhead –
  For OFDM based LP-WUS carrying information of up to 24bits, the overhead up to 0.16% for 20MHz or 100MHz system BW
  For OOK/FSK-2 based LP-WUS carrying information up to 24bit, the overhead is up to 4.4% for 20MHz
Network Energy Consumptions
  The increase of the network energy consumption caused by the addition of the LP-SS signal transmission with 320ms periodicity, 4 or 8 beams and no more than 14 symbols is (0.06%~3.9%), (0.07%~2.716%), (0.388%~1.076%) for zero load, low load and medium load respectively

## Slide 4: LP-WUR architecture
For OOK waveform,
  For RF envelope detection,
    Relative Power consumption for ON duration: 0.01 - 0.2
    Noise figure: 12 - 22 dB
  For heterodyne architecture,
    Relative power consumption for ON state: 0.1 – 4.0
    Noise figure: 9 - 15 dB.
  For homodyne/zero-IF architecture,
    Relative power consumption for ON state: 0.05 – 4.0
    Noise figure: 10 - 16 dB.
For FSK waveform- The LP-WUR architectures is based on parallel OOK receivers
  For parallel heterodyne architecture,
    Relative power consumption for ON state: 0.1 – 1.0
    Noise figure: 9 - 15 dB.
  For parallel homodyne/zero-IF architecture,
    Relative power consumption for ON state: 0.1 – 1.0
    Noise figure : 10~16 dB.
For OFDMA-based signals,
  For time-domain correlation,
    Relative power consumption for ON state: 0.15~10/30
    Noise figure: 7-25 dB
  For frequency-domain correlation,
    Relative power consumption for ON state: 1 - 30
    Noise figure: 7- 12 dB

## Slide 5: LLS performance
OFDM waveform
  Coverage for LP-WUS with lower resource overhead.
  Capable of reusing PSS/SSS as the RS for RRM measurement and
  Robustness to Timing errors
    can be further improved using sliding window at the receiver.
OOK-1/OOK-4
  High spectral efficiencies
  Robustness to frequency error and timing error decreased
    Can be improved to mitigate the effect of timing error by the sliding window or by pulse shaping filter in time domain. .
FSK-2
  spectral efficiencies varying with M
  Robustness to frequency error and moderate timing error.
    Can be further improved using frequency error correction (i.e., utilizing 2^M parallel receiver structure or frequency domain sliding window), larger guard band between segments at expense of less frequency diversity, and/or single frequency segment FSK2-envelope IF.
    Timing error robustness can be further improved using sliding window or by pulse shaping in time domain.
  Uniform distribution of frequency spectrum density can be achieved using single frequency segment FSK2-envelope IF which can provide robustness against frequency fading.
  Sequences to generate ON duration in OFDMA transmitter, if specified, can help receiver (with I/Q branches) performance.

## Slide 6: Proposals for Rel-19 LP-WUR WI
Specify the signals and waveforms for the UE low-power wakeup receiver (LP-WUR) in achieving further UE power saving for CONNECTED and IDLE/Inactive UEs (RAN1)
  Specify the OOK waveform modulated by OFDM of the low-power wakeup signals (LP-WUS)
  Specify the information carried by LP-WUS
  The physical layer procedure of UE monitoring of LP-WUS
Specify the LP-WUS signals/procedure for UE LP-WUR of IDLE/Inactive and CONNECD mode UEs in achieving UE power saving (RAN1, RAN2)
  Specify the LP-WUS as the early paging indication for IDLEL/Inactive mode UEs
  Specify the LP-WUS as wakeup indication for PDCCH monitoring with/without C-DRX configuration forCONNECTED mode UEs
  Study and specify whether LP-WUS is used for UE mobility management
Higher Layer Procedure enhancement for LP-WUR [RAN2]
  Configuration and procedure of LP-WUS signals
  MAC procedure in supporting wakeup indication by LP-WUS
  UE behavior of receiving LP-WUS
Performance of low-power wakeup receiver [RAN4]
  Specify the minimum performance of LP-WUR
  Specify the ACL of LP-WUS while it is transmitted with NR signals/channel in the same carrier