## Slide 1: Discussion on Rel-19 Sidelink Relay
CATT
3GPP TSG RAN Meeting #101 RP-232067
Bangalore, India, September 11-15, 2023

## Slide 2: Multi-path enhancements
Rel-18 Background
Rel-18 Only consider intra-gNB One direct path + one indirect path UE-UE interface can be PC5 or ideal
TS 22.261 requirements
Motivations of multi-path enhancements
The 5G system shall support same traffic flow of a remote UE to be relayed via different indirect network connection paths. The 5G system shall support different traffic flows of a remote UE to be relayed via different indirect network connection paths.
Potential enhancements
  Intra-gNB multi-path with two indirect paths
  Inter-gNB multi-path with one indirect path and one direct path
  Inter-gNB multi-path with two indirect paths

## Slide 3: Multi-hop
Rel-17/18 Background
Rel-17 Single hop U2N Relay Rel-18 Single hop U2U Relay
Single-hop U2N Relay
Single-hop U2U Relay
TS 22.261
  2~15 hops required
  SP-230521
  SA1 WID on U2U multi-hop Relay
Motivations of multi-hop U2U/U2N Relay
Scenario | Max. data rate (DL) | Max. data rate (UL) | End-to-end latency (note 7) | Area traffic capacity (DL) | Area traffic capacity (UL) | Area user density | Area | Range of a single hop (note 8) | Estimated number of hops
InHome Scenario (note 1) | 1 Gbit/s | 500 Mbit/s | 10 ms | 5 Gbit/s/ home | 2 Gbit/s /home | 50 devices /house | 10 m x 10m – 3 floors | 10 m indoor | 2 to 3
Factory Sensors (note 2) | 100 kbit/s | 5 Mbit/s | 50 ms to 1 s | 1 Gbit/s /factory | 50 Gbit/s /factory | 10000 devices /factory | 100 m x 100 m | 30 m indoor / metallic | 2 to 3
Smart Metering (note 3) | 100 bytes / 15 mins | 100 bytes / 15 mins | 10 s | 200 x 100 bytes / 15 mins /hectare | 200 x 100 bytes / 15 mins /hectare | 200 devices /hectare | 100 m x 100 m | > 100 m indoor / deep indoor | 2 to 5
Containers (note 4) | 100 bytes / 15 mins | 100 bytes / 15 mins | 10 s | 15000 x 100 bytes / 15 mins /ship | 15000 x 100 bytes / 15 mins /ship | 15000 containers /ship | 400 m x 60 m x 40 m | > 100 m indoor / outdoor / metallic | 3 to 9
Freight Wagons | 100 bytes / 15 mins | 100 bytes / 15 mins | 10 s | 200 x 100 bytes / 15 mins /train | 200 x 100 bytes / 15 mins /train | 120 wagons /train | 1 km | > 100 m outdoor / tunnel | 10 to 15
Public Safety (note 5) | 12 Mbit/s | 12 Mbit/s | 30 ms | 20 Mbit/s /building | 40 Mbit/s /building | 30 devices /building | 100 m x 100 m – 3 floors | > 50 m indoor (floor or stairwell) | 2 to 4
Wearables (note 6) | 10 Mbit/s | 10 Mbit/s | 10 ms | 20 Mbit/s per 100 m2 | 20 Mbit/s per 100 m2 | 10 wearables per 100 m2 | 10 m x 10 m | 10 m indoor / outdoor | 1 to 2
Multi-hop U2N and U2U Relay
Service1
Service2

## Slide 4: Rel-19 objectives
Specify mechanisms to enhance multi-path for the following scenarios [RAN2, RAN3]:
  Intra-gNB multi-path with two indirect paths
  Inter-gNB multi-path with one indirect path and one indirect path
  Inter-gNB multi-path with two indirect paths
Specify potential solutions for multi-hop U2N Relay and U2U Relay [RAN2, RAN3]:
  Routing
  Control plane procedures (e.g., paging/system information forwarding, RLM/RLF and etc)
  User plane procedures (e.g., QoS split, resource allocation and etc)
  Note: The interface between Remote UE and Relay UE can be PC5 or ideal as in Rel-18.