## Slide 1
Views on 2Rx Relaxation for XR Wearables
Apple Inc.
  3GPP TSG RAN Meeting #101
  Bangalore, India, September 11-15, 2023
  Source: Apple
  Agenda Item: 9.3.2.9
  RP-232101

## Slide 2
Background
The discussion in RAN#100 offline XR session addressed the following point from RAN#99e (RP-230740):
  Step-1: Recognize that form factor limitations of a subset of XR devices can make it impossible for these devices to support 4 antenna ports
    Exact characterization and form factor limitations of these devices are to be studied in RAN plenary. Contributions are invited to TSG-RAN#100 to address this.
The offline session reached the following agreement:
  Agreement: handheld smartphone devices are excluded from any 2Rx relaxation for XR wearables.
The offline session then discussed some possible candidate options for characterization of non-RedCap XR devices to which a 2-Rx relaxation could apply, including, but not necessarily limited to:
  Type of device:
    (see TR26.928), e.g. [glasses, other XR wearables (further definition required)]
    E.g. devices that are supported by ears and/or nose without straps over or behind head?
  Rx-chain-usable volumetric measure:
    E.g. smaller than a benchmark of approx. [derived from volume of a smartphone?]
      Consider how to take into account volume that is not available for Rx-chain use
  Rx-chain-usable surface area measure:
    E.g. smaller than a benchmark of approx. [derived from surface of a smartphone?]
      Consider how to take into account surface area that is not available for Rx-chain use
Conclusion: Companies are encouraged to consider further details in relation to the above for further discussion at RAN#101.

## Slide 3
Vision Pro
Apple Vision Pro features an ultra-high-resolution display system that packs 23 million pixels across two displays — more than a 4K TV for each eye — and the brand-new R1 chip, for a virtually lag-free, real-time view of the world.
It has a custom Apple M2 chip and a dedicated R1 chip for processing sensor data from:
  12 cameras for tracking the user's head, eyes, and hands.
  5 sensors including a LiDAR scanner for measuring the distance to objects in the environment.
  6 microphones for immersive sound
All of them take space and are critical to deliver satisfactory user experience.
Fitting XR wearable device, e.g., Vision Pro, with 2Rx can be very challenging, let alone 4Rx.
Source: https://www.apple.com/apple-vision-pro/

## Slide 4
Different XR wearable device may have different form factor in terms of dimension/size, etc., therefore, it is possible that not all XR wearable devices need the 2Rx relaxation.
However, imposing additional requirements for the XR device Type is not appropriate:
  Inevitably, the discussion involves the actual device industrial design
    3GPP is not the right place for discussion related to industrial design
  It is extremely unlikely or impossible for device companies to disclose the industrial design, e.g., device dimension, for the non-released devices to 3GPP, and sub-categorization is not feasible.
  Wording for eligible devices like “devices that are supported by ears and/or nose without straps over or behind head” would bar some XR devices from being supported with 2Rx for cellular connectivity.
    We believe this would be highly undesirable for device vendors/operators/consumers.
Analysis on the “Type of device” Option

## Slide 5
  As can be seen from Vision Pro, many cameras, sensors and speakers can be present on an XR device.
  XR wearable device design is inevitably multidisciplinary by nature, factors from many aspects related to user experience can impact the product design
    Product may have to support many extra components that are not needed for conventional devices such as smart phone to deliver the desirable user experience required for XR wearable devices.
  In order to support cellular connectivity, placement of cellular antenna needs additional surface/volume on the device and requires careful consideration of coexistence with other components in the device to avoid interference or disruption to the operation of other components.
    The relaxation for 2Rx should not be used to force device vendors to disclose design details especially to 3GPP.
  While both the volume metric and surface area metric are relevant, to simplify the discussion, RAN discussion should focus on the volumetric discussion.
  We believe the volumetric measure can be used to determine the condition where 2Rx relaxation is justified.
Analysis on the “Options 2/3”

## Slide 6
We propose the following, if Option 2 is adopted:
  Specify mechanism to enable (XR) wearable devices to support only 2Rx antenna ports in the NR bands in which 4Rx antenna ports is mandated in legacy, consider the combination of the following mechanisms
    Consider description of 2Rx wearable UE in TS 38.101-1 to restrict the applicability of 2Rx relaxation
      Text Proposal: “2Rx wearable UE: A UE which is intended to be worn on human head with less than X cubic millimeters for Rx-chain-usable volumetric measure”.
        TBD: the exact value of “X”.
    UE reports the 2Rx antenna port support explicitly via capability reporting, e.g., using a single bit to indicate the XR wearable UE or using the existing UE capability signaling for # of MIMO layers to differentiate 2Rx UE from 4Rx UE, etc.
    Declaration and verification of 2Rx wearable UE is through bodies other than 3GPP such as certification organization, e.g., GCF, etc.
      UE is expected to be 3GPP compliant, external body other than 3GPP should be responsible for the verification of the volumetric measure.
Apple proposal for 2Rx relaxation for Option 2

## Slide 7
Summary
Proposal: Rx-chain-usable volumetric measure is adopted to support 2Rx relaxation for XR wearable device in the NR bands in which 4Rx antenna ports is mandated in legacy, consider the combination of the following mechanisms as example
    Consider description of 2Rx wearable UE in TS 38.101-1 to restrict the applicability of 2Rx relaxation
      Text Proposal: “2Rx wearable UE: A UE which is intended to be worn on human head with less than X cubic millimeters for Rx-chain-usable volumetric measure”.
        TBD: the exact value of “X”.
    UE reports the 2Rx antenna port support explicitly via capability reporting, e.g., using a single bit to indicate the XR wearable UE or using the existing UE capability signaling for # of MIMO layers to differentiate 2Rx UE from 4Rx UE, etc.
    Declaration and verification of 2Rx wearable UE is through bodies other than 3GPP such as certification organization, e.g., GCF, etc.
      UE is expected to be 3GPP compliant, external body other than 3GPP should be responsible for the verification of the volumetric measure.

## Slide 8: Appendix

## Slide 9
2Rx Relaxation
In current NR, for NR Bands n7, n38, n41, n48, n77, n78, n79, and n104 , the UE is mandated to support 4Rx ports
  Except for vehicular UE and RedCap UE
Current NR already supports relaxation for vehicular and RedCap UE such that vehicular and Redcap UE is only mandated to support 2Rx ports in NR Bands n7, n38, n41, n48, n77, n78, n79, and n104. Following is the quote from TS38.101
It is crucial for 3GPP to support a new type of devices, such as XR wearable considering the following factors
  4Rx antennas may not be feasible due to the form factor limitation
  Large BW (e.g., 100MHz in FR1) and CA is feasible and important for high demanding XR services
  Detailed explanation and analysis can be found in RP-222483
Vehicular UE: A UE embedded in a vehicle, permanently connected to an embedded antenna system that radiates externally for NR operating bands. NOTE: Vehicular UE does not refer to other UE form factors placed inside the vehicle. NOTE 1: Four Rx antenna ports shall be the baseline for this operating band except for two Rx vehicular UE. Four Rx antenna ports for RedCap UE is not supported for this operating band.

## Slide 10
In “Extended Reality (XR) in 5G” 3GPP TR 26.928, Rel-16, XR devices with variety of form factors are classified.
For AR and VR, the following device types are identified:
  XR5G-A1 - Simple AR Wearable Glass wired
  XR5G-A2 - Simple AR Wearable Glass wireless
  XR5G-A3 - Smart AR HMD video see-through
  XR5G-A4 - AR Wearable Glass standalone
  XR5G-A5 - Smart AR Wearable Glass wireless
  XR5G-V1 - Simple VR Display wired
  XR5G-V2 - Simple VR Display wireless
  XR5G-V3 - Smart VR Viewer wireless tethering
  XR5G-V4 - VR HMD standalone
Source: TR 29.928
2Rx Relaxation