## Slide 1: Enhanced multi-path and multi-hop relay in Rel-19

## Slide 2: Motivation 1: Power saving and reduced UE complexity for multi-path Relay
  The UE configured with Rel-18 multi-path relaying should always maintain both direct path and indirect path regardless of which path is actually selected for user data transmission, otherwise frequent path addition, modification and/or removal are required.
  In Rel-18, the remote UE should be reconfigured with path removal and addition for releasing one path and adding one path for power saving. This requires signaling overhead and power consumption with frequency RRC reconfigurations for both relay UE and remote UE.
  Dynamic direct/indirect path activation/deactivation and possibly dynamic path selection can be helpful for power saving and better usage of multi-path operation.
  Rel-18 multi-path relaying can be further enhanced for power saving and RedCap UE in Rel-19.
gNB
Relay UE
Relay UE
Remote UE
Remote UE
Relay UE
Direct
path
Indirect
path
Indirect
path
WiFi/BT/SL
WiFi/BT/SL

## Slide 3: Motivation 2: Multi-path Relay for UAM
  Rel-18 multi-path relaying can support UAM scenarios by configuring passenger’s UE as the remote UE and UAM as the relay UE.
    The direct path of multi-path relaying can serve RRC signaling while the indirect path of multi-path relaying via UAM can serve user data of the passengers.
  The direct path of multi-path relaying for the remote UE can be deactivated or released by gNB in Rel-19 e.g. based on the height of the on-board remote UE.
    Multi-path relay based on non-3GPP UE-to-UE link in Rel-18 can be enhanced for UAM.
  Rel-18 multi-path relaying can support UAM scenarios and be further enhanced for UAM in Rel-19.
WiFi/SL
Indirect
path
Direct
path
gNB
Relay UE
Remote UE

## Slide 4: Motivation 3: Restriction to non-3GPP based UE-to-UE link
  In Rel-18 Scenario 2, UE-to-UE link is based on non-3GPP standard (e.g. WiFi, BT) with some restrictions:
    Bearer mapping on indirect path is restricted.
    Only ideal UE-to-UE link and one serving relay UE are currently considered
  Such restrictions can be removed for inter-operability and usage extension e.g. for in-car passenger device connectivity using relay in the vehicle mounted UE; smart watch connectivity using smart phone or vehicle as relay; and better control of indirect path under gNB.
    Restriction to bearer mapping on indirect path can be removed by using an adaptation layer on non-3GPP based UE-to-UE link in Rel-19.
    More than one relay UE with or without direct path can be considered for better usage of multi-path operation e.g. mobility of remote UE between vehicle and house, mobility of smart watch between smart phone and vehicle, dynamic indirect path selection for IoT devices.
    CN impact is seldom considered in Rel-18 Scenario 2. Considering SA workload for enhanced feature, RAN can keep CN less impacted in Rel-19.
  Enhance non-3GPP based UE-to-UE link for intra-gNB case without CN impact (as specified in Rel-18)

## Slide 5: Multi-path enhencements for PS, RedCap and UAM
  Direct/indirect path for the remote UE can be dynamically activated or deactivated by gNB for power saving
    The direct path can be deactivated for a UE on board or at cell edge. Otherwise the indirect path can be deactivated.
  Direct uplink transmission can be restricted for the remote UE for reduced UE complexity
    RedCap UE capable of sidelink or WiFi/BT (e.g. smart watch) can be implemented with reduced uplink capability.
    Uplink L1 control channels can be kept but uplink user data can always go on indirect path via the relay UE for RedCap Remote UE.
gNB
Indirect
path
Direct
path
RedCap
Remote UE
WiFi/BT/SL
Relay UE
Relay UE
WiFi/BT/SL
Indirect
path

## Slide 6: U2N/U2U SL relay enhancements for multi-hop
  Multi-hop L2 U2N relay can be supported for mission critical communications
    Support <gNB – Relay UE1 – Relay UE2 – Remote UE>
    Support L2 based multi-hop U2N relay by combining Rel-17 U2N relay and Rel-18 U2U relay
  Multi-hop U2U relay can be supported for mission critical communications
    Support <Remote UE1 – Relay UE1 – Relay UE2 – Remote UE2>
    Support L2 or L3 based multi-hop U2U relay
      Rel-18 U2U design (e.g. adaptation layer, QoS split and signaling procedures) should be considered as a baseline.
  Enhance L2 U2N relay and U2U relay for support of multi-hop SL relay

## Slide 7: Objectives
    Support power saving, UAM and reduced UE complexity for intra-gNB multi-path relaying [RAN2]
      Dynamic path activation/deactivation for SL relay and non-3GPP relay
        Support direct path activation/deactivation for multi-path relaying (e.g. for UAM)
        Support multiple indirect paths using multiple relay UEs with or without direct path (e.g. smart watch via vehicle and smart phone)
        Only one active indirect among one or more configured indirect paths under a same gNB
      Support reduced UE capability for multi-path relaying
        Support restriction to direct uplink data transmission
      Support non-ideal WiFi/BT and adaptation layer for non-3GPP relay i.e. no Rel-18 bearer mapping restriction in Scenario 2
    Enhance U2N relay and U2U relay for support of multi-hop SL relay [RAN2]
      Multi-hop L2 U2N relay based on combination of R17 U2N and R18 U2U
      Multi-hop L2 or L3 U2U relay based on R18 U2U design