## Slide 1
3GPP TSG RAN Meeting #101 RP-232114
Bangalore, September 11-15, 2023
Source: Huawei, HiSilicon
Title: Characterization and form factor for 2Rx XR wearable devices
Document for: Discussion and decision
Agenda Item: 9.3.2.9

## Slide 2
Background of “2Rx relaxation for XR wearable devices”
Discussion history in RAN plenary: Raised in RAN#96, endorse way forward in RP-231483 at RAN#100
Issue firstly raised
Issue re-submitted, but no discussion
Issue re-submitted, had some discussions, but no conclusion
Endorsed a way forward (see RP-230740)
202206 (RAN#96)
202209 (RAN#97)
202212 (RAN#98）
202303 (RAN#99)
Endorsed a way forward (see RP-231483)
202306 (RAN#100)
The offline session reached the following agreement:
Agreement: handheld smartphone devices are excluded from any 2Rx relaxation for XR wearables.
The offline session then discussed some possible candidate options for characterization of non-RedCap XR devices to which a 2-Rx relaxation could apply, including, but not necessarily limited to:
Type of device:
  (see TR26.928), e.g. [glasses, other XR wearables (further definition required)]
  E.g. devices that are supported by ears and/or nose without straps over or behind head?
Rx-chain-usable volumetric measure:
  E.g. smaller than a benchmark of approx. [derived from volume of a smartphone?]
    Consider how to take into account volume that is not available for Rx-chain use
Rx-chain-usable surface area measure:
  E.g. smaller than a benchmark of approx. [derived from surface of a smartphone?]
    Consider how to take into account surface area that is not available for Rx-chain use
Conclusion: Companies are encouraged to consider further details in relation to the above for further discussion at RAN#101.
RAN#99 discussions (Endorsed way forward below)
RAN#100 discussions (Endorsed way forward below)
Step-1: Recognize that form factor limitations of a subset of XR devices can make it impossible for these devices to support 4 antenna ports
Exact characterization and form factor limitations of these devices are to be studied in RAN plenary. Contributions are invited to TSG-RAN#100 to address this.
Step-2: Contingent on the outcome of the Step-1: Recognize the importance of identifying these devices in the network, and potential network impact (e.g. performance, coverage, capacity) and UE impact
Details of Step-2 will be further defined following the maturity of Step-1

## Slide 3
Discussion – Time plan to address XR 4Rx vs 2Rx issue
XR is one important industry to expand the value for 5G-Advanced
  Annual shipments of XR devices are increasing: about 15 million in 2022, and will go to 26/45 million in 2023/2025 (From Omida [1]).
  Timely readiness from devices helps building up the eco-system of 5G XR industry.
Q1: Time plan for 3GPP to resolve XR 4Rx vs 2Rx issue needs to be discussed according to the marketing trends
  Better to resolve this issue within Rel-18 timeframe, otherwise the opportunities for cellular system to support XR industry could slip
  RAN#101 decides the characterization of XR devices to which a 2Rx relaxation could apply, based on candidate options in RAN#100
  The subsequent work is to provide a suitable mechanism to identify these type of XR devices
    WG-level discussions are required
    Considering some legacy mechanism (e.g. SPID) can be potentially reused, 2 WG meetings could be sufficient
    RAN#102 can have a final decision on the identification mechanism
  Proposal 1: It is suggested to resolve XR 4Rx vs 2Rx issue in Rel-18 in 3GPP RAN as per the below time plan
  RAN decides the characterization of XR devices to which a 2Rx relaxation could apply at RAN#101
  RAN2 and RAN4 are tasked to provide candidate solutions to identify this type of XR devices in the network in 2023 Q4
  RAN aims to conclude the identification mechanism at RAN#102
[1] https://omdia.tech.informa.com/pr/2023/02-feb/omdia-near-eye-display-shipments-for-xr-applications-will-grow-by-67-in-2023-thanks-to-the-new-model

## Slide 4
Discussion – Technical consideration on XR 4Rx vs 2Rx
  Q2: Characterization of XR devices to which a 2Rx relaxation could apply
  3 candidate options are identified in RAN#100
    Option 1: Type of device
    Option 2: Rx-chain-usable volumetric measure
    Option 3: Rx-chain-usable surface area measure
  Rx-chain size of smartphones/XR devices
    Rx-chain = Antenna + Cable + Radio Frequency Integrated Circuit (RFIC)
    Antenna size
      Antenna size are dependent on the wavelength regardless whether devices are smartphones or XR devices
      Typical design for smartphones: line antennas and patch antennas
          Line antenna: 1/4 wavelength long (25mm@3GHz), <1 mm width (fit inside the frame of smartphone)
          Patch antenna: tens of mm^2 per antenna
          One smartphone usually has more than 10 antennas, and needs to consider spacing distance between antennas (>= half wavelength)
    RFIC: tens of mm^2 per RFIC, one device may have 1~2 RFIC (depending on the number of supported bands)
Line antenna inside the frame of smartphone
Observation 1: The current size of Rx-chains is already small enough and is difficult to separate between smartphones and XR devices.
Observation 2: The current design of Rx-chains has different forms and is difficult to define a methodology in 3GPP to measure.

## Slide 5
Discussion – Technical consideration on XR 4Rx vs 2Rx
  Detailed analysis on the candidate options
 | Option 1: Type of device | Option 3: Rx-chain-usable surface area measure
Potential way to define 2Rx XR devices | Introduce a new device type, which only allows XR glasses, and not allow XR headset or other XR devices, etc. the below is an example: Wearable Glasses XR UE: A wearable glasses UE that supports XR services and is worn on the head with the support only by ears and nose, which has no straps over or behind head and has a different form factor in contrast to smartphones and XR headsets. | Introduce a surface area threshold. If a device’s Rx-chain-usable surface area <= threshold, then it is assumed to be a XR device with form factor limitation, and can be relaxed to use 2Rx.
Specification impact | RAN2: specify identification mechanism for such new device Alt 1: similar mechanism as REDCAP, e.g. MSG1/MSG3 early identification Alt 2: similar mechanism as 2Rx for vehicles, e.g. a new SPID value for 2Rx XR devices RAN4: Add 2Rx exception for such new device (TS 38.101-1) RAN5: Add test cases | RAN2: UE capability reporting, e.g., UE reports its Rx-chain-usable surface area, this may be difficult to define, also dependent on the number of bands supported, how to locate the RF chains etc. RAN4: define the detailed form factors on Rx-chain, this may be complicated to consider different forms, e.g. line antenna, patch antennas, RFIC etc. RAN5: Add test case
Feasibility of this option | High. Similar as Vehicular UE and REDCAP UE. | Low. Difficult to define Rx-chain surface area or volumes.
Impact to smartphone | Low. The device type definition has clearly limited the usage for XR glasses only. | High. The Rx-chain limitation can not clearly separate XR devices and smartphones, and 2Rx relaxation can be applied to smartphones without clear separation.
Observation 3: Option 2/3 is difficult to define in 3GPP and may have impacts on smartphones, and Option 1 is the only feasible way forward.
Note: option 2 is similar as option 3 on the above analysis

## Slide 6
Proposed way forward
  Observation 1: The current size of Rx-chains is already small enough and is difficult to separate between smartphones and XR devices.
  Observation 2: The current design of Rx-chains has different forms and is difficult to define a methodology in 3GPP to measure.
  Observation 3: Option 2/3 is difficult to define in 3GPP and may have impact on smartphones, and Option 1 is the only feasible way forward.
  Proposal 1: It is suggested to resolve XR 4Rx vs 2Rx issue in Rel-18 in 3GPP RAN as per the below time plan
  RAN decides the characterization of XR devices to which a 2Rx relaxation could apply at RAN#101
  RAN2 and RAN4 are tasked to provide candidate solutions to identify this type of XR devices in the network in 2023 Q4
  RAN aims to conclude the identification mechanism at RAN#102
  Proposal 2: Adopt “Option 1: Type of device” to characterize XR devices to which 2Rx relaxation could apply.
  Wearable Glasses XR UE: A wearable glasses UE that supports XR services and is worn on the head with the support only by ears and nose, which has no straps over or behind head and has a different form factor in contrast to smartphones and XR headsets.
  Proposal 3: Task RAN WGs to further study options for identifying 2Rx XR devices.
  Option 1: similar mechanism as REDCAP, e.g. MSG1/MSG3 early identification
  Option 2: similar mechanism as 2Rx for vehicles, e.g. a new SPID (Subscriber Profile ID for RAT/Frequency Priority) value for 2Rx XR devices
  Proposal 4: Task RAN4 and RAN5 to differentiate the requirements and test cases between 2Rx XR devices and smartphones/other XR devices, to ensure 4Rx mandatory support for smartphones/other XR devices is not relaxed.