## Slide 1: Vehicle-Mounted Relay in Rel-19
RP-232141
Agenda Item: 8A.2.14.1
Source: Xiaomi
Document for: Discussion
3GPP TSG RAN#101 Bengaluru, India, September 11 – 15, 2023

## Slide 2
New service types (e.g. XR)
Non-Terrestrial Networks
Unmanned Aerial Vehicle
Communication System in Car
New scenarios to be considered in R19 VMR

## Slide 3: ECO-Communication System in Car
Motivation:
Various devices can be connected to a smart car via different access technologies (e.g. Wi-Fi, BlueTooth and 3GPP Sidelink/Uu).
Those devices in car may want to communicate locally or access local services in car.
Proposal:
Support of multiple access technologies， local service breakout and local switch
  => Full gNB + partial CN functions (e.g. UPF and N3IWF) onboard, focus on:
    Relay mechanism
    Integration
    Mobility
    Coordination with SA2 is needed

## Slide 4
VMR with NTN
Motivation:
NTN can provide better coverage for VMR (i.e. mobile IAB-node) to expand the VMR scenarios.
Transparent NTN is already supported in R18.
Proposal: support of VMR access to transparent NTN for IAB-node in transparent NTN, to improve the coverage. Following cases can be considered, case 1 can be considered firstly:
Case 1, R18 mobile IAB-node access to transparent NTN (both mIAB-node and its donor are on ground)
Case 2, R18 mobile IAB-node access to regenerative NTN (mIAB-donor is on ground)
Case 3, R19 VMR access to transparent NTN and regenerative NTN

## Slide 5
Option 2 IAB-node on UAV,
multi-hop.
VMR with UAV
Motivation: UAV can be deployed as IAB-node to provide services for more UEs in some scenarios, e.g. disaster monitoring, border surveillance, and emergency assistance.
Proposal: support R18 mobile IAB-node on UAV, consider single hop first and then multi hop.
UAV connected to IAB-donor via other IAB-nodes(s), to improve coverage.
Option 1 IAB-node on UAV, single-hop.
Notes: In some scenarios, e.g. disaster monitoring, border surveillance, and emergency assistance, unmanned aerial vehicles (UAVs) are a good choice for commercial application, due to ease of deployment, low acquisition and maintenance costs, high-manoeuvrability and the ability to hover.

## Slide 6
Backhaul QoS assurance
Motivation:
With the popularization of multimedia system, users may have XR services in more scenarios, e.g via VMR network.
There is a wide variety of backhaul types in VMR, e.g. via NTN, UAV if supported in R19.
There may be different paths and hops for a service in VMR topology.
QoS handling for XR services is different from the legacy services.
Proposal:
Ensure the backhaul QoS in R19 VMR topology network e.g. for XR services.

## Slide 7
Source: 3GPP TR 22.839 V18.1.0
R18 leftovers
Motivation:
There are scenarios where it is possible to improve performance of 5G UEs inside a vehicle, camped or connected via the vehicle relay to the 5G network, in particular when the UE is known to be located inside the vehicle.
This may not be fully supported in R18.
Proposal:
Support of on-board UE identification
Support group mobility for the onboard UEs.

## Slide 8
Conclusions
The following scenarios can be considered in R19 VMR:
In car services and communication.
Coverage enhancement to leverage NTN and UAV.
Backhaul QoS in VMR topology.
R18 leftovers on UE access control and mobility.
The following aspects can be discussed in R19 VMR:
Support of multiple access technologies, local service breakout and local switch.
Support of R18 mobile IAB-node access to transparent NTN.
Support of R18 mobile IAB-node on UAV, focus on single-hop.
Ensure the backhaul QoS in R19 VMR topology network.
Support of onboard UE identification and group mobility (depends on R18 progress).

## Slide 9: Thanks