## Slide 1: RAN Visible QoE in Rel-19
RP-232144
Agenda Item: 8A.2.14.2
Source: Xiaomi
Document for: Discussion
3GPP TSG RAN#101 Bengaluru, India, September 11 – 15, 2023

## Slide 2: RAN Visible QoE Collection for Mobility Optimization
Motivation:
Mobility optimization is one of the most important aspects in network optimizations.
UE may suffer bad experience during mobility even though the handover is successful.
Proposal:
RVQoE measurement can be triggered by mobility related events.
RVQoE report can be forwarded for mobility optimization.
UE movement
path with time
Start RVQoE
meas.
Stop RVQoE meas.
send RVQoE report
Forward RVQoE report for mobility optimization

## Slide 3: RAN Visible QoE Reporting via lower layer signalling
Motivation: The main purpose of RVQoE is for real-time scheduling, but existing reporting mechanism costs longer time, compared to the scheduling periods, which may lead to improper scheduling decisions.
Proposal: Support of RVQoE reporting via lower layer signalling for real-time scheduling.
RVQoE reporting via higher layer
(existing mechanism)
RVQoE reporting via lower layer
(greatly reduce latency)

## Slide 4: RAN Visible QoE Value
Motivation:
RVQoE value had been discussed since R17, but it’s not supported in R18, due to progress of SA4 and ITU-T, etc.
RVQoE value can be used for the RAN specific purposes.
Proposal:
Identify the RAN requirements on RVQoE value, e.g. lower latency or signalling overhead.
Define RVQoE value based on the RAN requirements, similar to CQI, which is also used for scheduling.
0. RVQoE value generation table
1. Generate the RVQoE value according to the table predefined or received from gNB
2. RVQoE value report

## Slide 5
Conclusions
The following aspects can be considered for RVQoE in R19:
Mobility optimization:
RVQoE measurement can be triggered by mobility related events.
RVQoE report can be used for mobility optimization.
Real-time scheduling:
Support of RVQoE reporting via lower layer signalling for real-time scheduling.
RAN Visible QoE Value:
Identify the requirements on RVQoE value, e.g. lower latency or signalling overhead
Define RVQoE value based on the RAN requirements.

## Slide 6: Thanks