## Slide 1: Views on AI/ML for NR Air Interface in Rel-19
3GPP TSG RAN Meeting #101
Bangalore, India, September 11-15, 2023
Source: ZTE, Sanechips
Agenda: 8A.2.1
RP-232156

## Slide 2: Views on AI/ML LCM aspects
LCM aspects | Initial views
Data collection | According to the study in RAN2, current signaling frameworks (e.g., Logged MDT, Immediate MDT, L3 measurements, L1 measurement, UAI, Early measurement, and LPP) are sufficient for data collection on AI/ML over air interface Reuse current reporting framework for data collection in Rel-19
Model/functionality identification | Functionality identification relies on distributed radio resource control by gNB as legacy Model identification requires more offline efforts on the model registration, model transfer and centralized model management, which has specification impacts on other WGs (e.g., SA) Functionality-based LCM can be a starting point for normative work in Rel-19
Performance monitoring | Due to the generalization limitation of AI/ML models, it’s hard to deploy an AI/ML model for all scenarios Define the requirements and procedures to monitor the performance on both active and inactive models/functionalities
Functionality/model switching/activation/deactivation/fallback | Network is responsible for the radio resource control and overall system throughput Network should have a final decision on a functionality/model that is not transparent to network Fallback mechanism is always necessary to avoid the network outage

## Slide 3: Views on AI/ML LCM aspects
LCM aspects | Initial views
Model training | Offline training is assumed in the Rel-18 study phase, which can be a starting point for WI in Rel-19
Model transfer/delivery | There are no clear motivations and benefits of model transfer for proprietary-format models For model transfer/delivery with open-format, how to describe a model with open-format should be further studied by other working groups The LCM procedures without model transfer can have a higher priority in Rel-19 (e.g., collaboration level y). However, the standardization in Rel-19 should be future-proof/compatible with model transfer in the future
UE capability/dynamic mechanism | UE processing capability on model/functionality and latency for model/functionality activation, deactivation, selection, switching and fallback. UE capabilities for the co-existing of both AI/ML-enabled features and non-AI/ML features Specify dynamic mechanisms to enable UE to report applicable models/functionalities
Some of the common LCM aspects can be studied/discussed together in the SI on AI/ML for RAN.

## Slide 4: Views on AI/ML use cases
Use cases | Initial views
Spatial-frequency domain CSI compression using two-sided AI model | Observations Not so attractive performance gains over legacy codebook even high model complexity is assumed High offline co-engineering efforts between UE and network vendors for model training Given the limited TU in RAN4, testing framework for the two-sided model may be hard to be finalized in Rel-18 Either drop this sub-use-case or further study the spatial-frequency domain CSI compression using two-sided model in Rel-19, including Increase performance gains (e.g., via model transfer/model switching) Reduce the offline co-engineering efforts (e.g., Type 3 training collaboration) Define testing framework for the two-sided model in RAN4
Time domain CSI prediction using UE sided model | Evaluation results show that time domain CSI prediction using UE-sided model can achieve performance gains over different benchmark schemes (i.e., the nearest historical CSI without prediction, non-AI/ML based CSI prediction and collaboration level x AI/ML based CSI prediction approach ) Specify the time domain CSI prediction using UE sided model in Rel-19 according to the study outcome in Rel-18 Reuse the Rel-18 MIMO enhancements for CSI prediction as much as possible

## Slide 5: Views on AI/ML use cases
Use cases | Initial views
Spatial-domain Downlink beam prediction for Set A of beams based on measurement results of Set B of beams | Evaluation results show that high beam prediction accuracy of Top-1/K beam can be achieved even with reduced number of beams for measurement. Specify AI/ML beam management for both spatial-domain downlink beam prediction and temporal downlink beam predication in Rel-19 according to the study outcome in Rel-18 Specify LCM aspects for AI/ML beam management on both UE-side model and network-side model
Temporal Downlink beam prediction for Set A of beams based on the historic measurement results of Set B of beams | 
Direct AI/ML positioning using UE location as AI/ML model output | Evaluation results show that the enriched channel information (e.g., additional paths, PDP and CIR) can significantly increase the positioning performance in some scenarios (e.g., heavy NLos scenarios) Model generalization cannot be maintained across drops/clutter parameters/InF scenarios It can be up to UE/gNB implementation for UE/gNB-side model Focus on enhancements to facilitate LMF-side model in Rel-19 for AI/ML based positioning
AI/ML assisted positioning using new/existing measurements as AI/ML model output | 
Focus on the normative work of the existing use cases.

## Slide 6: Thanks