## Slide 1: Proposal on AI/ML for NR air interface and ML-Aided predictive mobility in Rel-19

## Slide 2: Overall Scope for Rel-19
Normative work for Rel-18 use cases
  Rel-18 AI/ML SI studies general framework and 6 sub-use cases including
    CSI feedback enhancement
      CSI compression based on two-sided model
      CSI predication based on UE-sided model
    Beam management
      Spatial domain beam prediction based on one-sided model
      Temporal domain beam prediction based on one-sided model
    Positioning accuracy enhancement
      Direct positioning based on one-sided model
      AI/ML assisted positioning based on one-sided model
  For each sub-use case, RAN WGs have evaluated performance benefit and assesse potential specification impact during the study item. The conclusion is that, in general, AI/ML model based operations are expected to provide potential gain compared to existing scheme in terms of performance and/or overhead.
   To enable the AIML-enabled gain for the use cases, normative work should be initiated in Rel-19.
Study on higher layer application of AIML capabilities
  Predictive mobility is one of the most important higher layer functionalities that can benefit from AIML capabilities.
  To achieve the expected gain by enabling predictive mobility, the following area should be explored first:
    Predictive RRM
    Predictive mobility triggering
    Predictive RLM and proactive recovery
   It is important in Rel-19 to study the requirements and functionalities necessary to enable the predictive mobility. Corresponding normative work can be initiated in Rel-20.

## Slide 3: Consideration Point for Rel-18 use cases
Some challenging/controversial parts identified during SI are
  Model transfer
  Dataset delivery
  Model identification over-the-air
Way forward
  In order to facilitate AI/ML applications in air-interface, it will be beneficial to start work item with focused scope in Rel-19
  The work scope should be selected based on the following aspects
    Level of SI completeness and possible extension of SI can be considered in introducing Rel-19 WI
    Easier adaptation to vendors (e.g. keeping vendor-specific proprietary information)
    Expected performance gain
    Expected amount of specification impact

## Slide 4: Enhanced UE capability framework
Motivation
  In Rel-18 AI/ML SI, AI/ML framework is discussed for functionality/model-based LCM(life-cycle management)
  A key enhancement to facilitate AI/ML operation for UE-side model is to introduce enhanced UE capability framework
    In current specification, UE should report its capability based on “worst case” assumption to support a feature in any case.
    When UE uses AI/ML algorithm for a feature, the feature may not be supported in some condition, e.g. due to site/scenario-specific model, model deactivation/update, etc.
      Based on current UE capability framework, UE may have to report “not” support the feature due to the worst case assumption.
Scope
  Specify enhanced UE capability framework to facilitate UE-side AI/ML operation (e.g. dynamic update of applicable UE functionality) for Rel-18 use cases

## Slide 5: CSI feedback enhancement
Motivation
  For CSI compression based on two-sided model,
    At least three different types of offline training collaboration types were identified. Considering pros/cons in terms of flexibility, extendibility, privacy/proprietary and performance, Type 2 (joint training at NW and UE) can be deprioritized.
    Compared to legacy TypeII CSI, it is observed that AI/ML based CSI compression provides not very promising performance gain.
      -11~17% gain and -19~30% gain for mean UPT gain and 5% UPT gain, respectively, under FTP traffic model and 1-on-1 joint training with max rank 4 [1].
  For CSI prediction based on UE-sided model,
    Discussions on specification impact with limited scope
      Data collection
      Model monitoring and associated fallback operation
    Observations were made based on the small number of samples compared to CSI compression.
      -8~17% gain for FTP model, -2~15% gain for full buffer compared to non-AI based CSI prediction.
Scope
  Study and, if needed, specify CSI prediction (1st priority) or CSI compression with limited training collaboration type(s) (2nd priority) including at least following aspects.
    Data collection – No CSI-RS enhancement is assumed
    Inference
    LCM-related aspect
Figure 1. Illustration of CSI compression
[1] RAN1#114 chairman’s note

## Slide 6: Beam management
Motivation
  For temporal/spatial domain prediction based on one-sided model, followings are studied
    Alt.1: DL Tx beam prediction
    Alt.2: DL Rx beam prediction (deprioritized)
    Alt.3: DL Tx-Rx Beam pair prediction
  Compared to DL Tx beam prediction, DL Tx-Rx beam pair prediction has a lot of practical challenges such as representing UE beams in standard form, revealing vendor-specific proprietary information, restricting UE implementation-specific beam optimization.
    Note that clear performance benefit from DL Tx-Rx beam pair prediction over DL Tx beam prediction is not observed.
Scope
  Specify spatial/temporal DL Tx beam prediction based on one-sided AI/ML model including at least following aspects.
    Data collection – No SSB/CSI-RS enhancement is assumed
    Inference
    LCM-related aspect
Figure 2. Illustration of beam prediction

## Slide 7: Positioning accuracy enhancement
Motivation
  During the study item, following AI/ML based positioning methods were studied.
    Case 1: UE-based positioning with UE-side model, direct AI/ML or AI/ML assisted positioning
    Case 2a: UE-assisted/LMF-based positioning with UE-side model, AI/ML assisted positioning
    Case 2b: UE-assisted/LMF-based positioning with LMF-side model, direct AI/ML positioning
    Case 3a: NG-RAN node assisted positioning with gNB-side model, AI/ML assisted positioning
    Case 3b: NG-RAN node assisted positioning with LMF-side model, direct AI/ML positioning
  Given above variations, scope reduction of AI/ML based positioning needs to be considered.
  It is observed both AI/ML positioning methods can provide performance gain over existing positioning methods when generalization aspects are not considered.
Scope
  Specify direct and AI/ML assisted positioning including at least following aspects.
    Down-selection among five sub-use cases should be considered
    Data collection – No PRS/SRS enhancement is assumed
    Inference
    LCM-related aspect
    Note:
    Direct AI/ML positioning : the output of AI/ML model inference is UE location
    AI/ML assisted positioning: the output of the model inference is new measurement and/or enhancement of existing measurement

## Slide 8: Proposed objective for Rel-18 use cases
Specify enhanced UE capability framework to facilitate UE-side AI/ML operation (e.g. dynamic update of applicable UE functionality).
Study and, if needed, specify CSI prediction (1st priority) or CSI compression with limited training collaboration type(s) (2nd priority).
Specify spatial/temporal DL Tx beam prediction based on one-sided AI/ML model.
Specify direct and AI/ML assisted positioning based on one-sided AI/ML model.
Note: following aspects should be considered.
  Focus on signaling-based collaboration without model transfer (collaboration level y only).
  Focus on offline training only.
  Specification impact on
    Data collection without RS enhancement,
    Inference,
    Functionality/model based LCM operation.

## Slide 9: New Use case: Predictive Mobility
Justification
  In Rel-18, CSI/beam prediction has been considered as one of the main use cases of exploiting AIML capabilities.
  However, higher layer application of AIML remains unexplored.
    There are many higher layer functionalities that can benefit from exploiting AIML capabilities
  In our view, mobility is the most important and suitable area as higher layer application of AIML capabilities.
    Mobility is based measurements (L3 measurements for L3 mobility, L1 measurement for LTM)
    Predictive CSI measurements has been studied in Rel-18. Extension of Rel-18 CSI prediction can be a starting point for Rel-19 study for ‘Predictive Mobility’.
New use case: Predictive Mobility
  Study on a new use case, Predictive Mobility is proposed for Rel-19
  Scope of Predictive Mobility can include:
    Predictive RRM (L3 measurement, L1 measurements)
    Predictive mobility triggering (NW-triggered mobility based on predictive RRM, and conditional mobility based on predictive RRM)
    Predictive RLM and proactive recovery
  The predictive mobility use case can be led by RAN2 with possible involvement of other RAN WGs.

## Slide 10: New Use case: Predictive Mobility
Handover failure or unnecessary handover
  Handover problems such as handover failures or unnecessary handovers incur data interruption causing significant QoS degradation.
  The root cause of the handover problems is that the mobility decision is currently based on the present radio link quality. If there is a quality gap between the present and the future, the chance of the handover failure or wrong handover increases. Optimal mobility decision necessarily requires the knowledge of the future radio conditions for an appropriate time span.
Predictive Measurement and Predictive Mobility
  Time domain measurement prediction capabilities enabled by UE’s ML capabilities allows UE to predict radio quality for a source cell as well as target cells.
  Such predictive measurement capabilities can give new opportunity to avoid handover problem by performing predictive measurement reporting and/or predictive mobility execution.
  By avoiding handover problem via predictive measurement reporting and/or predictive mobility execution, quality of service can be significantly improved.
Time
RSRP
Time
RSRP
Time
RSRP
Serving Cell (1)
Neighbour Cell (2)
(a) Too Late HO
RLF
Serving Cell (1)
Neighbour Cell (2)
(b) Too Early HO
Neighbour Cell (2)
Serving Cell (1)
mobility
(Cell 1 -> Cell 2)
RLF
Neighbour Cell (3)
mobility
(Cell 1 -> Cell 2)
mobility
(Cell 2-> Cell 1)
(c) Ping-pong
Stiff
gradient

## Slide 11: New Use case: Predictive RRM
Predictive RRM
  Predictive Measurements for future time
    UE can perform measurements for serving cell and neighbour cells for future time.
    UE can derive predictive measurement results for a future time.
    UE can derive a future time at which predictive measurement results meet the report condition or execution condition for mobility.
Time
RSRP
Serving Cell (1)
Neighbour Cell (2)
Neighbour Cell (3)
Neighbour Cell (4)
Predictive measurement
Perform measurement
< Predictive Measurements for future time , and at >

## Slide 12: New Use case: Predictive Mobility
Predictive Mobility
  Predictive mobility decision based on predictive measurements
    Network-triggered Mobility
      UE can send measurement reports including predictive measurement results
      Network can decide a handover with an appropriate cell and an appropriate time based on predictive measurement reports.
    Conditional mobility
      UE can execute CHO to a suitable target cell among candidate target cells based on predictive measurement results of target cells
    Based on the predictive mobility, handover problems such as handover failures or unnecessary handovers can be avoided.
Time
RSRP
Time
RSRP
Time
RSRP
Serving Cell (1)
Neighbour Cell (2)
(1)Predictive measurement
(2)Mobility
Cell 1 -> Cell 2
(t1)
(t2)
(a) Avoidance of late HO
RLF
w/ Legacy mobility
Serving Cell (1)
Neighbour Cell (2)
(1)Predictive measurement
(t1)
(2)Mobility
Cell 1 -> Cell 2
(t2)
(b) Avoidance of early HO
Neighbour Cell (2)
Serving Cell (1)
Legacy mobility
(Cell 1 -> Cell 2)
RLF
w/ Legacy mobility
Neighbour Cell (3)
(1)Predictive measurement
(t1)
(2)Mobility
Cell 1 -> Cell 3
Legacy mobility
(Cell 1 -> Cell 2)
Legacy mobility
(Cell 2-> Cell 1)
(t2)
(c) Avoidance of Ping-pong

## Slide 13: New Use case: Predictive RLM
Predictive Radio Link Failure and Reactive Recovery
  Currently UE declares radio link failure (RLF) if ‘consecutive’ failures are detected. Radio link monitoring is based on measurement results of RLM-RS.
  Upon detection of RLF for a cell group, the operation of the cell group is suspended, i.e., service is interrupted or degraded.
  Recovery procedure is initiated via RRC re-establishment or, in case of DC, fast recovery. Until the recovery is completed, interruption or degraded service quality persists. Depending on the recovery procedure, UE may experience severe QoS degradation.
Predictive RLF Detection and Proactive Recovery
  Time domain measurement prediction capabilities enabled by UE’s ML capabilities allows UE to predict the occurrence of RLF in advance. Such predictive RLF detection can give new opportunity to avoid the pending RLF by triggering e.g., proactive failure reporting of mobility, rather than waiting for the RLF to just happen.
  By avoiding RLF via predictive RLF detection and proactive actions, quality of service can be significantly improved.
Predictive Beam Failure detection and Proactive Recovery
  Beam failure detection and BFR can be enhanced to predictive BFD and proactive BFR. Predictive BFD and proactive BFR can also improve QoS by avoiding beam interruption.
NR RLF
RSRP in ENDC (LTE B13 + NR FR2 n261) for mobile UE

## Slide 14: Extension of LCM and UE capabilities
ML-based model management for predictive mobility
  R18 ML-based model management is specific to RAN1 use cases
  In R19, extension of ML-based model management for predictive mobility is required
    For model management in LCM perspective (Model selection/(de)activation/switching/etc) based on predictive L3 measurement results and/or predictive mobility results
UE capability extension for predictive mobility
  Identification of necessary UE capabilities and network capabilities to enable predictive mobility
  Static/dynamic reporting of UE capabilities
  Inter-node capability propagation during UE mobility
General Framework for predictive mobility
Model Training
Management
Inference
Model Storage
Predictive
Measurement Results
Trained/Updated Model
Monitoring Data
Management Instruction (Model (de)activate, switching, etc.)
Training Data.
Model Transfer/Delivery
Data Collection
Predictive Measurement Results
HO Success/Failure
Predictive Mobility
Inference Data.

## Slide 15: Proposed objective for Predictive Mobility
Possible Work Plan for Predictive Mobility
  RAN2-led study in Rel-19, and corresponding normative work in Rel-20
Objectives for new use case - Predictive Mobility:
  1) To study requirement and functionalities to enable predictive mobility
    To study requirements and functionalities for predictive RRM measurements and measurement reporting
      Derivation of predictive measurements (L3 measurement for L3 HO and L1 measurements for LTM).
      Reporting condition for predictive measurement reporting.
    To study requirements and functionalities for predictive mobility triggering
      Predictive NW-triggered HO based on predictive measurement reporting is studied.
      Conditional HO based on predictive measurement evaluation is studied.
      Both UE and network side impacts need to be studied.
    To study requirements and functionalities for predictive RLM and proactive recovery
  2) To study ML-based model management for predictive mobility
    To study means for network to transfer/activate/deactivate/switch models for predictive mobility.
    To study means for network to evaluate the accuracy of predictive mobility
  3) UE capability extension for predictive mobility
    Identification of necessary UE capabilities and network capabilities to enable predictive mobility
    Static/dynamic reporting of UE capabilities
    Inter-node capability propagation during UE mobility

## Slide 16: Summary
Proposed work plan in Rel-19 AIML for air interface
  1) Normative work for use cases studied in Rel-18
  2) Study for new use case – Predictive Mobility
WI Objective for use cases studied in Rel-18 (RAN1-led)
  Specify enhanced UE capability framework to facilitate UE-side AI/ML operation (e.g. dynamic update of applicable UE functionality).
  Study and, if needed, specify CSI prediction (1st priority) or CSI compression with limited training collaboration type(s) (2nd priority).
  Specify spatial/temporal DL Tx beam prediction based on one-sided AI/ML model.
  Specify direct and AI/ML assisted positioning based on one-sided AI/ML model.
  Note: following aspects should be considered.
    Focus on signaling-based collaboration without model transfer (collaboration level y only).
    Focus on offline training only.
    Specification impact on
      Data collection without RS enhancement,
      Inference,
      Functionality/model based LCM operation
SI Objective for New use case – Predictive Mobility (RAN2-led)
  To study requirement and functionalities to enable predictive mobility
    To study requirements and functionalities for predictive RRM measurements and measurement reporting
    To study requirements and functionalities for predictive mobility triggering
    To study requirements and functionalities for predictive RLM and proactive recovery
  To study ML-based model management mechanism for predictive mobility
    To study means for network to evaluate the accuracy of predictive measurements
    To study means for network to activate/deactivate/switch predictive mobility.
  UE capability extension for predictive mobility