## Slide 1: Proposal on MIMO enhancements in Rel-19

## Slide 2: Overall Motivation
Further UL enhancement based on multi-panel UE
  UL is still a performance limiting factor of NR network.
  As indicated in the LSs from 5GAA to RAN in RWS-210360 and to RAN1 in R1-2205116 for MIMO-specific topics, UE multi-panel implementation is useful especially for various applications of vehicle UEs in FR1 as well as in FR2.
  In Rel-17/Rel-18 MIMO, UE multi-panel features such as panel-specific beam report, simultaneous Tx across multi-panel (STxMP), and panel/TRP-specific TA have been introduced to improve UL performance. However, these features are still under quite limited scope.

## Slide 3: Enhanced STxMP
Motivation
  Rel-18 STxMP supports limited combination only, i.e. PUSCH+PUSCH and PUCCH+PUCCH
  Rel-18 STxMP does not support asymmetric panel implementation, which is useful for vehicles (e.g. large panel(s) on upper body and small panel(s) on lower body)
  Rel-18 STxMP supports up to 2 panels and up to 4 layers only
  Rel-18 STxMP supports SFN scheme that does not provide coherent combining for URLLC applications
Scope
  Specify enhanced STxMP features to improve UL reliability and throughput
    Enhanced STxMP for various channel/RS combinations other than PUSCH+PUSCH and PUCCH+PUCCH
      Consider same or different channel/RS (e.g. SRS+SRS, PUCCH+PUSCH)
    Support of STxMP for UEs with asymmetric panel properties (e.g. different max layers per panel)
    Support of simultaneous transmission across more than 2 panels
    Support of STxMP with up to rank 8
    Support of coherent SFN STxMP

## Slide 4: Enhanced 2TA
Motivation
  Rel-18 2TA supports only with multi-DCI mTRP operation, while different TA for different panel/TRP is needed in any mTRP operation (e.g. dynamic TRP switching, sDCI mTRP, per-TRP CSI/beam reporting)
Scope
  Specify enhanced 2TA feature applicable in general mTRP operation
    2TA with S-DCI mTRP
    2TA for dynamic TRP switching (e.g. based on Rel-15 BM framework, Rel-18 uTCI framework)

## Slide 5: Enh for dynamic panel switching
Motivation
  Rel-17/18 panel-specific beam report does not support symmetric panels
  Current specification does not support dynamic SRS port number adaptation according to the panel-specific beam report
Scope
  Extension of panel-specific beam report for symmetric panels as well as for asymmetric panels
  Support of dynamic SRS port number adaptation for dynamic panel switching with asymmetric panels

## Slide 6: UL PT-RS enhancements
Motivation
  In order to support 8Tx UL operation and/or STxMP with more than 2 panels, up to 2 port UL PT-RS would not be sufficient to measure phase noise from different panels.
Scope
  Specify 3 and 4 UL PT-RS ports for more than 2 panel operation

## Slide 7: Proposed WI objective for Rel-19 MIMO
Enhanced STxMP features to improve UL reliability and throughput
  Enhanced STxMP for various channel/RS combinations other than PUSCH+PUSCH and PUCCH+PUCCH
  Support of STxMP for UEs with asymmetric panel properties
  Support of simultaneous transmission across more than 2 panels
  Support of STxMP with up to rank 8
  Support of coherent SFN STxMP
Enhanced 2TA feature
  Support of 2TA with S-DCI mTRP
  Support of 2TA for dynamic TRP switching
Enhancements for dynamic panel switching
  Extension of panel-specific beam report for symmetric panels
  Support of dynamic SRS port number adaptation for dynamic panel switching with asymmetric panels
UL PT-RS enhancement
  Specify up to 4 PT-RS ports