## Slide 1: Proposal on Duplex Evolution in Rel-19

## Slide 2: Background
Duplex evolution in Rel-18
  During the discussion on the initiation of Rel-18 SI on duplex evolution,
    Both subband-wise full duplex operation and spectrum shared full duplex operation were discussed [1]
    Enhancements for dynamic TDD operation to mitigate coexistence problem was discussed
  In the end, Rel-18 SI on duplex evolution [2] includes
    Duplex enhancement at gNB side assuming half duplex operation at UE side
    No restriction on frequency range
    SBFD and potential enhancements on dynamic/flexible TDD
  RAN WG1 has completed Rel-18 SI in September, 2023.
DL
UL
DL
Frequency
Subband-wise Full Duplex operation in Rel-19
DL
Carrier BW
UL
Frequency
Spectrum-shared Full Duplex operation for further study
Carrier BW
Notes: 현재 PSI 정보를 기반으로는 discard 만 수행할 것이다. 하지만 이걸로 충분하지 않고 PSI 기반의 reliability 및 prioritization을 해야 한다.
한줄로 표현될 수 있도록 하자. 기고의 observation 같이.

## Slide 3: Normative Work on Duplex Evolution
Motivation
  WI following Rel-18 SI should be introduced in Rel-19
  In general, evaluation results and technical discussion in Rel-18 shows sufficient gain and feasibility of SBFD operation
    At least for certain deployment scenarios and frequency ranges
    At least with certain gNB implementation, which is considered to be feasible by many companies
  Rel-19 WI on duplex evolution should reflect the study from Rel-18 SI [3]
    SBFD
      Supportable deployment scenarios and frequency ranges for semi-static SBFD operation
      Coverage Performance
      SBFD operation schemes
      Dynamic SBFD operations
      SBFD specific CLI handling schemes
    Dynamic/Flexible TDD
      CLI handling schemes for dynamic TDD and/or common for both SBFD and dynamic/flexible TDD
        Inter-gNB co-channel CLI handling schemes, Inter-UE co-channel CLI handling schemes
Notes: 현재 PSI 정보를 기반으로는 discard 만 수행할 것이다. 하지만 이걸로 충분하지 않고 PSI 기반의 reliability 및 prioritization을 해야 한다.
한줄로 표현될 수 있도록 하자. 기고의 observation 같이.

## Slide 4: Semi-static and/or Dynamic SBFD
Motivation
  For SBFD operation, bandwidth in SBFD symbol/slot is divided into DL subband and UL subband for simultaneous transmission and reception at gNB.
  Comparing between semi-static SBFD operation and static TDD, semi-static SBFD operation provides a benefit of UL performance enhancement, where the gain comes from assigning more UL resource. But, DL performance of semi-static SBFD operation is degraded due to the reduced DL resource.
  If switching SBFD symbol/slot into DL-only symbol/slot is allowed, the DL performance of SBFD can be compensated [4]. Furthermore, if switching SBFD symbol/slot into UL-only symbol/slot is allowed, further enhancement of UL performance can be achieved.
Scope
  Specify SBFD operation
    Support of semi-static/dynamic SBFD (SBFD symbol/slot time configuration, Subband configuration)
    Support of operation in SBFD symbol and non-SBFD symbol (FDRA, MCS, TBS, CSI-RS, CSI Measurement and reporting, PUCCH, SRS, Multi-antenna, CORESET, Search Space, PUSCH repetition, etc.)
    Support of UE behavior for supporting spectrum non-overlapped full duplex capable gNB (DL Rx and UL Tx, Timing advance, Power control, etc.)
Notes: 현재 PSI 정보를 기반으로는 discard 만 수행할 것이다. 하지만 이걸로 충분하지 않고 PSI 기반의 reliability 및 prioritization을 해야 한다.
한줄로 표현될 수 있도록 하자. 기고의 observation 같이.

## Slide 5: CLI handling for SBFD and/or dynamic TDD
Motivation
  For dynamic/flexible TDD, gNB-to-gNB co-channel CLI handling is required.
    Periodic NZP CSI-RS/SSB can be used for gNB-to-gNB co-channel CLI measurement and/or channel measurement.
    The knowledge among gNBs of semi-static SBFD time and frequency configuration can be used to determine whether CLI is existed in the resource.
    gNB can exchange beam related information among gNB(s) such as DL beam indication, preferred/non-preferred beam indication.
  For SBFD and dynamic/flexible TDD, UE-to-UE co-channel CLI handling is required.
    L1/L2 based CLI measurement and reporting provide benefits for inter-UE CLI handling.
      It can be optimized for short-term interference measurement and low latency.
      It can facilitate gNB adjusting UE scheduling for inter-UE CLI reduction.
    For L1/L2 UE-to-UE CLI measurement, followings can be considered.
      Periodic, semi-persistent, or aperiodic measurement resource
      Periodic, semi-persistent, or aperiodic reporting
Scope
  Specify co-channel CLI handling for SBFD and dynamic/flexible TDD
    Support of gNB-to-gNB CLI handling scheme (Co-channel CLI and/or channel measurement, Time/frequency resource coordination, Spatial domain coordination)
    Support of UE-to-UE CLI handling scheme (L1/L2 based CLI measurement and reporting including co-channel intra-/inter-subband CLI)
Notes: 현재 PSI 정보를 기반으로는 discard 만 수행할 것이다. 하지만 이걸로 충분하지 않고 PSI 기반의 reliability 및 prioritization을 해야 한다.
한줄로 표현될 수 있도록 하자. 기고의 observation 같이.

## Slide 6: Further Evolution beyond Duplex Evolution in Rel-18 SI
Motivation
  SBFD in Rel-18 SI follows conventional DL-UL resource separation in time-frequency domain
    Rel-18 SI excludes UE’s RF enhancements for full duplex operation
    Rel-18 SI considers limited enhancements for full duplex operation at gNB
  Further diverging service/traffic types require more flexible utilization of radio resources with reduced latency
    Full duplex (spectrum shared simultaneous DL-UL transmission/reception) operation within a carrier can be a strong candidate for further duplex enhancement
      Further enhancement at gNB implementation for full duplex operation (and at UE side as well) can be considered
  Therefore, spectrum shared full duplex (SSFD) operation can be studied in further releases as further evolution beyond duplex evolution studied in Rel-18
DL
UL
F
DL
&
UL
Guard
F
T
T
F
T
Half duplex operation
(Conventional)
SBFD operation
(Rel-18 SI)
SSFD operation
(Further evolution)
Notes: 현재 PSI 정보를 기반으로는 discard 만 수행할 것이다. 하지만 이걸로 충분하지 않고 PSI 기반의 reliability 및 prioritization을 해야 한다.
한줄로 표현될 수 있도록 하자. 기고의 observation 같이.

## Slide 7: Proposal
Rel-19 WI on duplex evolution may includes the following objectives
  SBFD operation
    Semi-static/dynamic SBFD (SBFD symbol/slot time configuration, Subband configuration)
    Operation in SBFD symbol and non-SBFD symbol (FDRA, MCS, TBS, CSI-RS, CSI Measurement and reporting, PUCCH, SRS, Multi-antenna, CORESET, Search Space, PUSCH repetition, etc.)
    UE behavior for supporting spectrum non-overlapped full duplex capable gNB (DL Rx and UL Tx, Timing advance, Power control, etc.)
  Co-channel CLI handling schemes for SBFD and dynamic/flexible TDD
    gNB-to-gNB CLI handling schemes (Co-channel CLI and/or channel measurement, Time/frequency resource coordination, Spatial domain coordination)
    UE-to-UE CLI handling schemes (L1/L2 based CLI measurement and reporting including co-channel intra-/inter-subband CLI)
Study for further duplex evolution beyond Rel-18 study can be considered
  Further duplex evolution beyond Rel-18 study may consist of study on the spectrum shared full duplex operation
  Considering the reasonable work load of Rel-19,
    Further duplex evolution may be considered as future study (e.g., in Rel-20) while Rel-19 focuses on normative work following Rel-18 SI on duplex evolution
Notes: 현재 PSI 정보를 기반으로는 discard 만 수행할 것이다. 하지만 이걸로 충분하지 않고 PSI 기반의 reliability 및 prioritization을 해야 한다.
한줄로 표현될 수 있도록 하자. 기고의 observation 같이.

## Slide 8: References
  [1] RWS-210242, “Proposal on the work scope of Rel-18 SI for full duplex operation”, LG Electronics, KT Corp., SK Telecom, Fraunhofer, CEWiT, IITM, ETRI
  [2] RP-213591, “New SI: Study on evolution of NR duplex operation”, CMCC (moderator)
  [3] R1-232412, “TR 38.858 v1.0.0 for study on evolution of NR duplex operation”, CMCC
  [4] R1-2305383, “Study on Evaluation for NR duplex evolution”, LG Electronics
Notes: 현재 PSI 정보를 기반으로는 discard 만 수행할 것이다. 하지만 이걸로 충분하지 않고 PSI 기반의 reliability 및 prioritization을 해야 한다.
한줄로 표현될 수 있도록 하자. 기고의 observation 같이.