## Slide 1: Proposal on network energy saving in Rel-19
3GPP TSG RAN Meeting #101
Bangalore, India, September 11-15, 2023
Agenda Item: 8A.2.5
RP-232196

## Slide 2: Background
During Rel-18 NW Energy Saving (NES) SI phase, various T/F/S/P-domain NES techniques were studied, as enumerated below.
Considering impacts on legacy NR UEs and performance analysis, some NES techniques (i.e., B-1-1, A-4, C-1, D-1 techniques) out of studied ones are included in Rel-18 NES WID.
Domain | Technique
Time | A-1: Adapting transmission/reception of common channels/signals A-1-1: Simplified SSB without PBCH or with partial PBCH A-1-2: Skipping of SSB/SIB1 transmission occasion A-1-3: Configuration/adaptation of longer periodicity of SSB/SIB1 and/or uplink random access opportunities A-1-4: Adapting paging or SSB transmission patterns A-1-5: Dynamically adapting PRACH periodicity and occasions A-1-6: Scheduling of SIB1 without PDCCH
 | A-2: Adaptation of UE specific signals and channels
 | A-3: UE wake up signal (WUS) for gNB A-3-1: UE WUS triggering gNB for SSB/SIB/RACH A-3-2: UE WUS triggering gNB to wake up in case of uplink traffic arrival
 | A-4: Adaptation of DTX/DRX
 | A-5: Adaptation of SSB/SIB1 A-5-1: SSB- and/or SIB1-less operation for non-CA A-5-2: On-demand SSB/SIB1
Domain | Technique
Frequency | B-1: Multi-carrier energy savings enhancements B-1-1: SSB- and/or SIB1-less operation for inter-band CA B-1-2: Dynamic UE-group PCell switching
 | B-2: Adaptation of bandwidth part of UE(s) within a carrier
 | B-3: Adaptation of bandwidth of UE(s) within a BWP
Spatial | C-1: Adaptation of spatial elements
 | C-2: Adaptation of TRPs in mTRP operation
Power | D-1: Adaptation of transmission power of signals and channels
 | D-2: Over the air digital pre-distortion
 | D-3: Tone reservation
 | D-4: PA power bias adaptation
 | D-5: UE post-distortion
Notes: 현재 PSI 정보를 기반으로는 discard 만 수행할 것이다. 하지만 이걸로 충분하지 않고 PSI 기반의 reliability 및 prioritization을 해야 한다.
한줄로 표현될 수 있도록 하자. 기고의 observation 같이.

## Slide 3: Motivation (1)
Rel-18 NES WI introduces spatial domain techniques focusing on single TRP operation.
For adaptation of TRPs in multi-TRP operation (C-2 technique),
  Substantial network energy saving gain has been shown during NES SI phase.
  As captured in TR 38.864, no impact for legacy UEs is foreseen if the adaptation technique is used on a UE-specific basis.
To enable efficient adaptation of TRPs, the enhancements of CSI, TCI, beam management and repetition related procedures can be considered in Rel-19.
Multi-TRP operation with enhanced NES
Notes: 현재 PSI 정보를 기반으로는 discard 만 수행할 것이다. 하지만 이걸로 충분하지 않고 PSI 기반의 reliability 및 prioritization을 해야 한다.
한줄로 표현될 수 있도록 하자. 기고의 observation 같이.

## Slide 4: Motivation (2)
Rel-18 NES SI/WI has been initially considered/evaluated assuming deployment scenario without NCR.
To make NES feature more versatile, support of NES can be extended to additional scenario/deployment such as NCR.
The following aspects can be considered to support NES techniques under NCR deployment:
  Backhaul/control link behavior for efficient interaction between NES-capable gNB and associated NCR, to consider the case where the gNB would operate with S/P-domain adaptation or cell DTX/DRX adaptation for NW energy saving
Notes: 현재 PSI 정보를 기반으로는 discard 만 수행할 것이다. 하지만 이걸로 충분하지 않고 PSI 기반의 reliability 및 prioritization을 해야 한다.
한줄로 표현될 수 있도록 하자. 기고의 observation 같이.

## Slide 5: Motivation (3)
In addition, the following Rel-18 leftover items can be considered in Rel-19.
  CSI overhead/complexity reduction for SD/PD adaptation
    For example, configure common or differential report across sub-configurations for a CSI quantity
  TCI configuration enhancement for SD/PD adaptation
    For example, configure multiple candidate QCL-reference RSs or multiple candidate sets of TCI state
  Beam management enhancement for SD/PD adaptation
    For example, adjust UE’s RX beam and/or number of repetitions for the CSI-RS configured for BM
  PUCCH resource adaptation for SD/PD adaptation
    For example, use different PUCCH resource according to the number of activated sub-configurations
Notes: 현재 PSI 정보를 기반으로는 discard 만 수행할 것이다. 하지만 이걸로 충분하지 않고 PSI 기반의 reliability 및 prioritization을 해야 한다.
한줄로 표현될 수 있도록 하자. 기고의 observation 같이.

## Slide 6: Proposal on network energy saving in Rel-19
Dynamic TRP adaptation (on/off) mechanism for NW energy savings in multi-TRP operation
  Enhancements of CSI, TCI, beam management and repetition related procedures to enable efficient adaptation of TRPs
Enhancement to support NES techniques under NCR deployment considering:
  Backhaul/control link behavior for efficient interaction between NES-capable gNB and associated NCR
Leftover issues of Rel-18 NES
  CSI overhead/complexity reduction for SD/PD adaptation
  TCI configuration enhancement for SD/PD adaptation
  Beam management enhancement for SD/PD adaptation
  PUCCH resource adaptation for SD/PD adaptation