## Slide 1: Proposal on positioning enhancements in Rel-19
3GPP TSG RAN Meeting #101
Bangalore, India, September 11-15, 2023
Agenda item: 8A.2.12.4
RP-232198

## Slide 2: Introduction
Rel-18
SL ranging/positioning
Higher accuracy (No target)
  CPP
  Bandwidth aggregation
Power efficiency
FH for RedCap positioning
RAT-dependent Integrity
Potential enhancements
in Rel-19
Higher accuracy with reliable performance
  CPP enhancement [< x cm (90%)]
  SL positioning in U-band
Enhanced positioning methods and new positioning framework introduced in Rel-18
  In Rel-18 several enhanced positioning methods including CPP, LPHAP, and bandwidth aggregation are introduced for achieving higher accuracy and/or power efficiency
  In Rel-18 new positioning framework including Sidelink positioning and RedCap positioning are introduced.
  Only essential issues has been treated and some leftover issues are remained.
Highlights of Rel-19 positioning enhancements in Rel-19 workshop
  The positioning enhancements is categorized as an additional RAN1-led candidate topic.
  Several proposals for positioning enhancement in Rel-19 was discussed during the Rel-19 workshop. Based on the inputs from the proponents, following topics are supported for majority, and can be considered as high priority items for Rel-19 positioning enhancements.
    CPP enhancements
    Sidelink positioning enhancements
Rel-17
Higher accuracy
  <1m (90%) for commercial
  <0.2m (90%) for IIoT
Low latency location
Network/Device efficiency
GNSS positioning integrity
Rel-16
Introduce NR RAT-dependent positioning methods
For commercial use cases <3m (80%) for indoor <10m (80%) for outdoor
Notes: 현재 PSI 정보를 기반으로는 discard 만 수행할 것이다. 하지만 이걸로 충분하지 않고 PSI 기반의 reliability 및 prioritization을 해야 한다.
한줄로 표현될 수 있도록 하자. 기고의 observation 같이.

## Slide 3: Carrier Phase Positioning Enhancement
Motivation
  Rel-18 positioning introduces basic features to enhance positioning accuracy based on CPP.
  Further enhancements on the positioning accuracy for various scenarios is necessary.
  Multi-measurements
    During Rel-18, several multi-measurements based approach for CPP has been discussed
      RSCPs/RSCPDs on multiple carriers within a PFL  Integer ambiguity resolution
      Multi-shot RSCP/RSCPD reporting  Accuracy improvement / Tracking
      Additional path reporting  Multipath mitigation
    For reliable CPP performance, the multi-measurements based approaches are highly desirable
  PRU specific signaling and behavior
    Only basic features (e.g. simultaneous measurement/transmission) for PRU assisted CPP are specified in Rel-18.
    Several aspects, including positioning accuracy and resource overhead/complexity reduction, needs to be considered further for more efficient PRU supports.
  Other remaining issues
    Narrowband CPP (e.g. CPP for RedCap UEs)
    Support for standalone reporting of carrier phase measurements
Objective
  Enhancement on signaling and measurement report for the carrier phase positioning
    Specify multi-measurements reporting (in time/frequency domain)
    Study and specify PRU specific enhancements (including signaling, measurements and reporting)
    Other remaining issues (e.g. standalone CPP, RedCap CPP)
Fig. 1 PRU specific signaling and behavior
Fig. 2 Rel-18 CPP performance with 20MHz BW
Notes: 현재 PSI 정보를 기반으로는 discard 만 수행할 것이다. 하지만 이걸로 충분하지 않고 PSI 기반의 reliability 및 prioritization을 해야 한다.
한줄로 표현될 수 있도록 하자. 기고의 observation 같이.

## Slide 4: Sidelink Positioning in Unlicensed Band
Motivation
  There are increasing demands for commercial use cases e.g. a positioning service in home environment.
  Rel.18 SL positioning needs to be enhanced for providing a better location-based service.
  Large bandwidth and spectrum availability are huddle for high accuracy positioning in the licensed band.
  Location-based service should be available even in out-of-network-coverage area.
  Rel-18 sidelink positioning is focused on ITS dedicated and FR1 licensed bands, where the supported bandwidth may not be sufficient for achieving such high accuracy positioning requirements.
Objective
  Support sidelink positioning using FR1 unlicensed band
    Unlicensed band can provide enhanced accuracy due to wide bandwidth.
    Rel.18 SL-U channel access and the physical layer structure is reused as much as possible
Notes: 현재 PSI 정보를 기반으로는 discard 만 수행할 것이다. 하지만 이걸로 충분하지 않고 PSI 기반의 reliability 및 prioritization을 해야 한다.
한줄로 표현될 수 있도록 하자. 기고의 observation 같이.

## Slide 5: Summary
Carrier Phase Positioning Enhancement
  Enhancement on signaling and measurement report for the carrier phase positioning
    Specify multi-measurements reporting (in time/frequency domain)
    Study and specify PRU specific enhancements (including signaling, measurements and reporting)
    Other remaining issues (e.g. standalone CPP, RedCap CPP)
Sidelink Positioning in Unlicensed Band
  Support sidelink positioning using FR1 unlicensed band
    Unlicensed band can provide enhanced accuracy due to wide bandwidth.
    Rel.18 SL-U channel access and the physical layer structure is reused as much as possible
Notes: 현재 PSI 정보를 기반으로는 discard 만 수행할 것이다. 하지만 이걸로 충분하지 않고 PSI 기반의 reliability 및 prioritization을 해야 한다.
한줄로 표현될 수 있도록 하자. 기고의 observation 같이.