## Slide 1
0
Views on Ambient IoT
September 2023
3GPP TSG RAN #101 RP-232207
Bangalore, India, September 11-15, 2023
Agenda Item: 8A.2.4
Source: CMCC
Type: Discussion

## Slide 2
Summary
Use case/deployment/device type/others
Work plan for Rel-19
SI/WI objective for Rel-19
Content

## Slide 3
RAN level SI has studied on the following key topics and all captured in TR 38.848 for further study
4 representative use cases, 3 categories of devices, 4 RAN connectivity topologies，
Continuing finalizing the remaining RAN design targets section, any further comparison and assessment
Status quo of Rel-18 AIoT SI
Summary
Timeline: Strong interests from industrial, to meet the demands of vertical customers more expeditiously, by the end of 2025 Q4.
SI/WI: A follow up WG SI/WI is expected to start in Rel-19 with 9 month SI + 9 month WI
Target: The new IoT technology shall provide cost and power consumption much lower than the existing NB-IoT and eMTC technologies, and thus is not to be a replacement for them.
Deployment
  Topology 1 and 2 for licensed band should be prioritized for consideration.
  All standalone, in-band and guard-band operation can be considered.
Device type
  Strive for common design part for Device A/B/C as much as possible and complete specification within Rel-19.
Use cases：for Rel-19, inventory can be considered as basic use case, while it can also work for sensor and activator/command. Study of positioning is of interests.
Coverage
  Device B/C, target for comparable coverage to the current NR bottleneck. Tradeoff between coverage and complexity/power consumption is necessary.
  Device A, strive for good coverage for topology 1 as much as possible and good proximity coverage for topology 2 (? meter)
Additional highlighted point for R19 SI/WI

## Slide 4
IoT use case
Use case category | Use Cases identified in TR 22.840 by SA1 | Max E2E latency | Communication Range | Positioning Accuracy | Data Rate | Message Size | Device density | Device speed
inventory | 1; 2; 5; 7; 16; 21; 24; 27 | ~1s | 30 m (indoor) | 3 m, 90% | <1000 bits/s | <256 bit | 1.5 million per km2 | < 6 km/h
sensor | 3; 6; 11; 13; 15; 18; 19; 20; 22; 23; 24; 25; 26 | 1~30s | 50 m (indoor), 200 m(outdoor) | NA | <1000 bits/s | <100 bytes | 1000 per km2 | Static
Positioning | 2; 4; 7; 8; 9; 10; 12; 14; 16; 24; 27 | 1~10s | 50 m (indoor), 200 m(outdoor) | 1~3 m, 90% | <1000 bits/s | 256 bits | 1000 per km2 | 5 km/h (indoor) 20 km/h (outdoor)
Activator/command | 17; 28 | NA | NA | NA | NA | NA | NA | NA
Use cases
Whether to include all the 4 use cases into R19 WG SI?
  TR 38.848 captured the following representative use cases: Inventory; sensors; positioning; activator.
Observation: Inventory and sensor use case share similar requirements except message size, while positioning requires specific design on L1/L2 signaling and architecture
Proposal 1: Similar as taking eMBB as 5G design baseline, use case of inventory can be considered as basic use case for ambient IoT design. The design can compatiable with sensor and activator, while positioning use cases are considered for study as technical enhancement on top of baseline.

## Slide 5
Deployment (1)
Topology 1
Topology 2
Topology 3a with downlink assistance
Topology 3b with uplink assistance
Topology 4
TR 38.848 captured the following 5 topologies, Whether all the RAN topologies will be included in R19 WG SI?
Proposal 2: Design a unified ambient-link interface applicable for topology 1 & 2, which guarantees the ambient IoT device can access to either gNB or intermediate node. Other topologies are de-prioritized in Rel-19.
Topologies

## Slide 6
Deployment (2)
Spectrum and deployment
The following operations flexible deployment are to be considered,
  Mode A (in-band operation): Frequency bands in licensed spectrum, coexistence with UEs and infrastructure in frequency bands for NR
  Mode B (standalone operation) : Frequency bands in licensed spectrum, standalone operation in a narrow BW outside the NR carrier.
    Mode B-1: no additional GB needed among A-IoT CCs
    Mode B-2: additional GB needed among A-IoT CCs
  Mode C (guard-band operation): Frequency bands in licensed spectrum, standalone operation in a narrow BW in the guard-band of NR.
  Questions: Discuss which mode the device type can be supported?
Proposal 3： Both standalone (with/without additional GB among CCs), in-band and guard-band operation in licensed spectrum is supported.

## Slide 7
Design options for passive and active device
Option 1: Take passive device design as basic. Then reuse designs for semi-passive and active device design as much as possible.
Option 2: Take active device design as basic. Then reuse designs for semi-passive and active device as much as possible
Option 3: Parallel and strive for common design for passive/semi-passive and active device as much as possible.
Observations:
If active device is to be studied in Rel-19, it should be limited to reuse the basic design of passive device as much as possible, at least for PHY UL/DL shared channel and L2/3 procedures.
To minimize the study and standardization work, the first release can focus on the basic and common part for passive device and active device.
Strive for option 3 to allow A-IoT much broader usage in future.
Clear and significant differences between active device (device C) and existing NB-IoT/eMTC devices, not to be replacement of them.
Proposal 4:
  Passive/semi-passive/active device are recommended to be studied and specified in Rel-19 design.
  Strive for common design for passive/semi-passive and active device as much as possible
  If active device will be specified in Rel-19, the air interface design for active device should reuse the design of passive/semi-passive as much as possible.
Device categories
Ambient IoT Device categories
7

## Slide 8
Other aspects
Coverage improvement - Power pooling and multiple site
The following coverage target can be considered
Device B/C, target for comparable coverage to the current NR bottleneck. Tradeoff between coverage and complexity/power consumption is necessary.
Device A, strive for good coverage for topology 1 as much as possible and good proximity coverage for topology 2 (30~50 meter)
Multiple site (gNB/TRP)
Mainly used for RF energy harvesting coverage improvement purpose when there is not lots of site coordination/backhauling
Can be used for data coverage boosting if sufficient site coordination exists.
Power pooling
Study the gNB power pooling techniques to boost the coverage of the both RF energy harvesting and data receiving coverage
  Note: the data rate and latency may be degraded due to longer time to harvesting energy and Tx/Rx data.
Energy harvesting
Optimize energy harvesting procedure to enable communication protocol matching with A-IoT device energy storage/discharge
Assistant information of tag status reporting, e.g., state of charge,…
Mobility
Necessary enhancement to support A-IoT device measurement based on LP-SS, at least for serving-cell
  Evaluate LP-RSRP/RSRQ accuracy
  Necessary procedures to support measurement
Proposal 5: Study and specify the following aspects for A-IoT at least for device A/B
  Study the gNB power pooling techniques to boost the coverage of the both RF energy harvesting and data receiving coverage
  Energy harvesting procedure to enable communication protocol matching with A-IoT device energy storage/discharge and related assistant information.
  Necessary enhancement to support A-IoT device measurement based on LP-SS at least for serving-cell
  Single site operation is baseline, and multiple site (gNB/TRP) operation can be considered.

## Slide 9
Work plan
SA1
Q1
Q2
Q3
Q4
Q1
Q2
Q3
Q4
Q1
Q2
Q3
Q4
Rel-18
R18 L1 Start
R18 R1
Func. Freeze
R18 R2/3/4
Func. Freeze
R18 ASN.1
Freeze
Rel-19
Q1
Q2
Q3
R19 R2/3/4
Func. Freeze
R19 R1
Func. Freeze
2023.9 R19 L1 Start
SA1 R19 SI: Study on Ambient power-enabled Internet of Things
Start@SA1#97
R18 A-IoT RAN level SI
R19 A-IoT SA2 SI
A-IoT SA2 WI
RAN
SA2
R19 A-IoT RAN1/2/3/4 SI
RAN WG
Complete before Jun 2023
A-IoT RAN1/2/3/4 WI
2022
2023
2024
Approved@RAN#97
TBD
TBD
2025
Option 1: 18 month SI in Rel-19. To study all the 4 key use cases, 3 categories and topology 1&2.
Option 2: 9 month SI + 9 month WI in Rel-19. Focus only on the common and basic functions for passive device. The benefit is to meet the urgent market requirement at 2025.
  Proposal 6: We propose to have a 9 month SI + 9 month WI in Rel-19, with such scope：
      focus on the basic and common design for inventory use case, passive device and common ambient-link air interface for topology 1&2.
      If active device is considered into the scope, strive for common design to passive device as much as possible

## Slide 10
Ambient IoT SI/WI Objectives
Identify evaluation methodology and KPIs based on RAN design target (SI only, RAN1)
  Target power/coverage/sensitivity/battery life/massive connection density for each device type
  Evaluation methodologies and results to be provided, including performance and coverage evaluation by considering appropriate scenarios/topology, impairment model and to analysis whether the AIoT can satisfy the coverage target.
Device hardware architecture(SI only, RAN1/RAN4)
  Device architecture for each device type
Study and specify necessary physical layer aspects, focusing on the basic and common design for inventory use case, passive device and common ambient-link air interface for topology 1&2, including (RAN1/RAN2)
  Waveform/numerology/modulation/frame structure/coding
  Basic DL/UL physical channels
  Necessary L1 procedures
Study and specify necessary L2/L3 control plane and user plane for passive device, including (RAN2)
  minimum CP functions, e.g., access/collision control, paging, security, mobility management
  minimum UP protocol layer and procedures, e.g., RLC/PDCP-less protocol, random access, packet structure
Study on the RAN architecture, including either gNB or UE act as reader, with/without CN connection (RAN3)
Coexistence with UEs and infrastructure with existing 3GPP technologies, e.g., LTE, NR, NB-IoT (RAN4/RAN1)
Study on the spectrum for Ambient-IoT (RAN4)
Study and specify necessary enhancement to support A-IoT device measurement based on LP-SS, at least for serving-cell (RAN4/1/2)
  Measurement accuracy and criteria (RAN4)
  Necessary procedures to support measurement (RAN2)

## Slide 11
Thank you!