## Slide 1
0
September 2023
NR NTN evolution in R19
3GPP TSG RAN #101 RP-232210
Bangalore, India, September 11-15, 2023
Agenda Item: 8A.2.7
Source: CMCC
Type: Discussion

## Slide 2
Motivations
In R17&R18, only transparent payload is considered. However, regenerative architecture can bring the following benefits:
  propagation delay reduction in Uu
  data communication could use ISL(inter-satellite link), which is even applied to less NTN Gateway scenarios
  regenerative architecture networking is more flexible and easier forward compatibility, e.g. supporting of more sparse locations of feeder links.
Regenerative payload with ISL
Support regenerative payload to reduce propagation delay (RAN3)
  study Full gNB on board
  study only DU on board (be de-prioritize）
  QoS split during the involved links
Potential Objectives
Field of view of the satellite (or UAS platform)
Satellite
(or UAS platform)
Satellite
(or UAS platform)
Feeder link
(mandatory if no ISL)
Feeder link
Fig. Non-terrestrial network typical scenario and network architecture with regenerative payload

## Slide 3
Motivations
The satellite (or UAS platform) typically generates several beams over a given service area：
  Considering a small difference in signal strength between two beams in a region of overlap, a new triggering for beam switching can be studied，e.g. location/time-based triggering for conditional beam switching
  Considering the large cell size of NTN, many devices may be served within a single beam. Depending on constellation assumptions (e.g. propagation delay and satellite speed) and UE density, many UEs may need to perform beam switching at a given time, a possible group beam switching command can be studied to reduce signalling overhead
Considerging the coverage area of NTN is much larger than that of TN, the beam number within one satellite is large but also limited.
  Only limited area can be covered by the beam due to limited transmission capabilty of satellite. And a large portion of the service area is not covered at the same time, e.g. suppose total beam units of one satellite is 1024, while there are only 128 beams for signalling/data transmission simultaneously, it is essential to study how to achieve full coverage as soon as possible .
Multiple beam operation in NTN
    Support multiple beam operation in NTN (RAN2,RAN1)
  Beam management and reporting over the multiple beams from the satellite
    e.g. location/time-based triggering for (group) conditional beam switching
  The enhancements for beam management in case of limited beam coverage
    reducing the CSI-RS feedback reporting
Potential Objectives
Fig. same PCI for several satellite beams
Unit
Unit
Unit
Unit
Unit
Unit
Unit
Unit
Unit
Unit
Unit
Unit
Unit
Unit
Unit
Beam Sweeping

## Slide 4
Motivations/Background
In Rel-18, satellite switching without PCI change was supported to reduce the UE complexity and power consumption during the satellite switching.
  Hard satellite switching
    In RAN1#113, satellite switching without PCI change was considered as feasible for hard satellite switching. And RAN2 has began the work based on the context of hard satellite switching.
  Soft satellite switching
    In RAN1#114 meeting, it was concluded that the soft satellite switching is also feasible based on some conditions.
    Due to limited TU, no further technical discussion was carried out in RAN1
    Under those conditions, the same UE behavior was assumed for both hard satellite switching and soft satellite switching.
NTN Mobility enhancement for PCI unchanged

## Slide 5
Further consideration for supporting soft switching without PCI changed
SSB collisions and measurements were observed during the discussion. Limited standard efforts can solve the issue and reduce the complexity of implementation.
  For SSB collisions, “Interference avoidance/mitigation between two satellites may potentially be done by gNB implementation at least to ensure non-colliding SSB with same PCI at UE side.”, This can be achieved, e.g., by assigning different SSB index for different satellites. Then legacy UEs can be operated for PCI unchanged. However, further investigations on the feasibility is expected, including performance and potential specification impact.
  For measurement,
    The following behaviors are assumed from RAN1 considerations
      #1: UE is provided with the information on new common TA, K_mac, ephemeris and cell-specific K-offset are applied during resynchronization to new satellite.
      #2: UE may be provided with the information if needed to detect the SSB of the new satellite for soft satellite switching.
    Assumption #1 is compatible for legacy UEs for PCI unchanged deployment.
    Assumption #2 is not compatible for legacy UEs. Since legacy UE does not have these new information. Such that legacy UEs cannot detect the new satellite for soft satellite switching. New UEs should be OK to operate so.
    In addition, considering the HO case of TN to NTN which is less discussed in R17/R18, mobility enhancements for this case are expected to be further considered.
NTN Mobility enhancement for PCI unchanged
Mobility enhancements [RAN2, RAN4, RAN1]
  For soft satellite switching without PCI change in quasi-earth fixed cell case,
    Specify necessary enhancements of UE measurements that allows more detections of the satellites within the PCI unchanged area. [RAN2, RAN4]
    Study performance impact of SSB collisions and potential specification impact, specify techniques according to the outcomes. [RAN1, RAN2]
  Study and specify mobility enhancements for some new cases, e.g., TN-NTN mobility with QoS adaptation(e.g. PDB relax due to long RTT). [RAN2, RAN1]
Potential Objectives

## Slide 6
Motivations
Rel-18 only focus on UL channel coverage enancements for NTN scenarios to support commercial smartphones services
Considering the NTN characteristics including large propagation delay and potential limited DL transmit power, potential issues and enhancements of DL coverage should be further studied.
DL coverage enhancement
Study and specify NR NTN-specific DL coverage enhancements in Rel-19(RAN1,RAN4,RAN2)
  Coverage performance evaluation:
    Identify the bottleneck of DL channels and the coverage gap
      Working scenarios should be first identified.
      Option 1:
        Reuse the Rel-18 evaluations as much as possible
        Limited additional evaluations required
      Option 2:
        New evaluations with fully aligned assumptions
  Study and specify DL coverage enhancements, at least for NTN
    DL beam enhancements, repetition, etc.
Potential Objectives
During Rel-18 NTN, DL coverage performance of PDSCH (for VoIP, low data rate, Msg2, Msg4), PDCCH, SSB have been evaluated.
  DL coverage limitations was observed during the evaluations, e.g. Msg4 PDSCH (2.2~2.8dB gap) in the LEO scenarios, PDCCH without repetition (1.9~2.6dB gap) in the NLOS scenarios for LEO.
DL coverage will be significantly restricted if the satellite transmission power is limited.
Potential issues

## Slide 7
Motivations
In R18, regarding network verified UE location, we focus on single satellite and existing LCS framework for verification.
For R19, we could further consider multiple satellites case to purse more accurate UE positioning calculation considering the positioning inaccuracy issue due to long propagation delay in single satellite case of NTN system.
Network verified UE location enhancements
Support network verified UE location enhancements (RAN1, RAN2)
  study multiple satellites for network verified UE location (e.g., satellite-specific assistant information to LMF)
Potential Objectives

## Slide 8
THANK YOU !