## Slide 1
0
Considerations on XR enhancement for Rel-19
3GPP TSG RAN RP#101 RP-232212
Bangalore, Sept. 11th-15th, 2023
Agenda Item: | 8A.2.8
Source: | CMCC
Document for: | Discussion

## Slide 2
Motivation
R18 SI/WI leftover
  Enhancement for XR capacity and power saving
R19 XR feature
  Support for Multi-modal traffic flow
  Support for XR-specific RRM measurement enhancement
  Support for XR-specific latency and reliability enhancement
Content

## Slide 3
Motivation
General observations
Rel-18 SI/WI leftover： Rel-18 XR enhancement focus on video data. The requirements of other component, e.g., audio, haptic and movement were not fully considered. Due to time constraints, Rel-18 XR SI/WI only focused on a limited scope. There is a need to continue Rel-18 work, i.e., power saving and capacity in Rel-19. Fully study on XR awareness, e.g., QoS flow coordination and inter-PDU set dependency. Rel-19 XR feature: The growth of XR traffic in the future will impose more stringent requirements on device power consumption and network capacity. New traffic flow may be added to XR service ,e.g., haptic data from XR glove, in Rel-19. Further research is essential on new topics, e.g., multi-modal, mobility and XR-specific RRM measurement, etc.

## Slide 4
Rel-18 SI/WI leftover: Capacity and power saving
Background
Background : Capacity improvements for XR in Rel-18 mainly focus on BSR, CG and discarding. With DSR introduced in Rel-18, the corresponding LCP and delay-aware scheduling mechanism require considerations. Gaussian BSR table has the least quantization error for video frame, but not exploited in Rel-18. For PDU set discarding, PUSCH skipping can be exploited for DG to avoid unnecessary uplink transmission.
Study further capacity and power saving enhancement for XR [RAN1, RAN2] Introduce Gaussian BSR table for less quantization error. Identify assistance information and PDU set information transferring mechanism to support XR in NR-DC. Specify LCP enhancement based on delay status for delay-aware scheduling. Specify PUSCH skipping for unnecessary uplink transmission caused by discard operation.
Objective
1080p@60fps, using NVENC

## Slide 5
Rel-19 new feature: Multi-modal flows
Background
For multiple flows, inter-flow synchronization and coordination of one UE is necessary due to separate devices connected to one terminal, e.g., separate glove and glass, and multi-camera capture. For single UE, synchronization and coordination of QoS flows is also needed. Can be studied in inter-PDU dependency.
Study multi-modal related enhancement for XR [RAN1, RAN2, RAN3] Specify inter-PDU set dependency for integrity scheduling and differentiate scheduling e.g. the UE will prioritize multiplexing the data in one PDU set into same MAC PDU(s) e.g. he UE will prioritize multiplexing an retransmission and a new transmission of another data of one PDU set into same MAC PDU(s) Specify coordination among QoS flow form the same XR instance. Specify inter-PDU set discard enhancement. Specify inter-flows synchronization and coordination. Specify scheduling enhancement for data transmission alignment, e.g. LCP enhancement, DCI shceduling enhancement. Specify further assistance information for multi-modal.
Objective
Multi-modal Data: Multi-modal Data is defined to describe the input data from different kinds of devices/sensors or the output data to different kinds of destinations (e.g. one or more UEs) required for the same task or application. Multi-modal Data consists of more than one Single-modal Data, and there is strong dependency among each Single-modal Data. Single-modal Data can be seen as one type of data.

## Slide 6
Rel-19 new feature: RRM measurement
Background
Measurement gap is introduced for UE that cannot perform RRM measurement and data reception/transmission simultaneously. In FR2, UE may needs MG for intra-frequency measurement. Measurement gap and SMTC configuration can cause sensible capacity and latency deterioration for XR user. RRM measurement is essential for UE in the edge of cellular or with high mobility
Study RRM measurement related enhancement for XR [RAN1, RAN2, RAN4] Specify conditional RRM measurement relaxing. Specify scheduling enhancement to ensure RRM measurement for high-mob UE with minimal capacity and latency deterioration.
Objective

## Slide 7
Rel-19 new feature: Latency and reliability
Background
Due to potential introduction of frequent generated small packet, i.e., haptic data and existing audio data, ensuring latency and reliability is necessary for guaranteeing user experience. Latency requirements demand new challenges due to high data rate. Introduction of retransmission-less CG (HARQ Mode B) in XR benefits power consumption but causes delayed retransmission of HMD pose and movement information. Can cause dizziness for XR user. Introduction of PSI causes different reliability requirements for PDU sets, requiring corresponding reliable transmission mechanism, especially when mixed PDU sets multiplexed in same TB.
Study latency and reliability enhancement for XR [RAN1, RAN2, RAN3] Specify latency enhancement for frequent small packet e.g., movement and haptic, to reduce RTT, e.g. coordination of UL and DL transmission and C-DRX configuration. Specify reliability enhancement for mixed XR traffic flow with different PSI.
Objective

## Slide 8
Thank you!