## Slide 1: NR coverage enhancements for Rel-19
China Telecom, Orange, Xiaomi, New H3C, TCL
Sept. 2023
3GPP TSG RAN Meeting #101
Bangalore, India, September 11-15, 2023
Agenda:8A.2.12.3
RP-232265

## Slide 2: Rel-17/18 coverage enhancements
  In Rel-17, following features are specified for NR coverage enhancements
  PUSCH enhancements: maximum number of repetition up to 32, available slot counting, TBoMS, DMRS bundling, inter-slot frequency hopping with DMRS bundling
  PUCCH enhancements: dynamic repetition indication, DMRS bundling, inter-slot frequency hopping with DMRS bundling
  Type A PUSCH repetitions for Msg3
  In Rel-18, following features are being studied/specified for NR coverage enhancements
  PRACH enhancement: multiple PRACH transmissions w/ same beam
  Power domain enhancement: Enhancements to realize increasing UE power high limit for CA and DC, MPR/PAR reduction
  Dynamic switching between DFT-S-OFDM and CP-OFDM

## Slide 3: Motivation of coverage enhancements in Rel-19
  Further extension of coverage enhancements solutions
  Rel-17 and Rel-18 work have provided a fundamental solutions for coverage enhancement, but there are some additional restrictions on the specified solutions, which can be further improved. On the other hand, the target UL data rate is set as 1Mbps for urban scenario, however, from operators’ requirement, the target data rate is higher than 1Mbps in practical network, e.g., 2Mbps. Thus, a better coverage performance is needed.

## Slide 4: Potential schemes/scopes for further Cov. Enh. (1/4)
  Multiple PRACH transmissions with different beams
  During the discussion in Rel-18, it can be observed that multiple PRACH transmissions with different beams will facilitate the coverage in some cases, e.g., for the case when beam correspondence is not supported. In addition, beam indication for subsequent UL transmission can be realized based on multiple PRACH transmissions with different beam, e.g., beam indication for Msg.3 transmission.
  Thus, we have the following proposals for multiple PRACH transmissions with different beams
    Support multiple PRACH transmissions with different beams.
    Support mechanism to realize UL beam indication based on multiple PRACH transmissions.
  PRACH transmissions with different beams
  For instance, if gNB can identify this beam is the best UL beam for corresponding UE, then indicate it to the UE.

## Slide 5: Potential schemes/scopes for further Cov. Enh. (2/4)
  Msg5 PUSCH repetition
  Currently, repetition is supported for most of the UL channels except for one important channel, i.e., PUSCH scheduled by DCI format 0_0 with CRC scrambled by C-RNTI (AKA. Msg5) .
  Based on the filed test, Msg5 PUSCH becomes the coverage bottleneck during the initial access. The main reason lies in Msg5 has a very large payload size, e.g., >100 Bytes. The situation would get worse when Msg3 repetition is implemented cause more UEs would access to the network while congested during Msg5 transmission.
  Thus, we have the following proposal:
    Support PUSCH repetition type A for a PUSCH scheduled by DCI 0_0 with CRC scrambled by C-RNTI.

## Slide 6: Potential schemes/scopes for further Cov. Enh. (3/4)
  Power domain enhancement
  During the discussion in Rel-18, MPR/PAR reduction is proved to facilitate the coverage. Simulations of FDSS w/ spectrum extension (FDSS-SE) show its benefit compared with transparent FDSS, but FDSS-SE is not supported in Rel-18. However, solid work on FDSS-SE has been done including identification of RAN1 spec impact and extension indication. Thus, we think it is necessary to support FDSS-SE in Rel-19.
  During the discussion in Rel-18, high power transmission in CA/DC is also discussed/specified, and ΔP_PowerClass is supported in the PHR report to have a better power scheduling effect. However, the evaluation period of the duty cycle to report ΔP_PowerClass and power fallback caused by P-MPR is not considered in Rel-18, which may affect the accuracy and effect of power scheduling. To further enhance the coverage, we think enhancement on PHR report is needed in Rel-19.
  Thus, we have the following proposal for power domain enhancement.
    Support enhancements for further MPR reduction.
      E.g., FDSS with spectrum extension
    Support PHR report enhancement for high power transmissions in CA/DC.
      P-MPR report
      Duration for SAR measurement

## Slide 7: Potential schemes/scopes for further Cov. Enh. (4/4)
  Enhanced DMRS bundling
  DMRS bundling is beneficial to improve PUSCH coverage performance. However, in Rel-17, modulation order is restricted to not higher than QPSK for DMRS bundling, and only single TB is supported. The theoretical supported data rate w/ QPSK is 0.8Mbps w/ 4 repetitions, 0.4Mbps w/ 8 repetitions for TDD DDDSU DDSUU, which can hardly meet the practical requirement of operators. In addition, DMRS bundling for non-consecutive slots is not supported in Rel-17, which limits the performance of DMRS bundling for TDD system.
  Thus, we propose to support the following schemes:
    DMRS bundling for different TBs
    High modulation order for DMRS bundling
    DMRS bundling for non-consecutive slots

## Slide 8: Potential scopes for Rel-19 coverage enhancements
  The potential scope is listed as follows
  Support multiple PRACH transmissions with different beams.
  Support PUSCH repetition type A for a PUSCH scheduled by DCI 0_0 with CRC scrambled by C-RNTI.
  Support further power domain enhancements.
    Support enhancements for further MPR reduction.
      E.g., FDSS with spectrum extension
    Support PHR report enhancement for high power transmissions in CA/DC.
      P-MPR report
      Duration for SAR measurement
  Support DMRS bundling enhancement
    DMRS bundling for different TBs.
    High modulation order for DMRS bundling.
    DMRS bundling for non-consecutive slots.

## Slide 9: Thanks!