## Slide 1: Views on RIS for Rel-19
China Telecom
Sept. 2023
3GPP TSG RAN Meeting #101
Bangalore, India, September 11-15, 2023
Agenda:8A.2.15
RP-232279

## Slide 2: Motivation of Reconfigurable intelligent surface (RIS)
  State of art technique for coverage extension
  Reconfigurable intelligent surface (RIS) has been studied in both academia and industry in recent years as a hot topic. Different from network-controlled repeater (NCR), RIS mainly consist of passive or nearly passive electronic units which can adjust the phase and/or amplitude of the impinging signals. Moreover, RIS may work in a reflection/refraction mode, which can directly reflect/refract the impinging signals in a beamforming manner. RIS intends to provides a low-cost, low-power consumption coverage extension & energy efficient solutions both for indoor and outdoor.

## Slide 3: Potential benefits of RIS
  Study on RIS
  RIS mainly consists of passive or nearly passive electronic elements, which are programmable and can adjust the phase and/or amplitude of the impinging signals to realize beamforming. RIS intends to provides a low-cost, low-power consumption coverage extension & energy efficient solutions both for indoor and outdoor scenarios.
  RIS is beneficial for the coverage, especially for FR2.
    E.g., deal with coverage issue due to blockage
Gain (dB)
diode
  Demo of RIS and RIS element
  Gain of reflection beam based on test

## Slide 4: Potential scopes for the study on RIS
  The potential scope of the study on RIS
  Generally, we think the study can include at least the following aspects.
    Deployment scenarios
      E.g., O2I, I2I, O2O etc.
    System model
      RIS type (e.g., reflection, active/passive)；RIS architecture, related component (forwarding, control)；Modeling of RIS element (materials and related parameters, e.g., reflection factor)
    For UE-transparent/UE-non-transparent RIS, study shared control mechanism with NCR (signaling, control information, beam management), RIS-specific control mechanism, if any.
    RIS capability (Beam switching, supported beams)
    Full duplex operation
    Performance evaluation

## Slide 5: Thanks!