## Slide 1: NTN testing issues between RAN4 and RAN5
MediaTek Inc., Unisoc, Spreadtrum
3GPP TSG-RAN Meeting # 101 RP-232309
Bangalore, India, September 11 – 15, 2023 Agenda Item 13.4.1

## Slide 2: Outline
Background
Issue #1: Work partition between RAN4 and RAN5 on introducing TE-emulated channel model
Issue #2: Guidance required to proceed RAN4 and RAN5 works
Summary

## Slide 3: Background
RAN4 has concluded the requirements and test case design for NR_NTN_solutions in Rel-17 and LTE_NBIoT_eMTC_NTN_req in Rel-18. RAN5 is now working on the corresponding conformance testing WIs NR_NTN_solutions_plus_CT-UEConTest and LTE_NBIOT_eMTC_NTN_req-UEConTest.
During the RAN5 discussions, companies identified some issues in the RAN4 requirements and test cases. Therefore, in May WG meeting, RAN5 sent an LS R5-233672 to RAN4, asking for some clarifications of NTN test settings.
In Aug WG meeting, RAN4 sent a reply LS R4-2314001 to RAN5.
During the discussion, we realized that there are some fundamental misalignment on how to proceed to work. Therefore, this paper is prepared for clarification and asking guidance from Plenary.
A short summary for the LS R4-2314001
  Q1a: [RF] requirements apply to both GSO and NGSO
  Q1b: [DMD] requirement in 38.101-4 apply to both GSO and NGSO
  Q2a1, Q2a2, Q2a3: [RF] Requirements apply to zero Doppler shift with constant delay
  Q2b: [RF] With zero Doppler and constant delay, UE pre-compensates delay but not Doppler
  Q2c: [RRM] Zero Doppler not applicable to NGSO. FFS GSO
  Q2d: [DMD] Zero Doppler is assumed
  Q3a: [RF] FFS delay and Doppler configuration for UL Tx freq error requirement
  Q3b: [RF] FFS constant or variable Doppler for UL Tx freq error requirement
  Q4a: [RF/DMD] No satellite propagator models considered
  Q4b: [RRM] TBD which TC considers Eckstein-Hechler propagator model
  Q5a: [DMD] No need for UE location update
  Q5b: [RRM] No need for UE location update

## Slide 4: Issue #1: Work partition between RAN4 and RAN5 on introducing TE-emulated channel model
During the RAN4 and RAN5 discussion, we realized that companies consider different approaches on how to introduce the Satellite propagator model (ephemeris) and TE-emulated channel model in RRM test cases for RAN4 and RAN5:
  It is very important to align companies understanding about which approach to proceed
Proposal 1: RAN#101 Plenary to provide guidance on work partition between RAN4 and RAN5 on introducing TE-emulated channel model, i.e., Approach #1 or #2 in above table.
Approach |  | RAN4 | RAN5
#1 | Satellite propagator model (ephemeris) | Define high-level guidance only (as in Annex B.5 in TS38.133) | Define detail settings
 | TE-emulated channel model | AWGN or TDL without Doppler/delay shifts due to satellite movement | Introduce additional Doppler/delay shifts due to satellite movement on top of RAN4 test cases
#2 | Satellite propagator model (ephemeris) | Define detail settings | Follow RAN4
 | TE-emulated channel model | AWGN or TDL with additional Doppler/delay shifts due to satellite movement | Follow RAN4
Doppler/delay shift: could be constant or time-varying
Current RAN4 status

## Slide 5: Issue #2: Guidance required to proceed RAN4 and RAN5 work
If Approach #2 is concluded in Issue #1, RAN4 would need to open the discussions (at least for RRM test cases, e.g., UL Tx timing accuracy) about how to introduce the TE-emulated channel model in order to match the satellite propagator model. The main goal is to ensure that only the correctly-implemented UEs can pass the NGSO test cases.
In our view, the outcome would be rather similar to the channel model defined for high-speed train (Annex B.3 in TS38.101-4). Two differences are that
  1) Not only Doppler shift but also delay shift need to be explicitly modeled, and
  2) The changes of Doppler and delay shifts need to match the satellite propagator model in every time instant.
The RAN4 workload is not trivial. If RAN4 needs a long time to conclude the new TE-emulated channel model, it will consume RAN4 TUs. Therefore, we request Plenary to provide a guidance to RAN4 on how to work on the TE-emulated channel model. Furthermore,
  A RAN-task in Q4 2023 to be considered to identify a minimum set of test cases to be introduced with NGSO testing environment to minimize RAN4 workload
  If needed, LS with latest progress can be sent RAN5 in every meeting to minimize the waiting gap in between
Proposal 2: If Approach #2 is concluded in Issue #1, Plenary to provide further guidance on how to proceed RAN4 RRM work for NGSO, e.g., a RAN-task in Q4 2023 and an early Rel-19 WI.
  The RAN-task is to identify a minimum set of test cases to be introduced with NGSO testing environment to minimize RAN4 workload
  LS with latest progress can be sent RAN5 in every meeting to minimize the waiting gap in between
Notes: Add some cross-WG coordinations to ensure RAN5 closely follow RAN4 progress to minimize the delay in RAN5

## Slide 6: Issue #2: Guidance required to proceed RAN4 and RAN5 work
Also, if Approach #2 is concluded in Issue #1, it will also impact the ongoing RAN5 works. Current RAN5 WI scope include both GSO and NGSO.
  For GSO, current TE-emulated channel models in RAN4 are sufficient for RAN5 to proceed to work, because the Doppler/timing shifts will not impact the performance much. RAN5 can either introduce a test function for UE to skip timing/frequency pre-compensation or introduce a special propagator model for static satellites.
  For NGSO, RAN5 has to wait for RAN4 to introduce new TE-emulated channel models (associated to satellite movement) first. This may imply some delay to the WI completion.
As different companies may have different priority to GSO and NGSO deployment scenarios. We request Plenary to come out a solution to accommodate the different deployment schedules for GSO and NGSO.
  For IoT-NTN, consider to only work on NB-IoT (I.e., without eMTC), if the workload in RAN5 is an issue.
Proposal 3: If Approach #2 is concluded in Issue #1, Plenary to come out a solution on RAN5 WIs to accommodate the different market needs for GSO and NGSO , e.g., split the Rel-18 RAN5 WIs based on GSO and NGSO.
  For IoT-NTN, consider to only work on NB-IoT (i.e. without eMTC), if the workload in RAN5 is an issue

## Slide 7: Summary
Proposal 1: RAN Plenary to provide guidance on work partition between RAN4 and RAN5 on introducing TE-emulated channel model, i.e., Approach #1 or #2 in page 4.
Proposal 2: If Approach #2 is concluded in Issue #1, Plenary to provide further guidance on how to proceed RAN4 RRM work, e.g., a RAN-task in Q4 2023 and an early Rel-19 WI.
  The RAN-task is to identify a minimum set of test cases to be introduced with NGSO testing environment to minimize RAN4 workload
  LS with latest progress can be sent RAN5 in every meeting to minimize the waiting gap in between
Proposal 3: If Approach #2 is concluded in Issue #1, Plenary to come out a solution on RAN5 WIs to accommodate the different market needs for GSO and NGSO , e.g., split the Rel-18 RAN5 WIs based on GSO and NGSO.
  For IoT-NTN, consider to only work on NB-IoT (I.e., without eMTC), if the workload in RAN5 is an issue

## Slide 8: Thank you!