## Slide 1: Sidelink Positioning Enhancements for Automotive Requirements
3GPP TSG RAN Meeting #101 Bangalore, India, September 11-15, 2023
RP-232385
Bosch

## Slide 2: Further SL Positioning Enhancements
Sidelink Positioning Enhancements for Automotive Requirements
Highlights: Support studying and specifying SL Positioning in Rel-19 either as an individual WI or within a general Rel-19 positioning enhancements WI
Motivation for Enhanced Positioning for V2X in Rel-19
High accuracy position in automotive challenging environments requires further enhancements to Rel-18 SL positioning.
Stringent positioning requirements for V2X (e.g., Set 3 TR38.845) could not be achieved in Rel. 18 in realistic evaluation scenarios (considering, e.g., available bandwidth)
Further assistance information reporting (e.g., exploiting existing “awareness/sensor information” in VRUs and vehicles) could enhance positioning accuracy compared to Rel-18 outcome, e.g., AoA could be enhanced by antenna orientation
SL Positioning enhancements are identified in 5GAA automotive input to 3GPP Rel-19 workshop [RWS-230164]
In RWS-230164, 5GAA identified multiple SL positioning enhancements requirements including:
  accuracy enhancements, SL positioning integrity, and further enhanced RAT independent positioning techniques
Example: Urban VRU Protection with SL Positioning
Notes: 5GAA Work Item leader on Positioning

## Slide 3: Proposal for Sidelink Positioning Enhancements WI
Sidelink Positioning Enhancements for Automotive Requirements
Proposals for Rel-19 SL Positioning WI:
Study and specify SL positioning for multi-band operation in FR1 (licensed/unlicensed Spectrum) and FR2 (licensed/unlicensed spectrum) [RAN1,RAN2]
Study and specify CPP and Integrity for SL Positioning [RAN1, RAN2]
Study and specify possible RAN impact for enhanced assistance information reporting to increase positioning accuracy [RAN2]
Open topics from Rel-18 SL Pos WI :
Rel-18 only supports limited functionalities achieving limited positioning accuracy
Considers carrier phase positioning (CPP) and positioning integrity for Uu Pos only
Needing further enhancements on reporting assistance information to enrich positioning accuracy (e.g., AoA) including, e.g., antenna orientation and other sensor information

## Slide 4: References
Sidelink Positioning Enhancements for Automotive Requirements
RWS-230164, “5GAA input to 3GPP Rel-19 Workshop,” 5GAA, Rel-19 RAN Workshop, Taipei, June 2023
RWS-230468, “Further Positioning Enhancements for Rel-19,” Bosch, Rel-19 RAN Workshop, Taipei, June 2023
RP-232343, “Views on Positioning Enhancements in Rel-19,” CATT et al., RAN#101, Bangalore, Sep. 2023

## Slide 5
Reliability
Positioning
Technology
AI/ML Technology
TCO
Health Monitoring
VRU/eBike/µMobility
ADAS Services
Energy Management
Machine User Interaction (XR)
Digital Twins
TN/NTN Integration
Sensor Sharing
Vehicle Motion Control
NTN-IoT
TSC/TSN‡
RAN sensing
Connected Vehicles Services
Sensing Technology
Availability
V2X Services
Non-RAT Positioning
Thank you!