## Slide 1: NTN Evolution for Automotive Requirements
3GPP TSG RAN Meeting #101 Bangalore, India, September 11-15, 2023
RP-232393
Bosch, Fraunhofer IIS

## Slide 2: Motivation for NTN Further Enhancements
NTN Evolution for Automotive Requirements
5GAA considers NTN as the automotive highest priority topic for Rel-19 packages [RWS-230164]
The automotive services require ubiquitous connectivity and coverage for advanced use cases, which can only be guaranteed via integrating terrestrial and non-terrestrial network
The vehicle capabilities, its on-board UE characteristics, and the supported automotive use cases differ from the existing NTN requirements in Rel.-17/18*
  (e.g., required throughput, antenna models, UE power class(es), mobility, etc.)
TN-NTN integration requires further enhancements for automotive (e.g., further enhanced mobility and support of service continuity), which allows better user experience
Different automotive services are well suiting Multicast and Broadcast Services (MBS) nature, which can be utilized if NTN enables 5G MBS**
NR NTN and Automotive Connectivity
* From 5GAA document [RWS-230164]:
  E.g., current handheld antenna is limiting data rate for NTN
  E.g., VSAT antenna (60 cm aperture) is too large for automotive
** MBS is supported by TN; however, the support of MBS in NTN is still missing

## Slide 3: Motivation for NTN Further Enhancements
NTN Evolution for Automotive Requirements
For Rel-19 NTN WI, consider the following enhancements:
Baseline:
Introduce different UE Types, i.e., vehicle UE including defining and specifying different antenna types/gains, different TX power class(es), improved noise figure [RAN4]*
  FFS: Study possible impacts on other WGs, e.g., [RAN1]
Mobility enhancements between TN and NTN and between NTN and TN to ensure service continuity [RAN2, RAN3]
Additionally:
Support discontinuous coverage for NR NTN (i.e., to overcoming coverage limitation during initial deployment phases) [RAN2, RAN3]
Support of NR MBS (Multicast and Broadcast Services) over NR NTN [RAN2, RAN3]**
Support Asynchronous multi-connectivity for, at least, different services (e.g., between NTN/TN and between two different satellite access (i.e., NGSO and GSO)) [RAN2, RAN3]‡
Further Proposals for NTN WI in Rel-19
* Need to be considered in RAN4 discussions during RAN#101
** MBS is supported by TN (NR Rel-17), while the support of MBS in NTN in RAN is still missing
‡ SA1 Rel-19 SI: Study on Upper layer traffic steer, switch and split over dual 3GPP access, introduces high-speed mobility uses cases benefiting from Terrestrial and Satellite Access dual access

## Slide 4: References
NTN Evolution for Automotive Requirements
RWS-230164, “5GAA input to 3GPP Rel-19 Workshop,” 5GAA, Rel-19 RAN Workshop, Taipei, June 2023
RWS-230467, “Bosch Views and Priorities for Rel-19,” Bosch, Rel-19 RAN Workshop, Taipei, June 2023
RWS-230048, “Consideration on RAN1/2/3 led NTN topics for Release 19,” Thales et al., Rel-19 RAN Workshop, Taipei, June 2023

## Slide 5
Reliability
Positioning
Technology
AI/ML Technology
TCO
Health Monitoring
VRU/eBike/µMobility
ADAS Services
Energy Management
Machine User Interaction (XR)
Digital Twins
TN/NTN Integration
Sensor Sharing
Vehicle Motion Control
NTN-IoT
TSC/TSN‡
RAN sensing
Connected Vehicles Services
Sensing Technology
Availability
V2X Services
Non-RAT Positioning
Thank you!