## Slide 1
RP-232419
Agenda Item: 8A.2.4
Type: Discussion
Document for: Discussion
3GPP TSG RAN 101
Bangalore, India,
September 11 – 15, 2023
Views and considerations for Rel-19 work on Ambient IoT
Sources: Novamint, EDF

## Slide 2
  This contribution was done in the context of EUWENA
  EUWENA (European Users Wireless Enterprise Network Association, https://www.euwena.eu) has been established in 2021, as a vehicle to entice and promote private wireless networks (Non Public Network for 3GPP) or services for industries and verticals.
  EUWENA mission statement: “Working together with all interested parties, EUWENA acts as a catalyst for the wider adoption of feature-rich private mobile networks across Europe. It advocates sufficient, accessible, affordable, harmonised spectrum and promotes an open, multi-vendor approach to advanced services and applications running in these networks. EUWENA’s ultimate goal through its actions is to make the adoption of such solutions as easy as possible for as many organisations as possible, thereby creating enhanced and sustained value for enterprises and wider society.”
  The analysis and recommendations have been conducted by EUWENA’s “Use Case” working Group
Disclaimer

## Slide 3
Verticals see a strong potential in Ambient IoT
Large number of Ambient IoT use cases are verticals driven
Full benefits of having 3GPP new approach such as Ambient IoT is to be able to be supported by Private Networks or dedicated networks
  Ports/Airports/mainports
  Smart Grid/Utilities
  Warehouses
  Hospitals
Spectrum aspect is paramount
The scenario currently privileged by 3GPP to support Ambient IoT is use of licensed spectrum (see RWS-230407)
See our view on the spectrum per use case types
Verticals perspectives on Ambient IoT

## Slide 4
Potential spectrum for Ambient IoT Indoor use cases
 |  |  | Unlicensed | MNO spectrum | NPN Spectrum | preferred solution
1 | Inventory: 10 use cases | Automated warehousing, automobile manufacturing, logistics, supply chain, etc. | Eventually | NO | YES | Vertical NPN spectrum
2 | Sensors: 6 use cases | Smart homes, smart agriculture, smart pig farm, etc. | Eventually | Eventually | Unlikely | Unlicensed or operator spectrum
3 | Positioning: 6 use cases | Lost item finding, personal belonging finding, positioning in shopping centre, museum guide, etc. | YES | Unlikely | NO | Unlicensed
4 | Command: 5 use cases | Electronic shelf label, elderly health care, device deactivation, etc | Eventually | Unlikely | Eventually | Unlicensed or vertical NPN spectrum
Analysis conducted by EUWENA’s “Use Case” working group

## Slide 5
Potential spectrum for Ambient IoT Outdoor use cases
 |  |  | Unlicensed | MNO spectrum | NPN Spectrum | preferred solution
5 | Inventory: 4 use cases | Airport terminal / shipping port asset tracking, medical instruments management, etc. | Eventually | NO | YES | Vertical NPN spectrum
6 | Sensors: 5 use cases | Smart grid, forest fire monitoring, manhole cover safety monitoring, bridge health monitoring, dairy farming, etc. | Eventually | Eventually for some use cases | Eventually | Unlicensed or vertical NPN spectrum
7 | Positioning (in public area): 3 use cases | Personal belonging finding, remote lost item finding, etc. | Eventually | Eventually | NO | Unlicensed or operator spectrum
8 | Command (in public area): 4 use cases | Controller in agriculture, elderly health care, device deactivation, etc. | YES | Eventually | NO | Unlicensed
Analysis conducted by EUWENA’s “Use Case” working group

## Slide 6
Considerations on spectrum for Ambient IoT
  Due to the nature of the type of device targeted (very small, ultra low power, without battery / with energy harvesting)
    Spectrum to consider should be in sub-GHz frequency bands
    Unlikely to support many frequency bands
  Many of the use cases are implying the device to move across the globe and to support all regions (for example, logistics, asset tracking…), it will require to support bands from only maximum one band for each region.
  Currently, there is no harmonized spectrum for Private Network in Europe
  There is no availability of sub-GHz spectrum for Private Network in Europe (currently an issue to deploy NB-IoT in private networks) – limited spectrum available
  Potential bands that could be used in Europe assuming small channelization are required: central gap of the 700 MHz band, 450 MHz, VHF: 174-230 MHz, 470-694 MHz?
  Unlikely to have similar spectrum for Verticals and for Operators and the different use cases associated
  Operator spectrum for Ambient IoT need as well harmonization and cannot use the same spectrum than existing LPWAN
  3GPP should work on Ambient IoT only if it can be deployed in all regions
  We should not work on technical and theoretical aspects of Ambient IoT without having addressed the real life deployment perspective in particular for spectrum

## Slide 7
Recommendations
Conduct a RAN4 study on spectrum deployment perspectives before to start any work on RAN1/2/3 aspects of Ambient IoT
Study should consider at minimum
  Regulations aspects and spectrum perspectives with inputs from regulators:
    National: Arcep, Ofcom, BNetzA, ACM, BIPT, FCC, RSSC…
    Regional: RSPG…
  Deployment scenarios & viability with inputs from
    Associations representing verticals interests and relevant for the use cases identified such as EUWENA, 5G ACIA, 5GAA…
    End users and operators from all regions in the cases with operator spectrum
Prioritize use cases to be addressed in RAN1/2/3 for Ambient IoT based on the findings from RAN4 study