## Slide 1
Rel-19 study on L2 user plane, high-speed packetization and protocol enhancements
  3GPP TSG RAN#101
  Bangalore, Sep 11 - 15, 2023
  Source: Apple Inc, T-Mobile USA, Vodafone, Nokia, Samsung, Intel Corp, NEC Corp
  Agenda Item: 8A.2.15
  RP-232430

## Slide 2
Motivation | Background
NR has over three releases and we are nearing the tail end of NR before 6G shapes in.
  Through these releases, several work-items/features were added into NR which directly impact the user-plane aspects (URLLC, NR-U, B71GHz, XR, UP IP etc.)
  However, RAN did not have an evaluation of what needs to be improved in user-plane as a result of evolution of NR.
    NR user-plane still operates using the Rel-15 design.
  It is very beneficial to plan for a study to ensure that:
    The user-plane design does not become a bottleneck or limiting factor in the 5G-Advanced NR operation.
    Scales up to newer features and releases of 5G NR
    Lays the framework for smooth transition to 6G where feasible.
There are a few broad areas where such study can be done
  High-speed packetization and header overhead reduction
  L2 User Plane Enhancements
  Gap Analysis of User Plane Performance Bottlenecks
  Security for MAC CE

## Slide 3
Motivation | High-speed packetization and header overhead reduction
The NR data structure was designed to support efficient HW processing, however, at the cost of higher L2 overhead
  The ratio of header vs payload reduces the number of user data bytes overall
  Plus, every SDU needs header processing at multiple layers (e.g., SDAP/PDCP/RLC/MAC)
UPIP is mandatory since Rel-16, which involves additional processing
  The time required for payload processing does not scale linearly with the payload size
5G-Advanced scales to higher data rates with heterogeneous payloads and a mix of many packets (e.g., 8K streaming, gaming)
  User Plane performance decreases and UE power consumption increases
Efficiency gains are possible if a lower number of packets is processed at once
  Load reduction for security operations
  Load reduction for packet generation and LCP

## Slide 4
Motivation | L2 User Plane Enhancements (1/2)
The SDAP layer was defined in Rel-15 when RLC AM was prevalent, without wide-spread deployment of new services over SDAP. Later 5G releases support a mix of heterogeneous payloads with varying QoS requirements.
  RLC UM has become a deployment for new services which necessitates enhanced transmission of RDI and end-marker PDUs. Moreover, redundant processing of the RQI bit is inefficient from UE perspective.
  For HO, if multiple QoS flows are mapped to the same DRB in the source and target gNBs, then in-order delivery cannot be guaranteed.
A growing amount of application layer operations possess a cumulative nature where the last packet is most relevant — such as TCP/QUIC ACKs, TFTP, IPSec, OSPF, certain AI algorithms, etc.
  5G NR user plane protocols do not take advantage of this type of traffic where the critical operation is the delivery of the latest packet. To help assist the application, it is also imperative to treat the most important packets of a given flow in due time.
With the introduction of higher SCS for beyond 52GHz, larger difference in SCS between carriers result in asymmetric transfer of data among carriers, where the L2/L3 ACK mechanism can have issues in dealing with large bursts of data on a carrier while waiting on data from the “slow” carrier, leading to data stalls/inefficient ACK handling.

## Slide 5
As 5G evolves to include more delay sensitive services, efficient congestion management techniques are paramount for scalability and optimized use of network resources. 5G NR supports L4S/ECN, however, it is important to detect and signal congestion as early as possible.
The amount and variety of SDFs and QoS flows coming into PDCP continues to increase. Traffic flows that do not require in-order delivery are often mapped to the same DRB together with traffic flows that require strict in-order delivery. Spreading those flows over separate DRBs would utilize a higher number of DRBs, causing higher processing and memory demands and increased power consumption. We can facilitate lower latency through selected out-of-order delivery for selected flows or packets.
For delay-critical GBR LCHs, the current LCP procedure based on PBR and BSD allows fulfilling either GFBR or MDBV (over PDB) rate requirement, but not both. When insufficient UL grants are provided to UE, there is risk of starvation for LCHs with lower priority. LCH restrictions to isolate grant usage have scalability issues in case of multiple delay-critical GBR LCHs per UE.
For use-cases with low PDB, the operation of RLC retransmissions involves some in-efficiencies where ReTx is not triggered fast enough or happens unnecessarily.
Motivation | L2 User Plane Enhancements (2/2)

## Slide 6
From an architectural and functional perspective, the UP protocol stack has largely stayed the same since 3G. However, requirements and use-cases have changed significantly.
  Increasing data rate expectations (Kbps to Gbps)
  Shrinking delay expectations (seconds to <20ms)
  Services migrating to the edge
  Changing transport layer protocols (TCP to QUIC)
  Increasing use of MAC CEs signalling sensitive information
There is a need to evaluate enhancements to the protocol stack to match emerging use-cases
  Immersive services such as XR introduce latency-sensitive high-throughput data and servicing such requirements usually needs higher energy consumption which can lead to heat dissipation issues. The protocol enhancements can help mitigate this.
  Advanced use-cases such as robots, audio/video production, industrial IoT continue to require high reliability for delay-constrained traffic
These aspects will only get more pronounced in the future
  A holistic study of the current UP stack performance and its gaps is needed to identify functionality required to meet requirements for 5G-advanced and the next years to come
Motivation | Gap Analysis of User Plane Performance Bottlenecks
References: RWS-230124

## Slide 7
Objectives:
Study enhancements to simplify the L2 processing and reduce the number of L2 headers
  Potential solutions may include combining multiple SDUs into one concatenated SDU
  Potential solutions may also include parallelization of user plane packets in the protocol stack.
Ensure compatibility with earlier releases by introduction of an optional add-on feature
Objectives | High-speed packetization and header overhead reduction

## Slide 8
Objectives | L2 User Plane Enhancements
Objectives (contd.):
Study benefits of out-of-order processing over the Uu interface and in higher layers and explore the possibility of selective out of order delivery for a DRB.
Study enhancements to natively support cumulative operations as part of 3GPP protocols to address QoS and performance limitations
Study mechanisms to enhance the packet forwarding treatments of important packets and/or traffic flows for reduced power consumption and optimized usage of spectrum
Study enhancements to SDAP for handover, RQoS and redundant processing of RQI, and reliability improvements
Study enhancements for congestion detection at the UE and the gNB, configuration and policy adjustments, and means to insert an L4S marking at the queue head of Layer2
Study enhancements to L2/L3 user plane protocols to handle asymmetric data-rate from carriers with different SCS.
Study LCP enhancements to allow serving DC-GBR LCHs according to their QoS requirements
Study RLC retransmission enhancements allowing operation of RLC AM with small packet delay budget

## Slide 9
Objectives (contd.):
Throughput performance
  Evaluate processing overhead and identify gaps within the NR stack for high-throughput traffic
  Identify areas of improvement needed to enable a lean and energy-efficient stack for high-throughput data transfer
Delay performance
  Evaluate delay performance and identify gaps within the NR stack to serve latency-sensitive traffic
  Identify areas of improvement needed to enable a responsive stack for latency-sensitive data transfer
Reliability
  Evaluate the reliability offered by the NR stack and its gaps to serve high-throughput latency-sensitive traffic
  Identify areas of improvement needed to meet reliability requirements for high-throughput latency-sensitive data transfer
Security improvement
  Study solutions to provide security for sensitive MAC CEs
References: RWS-230124
Objectives | Gap Analysis of User Plane Performance Bottlenecks

## Slide 10
Summary
Summary
  Rel-19 is nearing the tail of NR before 6G shapes in.
  Compared to earlier releases, recent advancements of new services and use-cases require higher throughput and lower latency with reasonable reliability, which require an optimized operation of the user plane at reasonable power consumption
  For fast market adoption 3GPP should identify relevant enhancements without the wait for the next generation
Proposal
  To help create a well-rounded 5G and simplify L2 processing, Rel-19 shall facilitate a study on L2 user plane, high-speed packetization and protocol stack enhancements. Objectives in earlier pages can be used as a base for further discussions.