## Slide 1
Discussion on Rel-19 XR enhancements
RP-232431
Ericsson
3GPP TSG-RAN #101
Bangalore, Sep 11-15 2023

## Slide 2: Rel-19 XR in RAN
Justification
Rel-17 XR SI evaluated XR performance and identified bottlenecks
Rel-18 XR SI/WI has been focusing on finding solutions in RAN to enhance XR capacity and power saving when assistance information about application is provided
Rel-19 XR should aim to further improve primarily the area of capacity, but also UE power saving and XR awareness
Smart AR
Cloud gaming

## Slide 3: Proposed Rel-19 XR areas
XR
awareness
UE power
saving
Capacity
Rel-19 XR
Capacity
UL delay-aware scheduling with dynamic logical channel prioritization
PDSCH reception based CQI
Measurement gap (MG) enhancements
UE power saving
DRX enhancements for multiple flows & carrier aggregation
PDCCH monitoring adaptation for carrier aggregation
XR awareness

## Slide 4: Capacity enhancements: UL delay-aware scheduling
Context
  Multiple flows within the same UE (XR and others)
  Rel-18 will introduce signaling of remaining delay
Motivation
  Existing logical channel prioritization (LCP) is based on fixed priority levels & bucket size for each LCID → restriction to prioritize urgent packets if they belong to the lower priority logical channel
Solution: Enhanced UL delay-aware scheduling with dynamic logical channel prioritization
Proposal: Support enhanced UL delay-aware scheduling with dynamic logical channel prioritization [RAN1, RAN2].
E.g. for two LCIDs: During a short period of time (shorter than RRC reconfiguration time), if some packets in LCID 2 (lower priority) become more urgent than packets in LCID 1 (higher priority), i.e. their remaining delay becomes shorter, the UE should reprioritize LCID 2 over LCID 1.

## Slide 5: Capacity enhancements: PDSCH reception based CQI
CSI reports are inaccurate
  Resource for measurement is separate from resource for PDSCH transmission
Solution: Introduce PDSCH reception based CQI report
  Motivation for XR: XR continuously generates PDSCH transmission, which can be used to improve CSI accuracy
Benefits:
  Improved link adaption for re-transmissions -> XR capacity improvement (right figure, ‘green’ compared to ‘blue’)
  Improved link adaptation for next initial transmission
  Faster outer-loop link adaption convergence
Proposal: Specify CQI reporting based on actual received PDSCH quality (e.g., PDSCH DMRS or PDSCH decoding based CQI) [RAN1, RAN2].
Reference: R1- 2208401

## Slide 6: Capacity enhancements: Measurement gaps
Measurement gaps (MGs) are periodic gaps in TX/RX that need to be configured in some cells, primarily for inter-frequency handover measurements, but may be needed also for intra-frequency measurements
Large degradation of XR capacity in cells with MG
Solution: gNB-controlled L1 signaling for dynamic utilization of MGs for XR mobility
  Both dynamic triggering and dynamic cancellation of MGs can be considered
Proposal: Specify gNB-controlled L1 signaling for dynamic utilization of measurement gaps for XR mobility [RAN1, RAN2, RAN4].
XR capacity threshold
Fraction of satisfied XR users (60 frames/sec) with or without measurement gap configured and activated. For ‘noGap’, no user has measurement gap, while for ‘3 ms gap length’ and ‘6 ms gap length’ all users have measurement gaps configured and activated with 3 ms or 6 ms gap length and 80 ms gap repetition period.

## Slide 7: UE power saving: DRX enhancements
Multiple interleaved periodic XR flows → difficult to minimize delay & also save UE power in the irregular sleeping gaps
Solution: Multiple active DRX configurations → up to 13.6% power saving gain (and 88.4% satisfied UEs)
For CA, different traffic patterns could occur on different carriers (e.g., different XR flows could be mapped to different carriers)
Solution: Consider independent DRX configurations per carrier
Proposal: Support multiple simultaneous DRX configurations to optimize power saving of UEs with multi-flow XR services [RAN2].
Proposal: Introduce more flexible control and configuration for the secondary DRX group in CA [RAN2].

## Slide 8: UE power saving: PDCCH monitoring adaptation for CA
Very sparse PDCCH monitoring can be used at L1 to save UE power on some carriers
However, a solution is needed to transmit the traffic fast, once the traffic arrives at RAN
Solution: Control fast PDCCH monitoring adaptation (SSSG switching) across serving cells – send L1 indication on one cell, which is applicable to another cell
  Useful especially for XR video traffic with jitter: The exact traffic arrival time is not known (cannot be predicted) and the data size is large (several slots needed for transmission), so scheduling is needed in multiple slots
Proposal: Support PDCCH monitoring adaptation controlled via one serving cell, for any of the other serving cells [RAN1].
Proposed solution

## Slide 10: Appendix: Simulation assumptions
Simulation assumptions for PDSCH reception based CQI and measurement gap simulation results are according to the table on the right side.
For simulations with measurement gaps enabled, the measurement gaps are only used for SSB measurements and are configured to be aligned with SSB locations where the SSBs are transmitted. The SSBs have a 20 ms periodicity.
To avoid all UEs to have measurement gaps at the same time, the UEs are randomly assigned to one of four measurement gap groups, where group i=0, 1, 2, 3 has measurement gaps with a starting time Ti in ms:
Ti (mod 80)=i∙20