## Slide 1: Multi-carrier enhancements in Rel-19
3GPP TSG RAN Meeting #101
Bangalore, India, September 11-15, 2023
RP-232432
Agenda Item: 8A.2.12.2
Source: Lenovo, CATT, China Unicom, New H3C, TCL Communication, xiaomi
Document for: Discussion

## Slide 2: Rel-18 Standardization outcome
Main standardization outcome
DCI format design:
  At most one PDSCH or PUSCH per scheduled cell
  New DCI formats, DCI 0_3 & DCI 1_3, introduced
  Up to 4 cells can be co-scheduled by one DCI 0_3/1_3
  DCI 0_3/1_3 can be used for single cell scheduling
  DCI 0_3/1_3 and DCI 0_0/1_0/0_1/1_1/0_2/1_2 can be monitored simultaneously from a same scheduling cell.
Basic framework
Supported cases:
  Only same SCS among co-scheduled cells is supported
  Only same carrier types (licensed/unlicensed, FR1/FR2/FR2-2) among co-scheduled cells is supported
  Only a single scheduling cell for each scheduled cell
  Only single PDSCH or PUSCH scheduled per scheduled cell
  Only TB-based transmission supported per scheduled cell
Up to 4 cells scheduled by one DCI format 1_3
Up to 4 cells scheduled by one DCI format 0_3

## Slide 3: Endorsed RAN chair’s summary in RWS-230488: Additional RAN1-led Candidate Topics
Low-power Wake-Up Signal (LP-WUS)/Wake-Up Radio (WUR)
  A possible conversion from Rel-18 SI to Rel-19 WI.
  Need to ensure successful completion of the SI and focus on essential areas
Multi-carrier enhancements
  The proposed areas for possible enhancements are quite diverging and wide
  Careful examination is necessary in terms of real commercial needs
Coverage Enhancements
Positioning Enhancements
SL evolution
  If included, critical to focus on a limited set of possible areas addressing real commercial needs

## Slide 4: Motivation for multi-carrier enhancements in Rel-19
Multi-carrier operation is very important for 5G commercial networks by aggregating various spectrum resources for providing high data rate and low latency communication.
Due to limited TU for Rel-18 MCE, some important use cases have been excluded from Rel-18, e.g., different SCS among co-scheduled cells, more than one scheduling cell for a scheduled cell. Co-scheduling carriers with different SCS is of high commercial needs for operators, e.g., 3.5GHz TDD + Sub-3GHz FDD. For a scheduled cell, supporting one scheduling cell for multi-cell scheduling and another scheduling cell for single-cell scheduling can offload PDCCH from the sole scheduling cell.
Supporting one or multiple PUSCHs/PDSCHs per scheduled cell can fully exploit the gain of UE power saving and PDCCH overhead reduction when scheduling cell in FR1 schedules cells in FR2.
DL carrier switching can adapt channel fluctuations among carriers to achieve higher DL throughput and cross-carrier DL/UL retransmission can reduce the retransmission latency especially for TDD networks.
For flexible and efficient usage of fragmented spectrums in low frequencies where an operator has, aggregating multiple carriers as one serving cell can achieve simplified cell management and load balance as well as power saving.

## Slide 5: Candidate objectives for Rel-19 Multi-Carrier Enhancements
Objective 1: Enhancements on multi-cell PUSCH/PDSCH scheduling by a single DCI [RAN1]
  Select one or multiple from below:
      Different SCS among co-scheduled cells by DCI format 0_3/1_3 is supported
      Up to two scheduling cells for a scheduled cell is supported
        One scheduling cell for multi-cell scheduling using DCI format 0_3/1_3 and another scheduling cell for single-cell scheduling using DCI format 0_0/1_0/0_1/1_1/0_2/1_2 if configured
      One or multiple PUSCHs/PDSCHs per scheduled cell is supported
        It is up to RAN1 to determine the maximum number of PUSCHs/PDSCHs per scheduled cell
Objective 2: Enhancements on cross-carrier transmission [RAN1, RAN4]
  DL carrier switching among different carriers is supported
  Cross-carrier retransmission for DL and UL is supported
Objective 3: Study, if necessary, specify mechanisms for more efficient multi-carrier operation [RAN1, RAN2, RAN4]
  Multiple contiguous or non-contiguous carriers are aggregated as a single serving cell
  Note: Further down-selection can be performed in Dec. RAN#102 meeting.

## Slide 6: Thanks
thanks