## Slide 1: Rel-19 mobility enhancements
Ericsson
3GPP TSG RAN#101
Bangalore, IN
2023-09-11 - 2023-09-15
Agenda Item: 8A.2.6
RP-232433

## Slide 2: Background
LTE Rel-14: make-before-break handover and RACH-less handover were introduced to shorten mobility interruption time for LTE
NR Rel-15: only basic L3 handover is supported
Rel-16: features were added to both LTE and NR to address short handover interruption time and increased mobility robustness:
  Dual Active Protocol Stack (DAPS) handover
  Conditional handover (CHO)
  Intra-node Conditional PSCell Change (CPC)
  For NR: 2-step random access, including 2-step CFRA (contention-free random access ) for handover
Rel-17: in feMIMO WI, work was started on inter-cell support for beam management including L1/L2-centric mobility for NR
  L1/L2-centric mobility was then removed from the WI due to lack of time
Rel-17: in further MR-DC/CA enhancements, inter-node CPC and Conditional PSCell Addition (CPA) was specified
Rel-18: in further NR mobility enhancements, L1/L2-triggered mobility (LTM), and various enhancements on CHO/CPC/CPA are being specified. There is also a study on early measurement reporting enhancements which may optionally include normative work.

## Slide 3: Extend LTM to inter-CU scenarios
Justification:
  L1/L2-triggered mobility (LTM) will in Rel-18 be limited to intra-CU mobility scenarios, also security key change will not be supported for LTM in Rel-18.
  Dual Active Protocol Stack (DAPS) supports inter-gNB but does not work for FR2 and CA/DC is not supported during the handover.
  Adding LTM as one way of performing inter-gNB mobility would provide benefits due to the short latency and interruption time with LTM.
  To support inter-CU LTM, at least security key information needs to be supported in the LTM configuration of an inter-CU candidate cell
    LTM cell switch needs to include change of security key
Objective:
  Specify mechanisms and procedures for L1/L2-triggered mobility for inter-CU scenarios including
    Signalling support for configuration of inter-CU candidate cells [RAN2, RAN3]
    Signalling support for L1 measurements configuration, early UL/DL sync [RAN2, RAN3]
    Signalling support and RRM requirements for Inter-CU LTM cell switch [RAN2, RAN3, RAN4]
    Note1: Rel-18 LTM shall be the baseline
    Note2: Inter-CU LTM should support at least security key change in addition to scenarios already supported in Rel-18

## Slide 4: LTM L1 measurement enhancements
Justification:
  Only basic LTM reporting supported in Rel-18: L1-RSRP based on SSB, using CSI reporting framework
  The lack of UE-initiated reporting may lead to high overhead
  Reporting based on SSB may not provide sufficient accuracy
Objective:
  Specify event-driven reporting over L1/2
  Specify measurements on CSI-RS

## Slide 5: Other LTM L1 enhancements
Justification:
  The lack of CSI reports for the target will lead to lower data rates until the first CSI report is received
UL and DL pre-synchronization are performed independently
  Separate signaling used: PDCCH order for UL pre-synchronization, MAC CE for DL pre-synchronization
    Unnecessary: the typical case is that the UL and DL pre-synchronization point to the same SSB
Objective:
  Specify methods to enable early CSI acquisition for the target
  Specify TCI state pre-activation using a PDCCH order

## Slide 6: Conditional triggering of low-latency handover
Justification:
  LTM relies on L1 measurement reports and network triggering of the LTM cell switch
    In scenarios such as rapidly decreasing coverage, the L1 report or the LTM cell switch MAC CE might get lost or delayed due to HARQ retransmissions, resulting in RLF in source cell
  Conditional Handover (CHO) is a way to increase robustness in these scenarios using a conditional triggering
    On the other hand, during execution of CHO, the interruption time is the same as legacy L3 handover due to UE needs to perform DL sync and random access
  Thus, there is not yet a solution that provides both short interruption and high robustness
  Alternative solutions
    LTM with conditional triggering (“conditional LTM”)
    Enhance CHO with e.g. early UL/DL sync and/or RACH-less
Objective:
  If agreed to be in the Rel-19 scope, RAN2 to study whether to specify conditional LTM or to enhance CHO with early sync/RACH-less
  The duration of the study should be one quarter

## Slide 7: Enhanced L3 measurement support for CHO/LTM
Justification:
  There are currently certain limitations in how L3 measurements can be used to effectively support the network in maintaining the limited set of candidates.
    The measurement report currently only includes a single cellsTriggered list, containing the list of cells fulfilling the entry condition for a certain event.
    Once the leaving condition is fulfilled, the cell is removed from the list, which means that even when reportOnLeave is set to true to trigger a measurement report upon leaving condition fulfilled for a cell, the measurement report will not contain the information of cells fulfilling the leaving condition.
    The number of cells to report is also limited to limit the size of the measurement report.
  This means that from the measurement report alone, it is not possible to determine whether the entering or leaving condition was triggered for the reported cell.
Objective:
  If not already addressed in Rel-18, add support in the measurement report to indicate whether an included cell is entering or leaving the reporting range [RAN2]

## Slide 8: Inter-frequency measurement priority information
Justification:
  The existing measurement framework for inter-frequency measurements allows the network to list a set of frequencies on which the UE is supposed to perform the measurements.
  With the increasing amount of frequency carriers in FR1 and especially FR2, one limitation that has become evident in the field is the lack of control from the network side on in which order the UE measures and reports the listed frequencies.
    This is currently left for UE implementation.
    UEs may end up measuring and reporting a certain carrier F1 first, triggering handover or CA/DC setup on F1, whereas other available carriers F2 and F3 remain unused.
    The network would currently only have limited means to control the offloading among F1-F3.
Objective:
  If not already addressed in Rel-18, specify strict priority order for inter-frequency measurements [RAN2, RAN4]